Copyright 1999, The American Institute of Architects (AIA)

# SECTION 08211 - FLUSH WOOD DOORS

This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

# PART 1 - GENERAL

# 1.1	RELATED DOCUMENTS

A.	Site drawings produced by Pinkham and Greer Consulting Engineers, foundation/basement plan drawings produced by TFH Architects PA and Structural Design Consulting, building drawings produced by TFH Architects, mechanical drawings produced by TFH Architects, electrical and lighting drawings produced by TFH Architects.  Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

# 1.2	SUMMARY

A.	This Section includes the following:

Adjust list below to suit Project.

1.	Hollow-core doors with hardboard faces.

Delete special services below if not applicable.  See Evaluations.

2.	Shop priming flush hardboard doors.

3.	Factory fitting flush hardboard doors to frames and factory machining for hardware.

Delete subparagraph below if louvers are not required for wood doors.

- Louvers for flush wood doors.

- Pre-hung door frame and hardware assemblies.

B.	Related Sections include the following:

List below only products, construction, and equipment that the reader might expect to find in this Section but are specified elsewhere.

Select one of two options in subparagraph below, depending on which Section is used to specify wood door frames, if they are used.  Both fire-rated and non-fire-rated wood door frames are specified in both Sections.

1.	Division 6 Section Finish Carpentry Interior for wood door frames.

Select one of two options in first subparagraph below if any doors are blueprint matched with wood paneling.

# 1.3	SUBMITTALS

A.	Product Data:  For each type of door.  Include details of core and edge construction and trim for openings.  Include factory-finishing specifications.

Delete paragraph below if not required or revise to suit Project.

B.	Shop Drawings:  Indicate location, size, and hand of each door; elevation of each kind of door; construction details not covered in Product Data; location and extent of hardware blocking; and other pertinent data.

Delete items below not required.

1.	Indicate dimensions and locations of mortises and holes for hardware.

2.	Indicate dimensions and locations of cutouts.

3.	Indicate doors to be factory finished and finish requirements.

4.	Indicate fire ratings for fire doors.

C.	Samples for Initial Selection:  Color charts consisting of actual materials in small sections for the following:

Delete subparagraphs below that do not apply to finishes retained in Part 2.

1.	Faces of Factory-Finished Doors:  Show the full range of colors available for opaque finishes.

D.	Samples for Verification:

Delete subparagraph below if no doors are factory finished.  Delete second sentence if no transparent factory finishes.

1.	Factory finishes applied to actual door face materials, approximately 8 by 10 inches (200 by 250 mm), for each material and finish.  For each wood species and transparent finish, provide set of three samples showing typical range of color and grain to be expected in the finished work.

Delete subparagraph below if doors do not have transparent finish.  Delete option if not factory finished.

2.	Corner sections of doors, approximately 8 by 10 inches (200 by 250 mm), with door faces and edgings representing typical range of color and grain for each species of veneer and solid lumber required.

# 1.4	QUALITY ASSURANCE

Revise paragraph below or insert exceptions where types of doors specified are not available from a single manufacturer.

A.	Source Limitations:  Obtain flush wood doors through one source from a single manufacturer.

Retain one standard below.  NWWDA I.S.1-A is less restrictive than AWI or WIC; WIC applies only in California, Nevada, and Oregon.  See Evaluations.  Review standard selected and coordinate its requirements with options selected.

B.	Quality Standard:  Comply with NWWDA I.S.1-A, "Architectural Wood Flush Doors

1.	Provide AWI Quality Certification Labels or an AWI letter of licensing for Project indicating that doors comply with requirements of grades specified.

Delete subparagraph above if AWI standard is not referenced in paragraph above.  Delete two subparagraphs below if WIC standard is not referenced in paragraph above.

Delete paragraph and subparagraphs below if no fire-rated doors.

C.	Fire-Rated Wood Doors:  Doors complying with NFPA 80 that are listed and labeled by a testing and inspecting agency acceptable to authorities having jurisdiction, for fire ratings indicated, based on testing according to NFPA 252.

Delete subparagraph below if UBC standard is referenced in paragraph above.  Second option below is based on positive-pressure testing requirement in final draft of International Building Code.

# 1.5	DELIVERY, STORAGE, AND HANDLING

A.	Comply with requirements of referenced standard and manufacturer's written instructions.

Retain first paragraph below for factory-finished doors and high-quality unfinished doors.  Second option is standard with some manufacturers, extra with others.

- Package doors individually in plastic bags or cardboard cartons.

C.	Mark each door on top and bottom rail with opening number used on Shop Drawings.

# 1.6	PROJECT CONDITIONS

A.	Environmental Limitations:  Do not deliver or install doors until building is enclosed, wet work is complete, and HVAC system is operating and will maintain temperature and relative humidity at occupancy levels during the remainder of the construction period.

Generally retain paragraph above; retain below if humidity will be controlled during occupancy.  If retaining below, select one of three relative humidity ranges or insert another based on local climatological data.  First option applies to most of U.S., Ontario, and Quebec; second, to damp coastal areas of southern U.S. and maritime provinces; and third, to dry southwestern U.S. and to Alberta, Manitoba, and Saskatchewan.  See map and discussion about relative humidity and moisture content at end of Section 1700 in AWI's quality standards.

# 1.7	WARRANTY

See Evaluations for door warranties.

When warranties are required, verify with Owner's counsel that special warranties stated in this Article are not less than remedies available to Owner under prevailing local laws.  Coordinate with Division 1 Section "Product Requirements."

A.	Special Warranty:  Manufacturer's standard form, signed by manufacturer, Installer, and Contractor, in which manufacturer agrees to repair or replace doors that are defective in materials or workmanship, have warped (bow, cup, or twist) more than 1/4 inch (6.4 mm) in a 42-by-84-inch (1067-by-2134-mm) section, or show telegraphing of core construction in face veneers exceeding 0.01 inch in a 3-inch (0.25 mm in a 75-mm) span.

Retain or delete subparagraph below to suit Project.  This provision is not standard with most manufacturers and could be an added cost if retained.

# 1.	Warranty shall also include installation and finishing that may be required due to repair or replacement of defective doors.

Revise subparagraph below to suit Project.  Standard manufacturer's warranty generally goes into effect on date of shipment, not Project acceptance.

# 2.	Warranty shall be in effect during the following period of time from date of Substantial Completion:

Delete requirements below for inapplicable types.

Retain one of three options in subparagraph below.  Warranties for exterior doors vary from none to five years; verify availability of warranty period with manufacturers selected before retaining.

# a.	Solid-Core Exterior Doors:  Two years.

Below is typical; revise if required.

# b.	Solid-Core Interior Doors:  Life of installation.

If retaining below, select one of two options.  Warranties vary with manufacturer and type of hollow core.

# c.	Hollow-Core Interior Doors:  One year.

# PART 2 - PRODUCTS

# 2.1	MANUFACTURERS

See Editing Instruction No. 1 in the Evaluations for cautions about naming manufacturers and products.

# A.	Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Product Requirements."

# B.	Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

1.	Flush Wood Doors:

See Editing Instruction No. 2 in the Evaluations before selecting manufacturers below.  Marlite and Poncraft Door only make doors with plastic-laminate faces.

a.	Algoma Hardwoods Inc.

b.	Ampco Products, Inc.

c.	Buell Door Company.

d.	Chappell Door Co.

e.	Eagle Plywood & Door Manufacturing, Inc.

f.	Eggers Industries; Architectural Door Division.

g.	GRAHAM Manufacturing Corp.

h.	Haley Brothers, Inc.

i.	Ideal Wood Products, Inc.

j.	IPIK Door Company.

k.	Lambton Doors.

l.	Marlite.

m.	Mohawk Flush Doors, Inc.

n.	Oshkosh Architectural Door Co.

o.	Poncraft Door Co.

p.	Southwood Door Co.

q.	Vancouver Door Company, Inc.

r.	VT Industries Inc.

s.	Weyerhaeuser Company.

# 2.2	DOOR CONSTRUCTION, GENERAL

A.	Doors for Opaque Finish:

Select one of three grades below.  WIC has no Economy grade for doors.

Select one of three faces below.  First is highest quality; last is most economical.  Coordinate with requirements of grade selected.

# 1.	Faces for Interior Doors:  Hardboard embossed with six panel configuration.

Delete subparagraph below if medium-density overlay is not used.

# 2.3	SOLID-CORE DOORS

Delete paragraph and subparagraphs below if no doors with particleboard cores.

A.	Particleboard Cores:  Comply with the following requirements:

Select one of two options in subparagraph below.  Second option makes a stronger door, has higher screw-holding capacity, and is standard with some manufacturers and optional with others.

# 1.	Particleboard:  ANSI A208.1, Grade  [LD-1] [LD-2].

Consider deleting subparagraph below.  Some door manufacturers contend that blocking weakens particleboard-core doors and is not required.  If retaining, select one of two options.

# 2.	Blocking:  Provide wood blocking in particleboard-core doors as follows:

If retaining subparagraph above and second option, retain subparagraphs below for blocking required.

a.	5-inch (125-mm) top-rail blocking, in doors indicated to have closers.

b.	5-inch (125-mm) bottom-rail blocking, in exterior doors and doors indicated to have kick, mop, or armor plates.

c.	5-inch (125-mm) midrail blocking, in doors indicated to have exit devices.

Usually delete "Blocking" Subparagraph and associated subparagraphs above and retain subparagraph below.

# 3.	Provide doors with either glued-block or structural composite lumber cores instead of particleboard cores at locations where exit devices are indicated.

B.	Interior Hardboard-Faced Doors:

1.	Core:  Either glued block or structural composite lumber.

Select one of three options in subparagraph above and one of two subparagraphs below.  Nonglued-block core is only available with second subparagraph.

# 2.	Construction:  Three plies, either bonded or nonbonded construction.

# 2.4	HOLLOW-CORE DOORS

A.	Interior Hardboard-Faced Doors:

Select one of two options in first subparagraph below; see referenced standard.

1.	Core:  Standard hollow core.

2.	Construction:  Hardboard faces glued directly to core.

3.	Blocking:  Provide wood blocking with minimum dimensions as follows:

a.	5-by-18-inch (125-by-460-mm) lock blocks at both stiles.

Blocking above is usually standard; subparagraphs below are optional.  Delete blocking not required.

# 2.5	LOUVERS AND LIGHT FRAMES

Delete this Article if no louvers or light frames are required.  Retain applicable types.  If more than one type is required, coordinate with Drawings.

A.	Wood Louvers:  Door manufacturer's standard solid-wood louvers, unless otherwise indicated.

# 2.6	FABRICATION

A.	Fabricate doors in sizes indicated for Project-site fitting.

Delete paragraph above or paragraph and subparagraph below.  Qualify above or below if exceptions.  Plastic-laminate-edged and factory-finished doors must be factory fitted and machined.  Fire-rated and plastic-laminate-faced doors with wood edges should also be factory fitted and machined.  Factory fitting and machining for other doors are optional.  See Evaluations.

B.	Factory fit doors to suit frame-opening sizes indicated, with the following uniform clearances and bevels, unless otherwise indicated:

Standard fitting may be inadequate for 2-1/2-inch (64-mm) and thicker doors or for doors exposed to wide changes in humidity and temperature.

# 1.	Comply with clearance requirements of referenced quality standard for fitting.  Comply with requirements in NFPA 80 for fire-rated doors.

Delete paragraph and subparagraphs below if doors are not premachined.

C.	Factory machine doors for hardware that is not surface applied.  Locate hardware to comply with DHI-WDHS-3.  Comply with final hardware schedules, door frame Shop Drawings, DHI A115-W series standards, and hardware templates.

Delete subparagraph below if no metal frames for wood doors.

# 1.	Coordinate measurements of hardware mortises in metal frames to verify dimensions and alignment before factory machining.

Retain subparagraph below with pairs of prefitted fire doors where astragals, etc., are required.

# 2.	Metal Astragals:  Premachine astragals and formed-steel edges for hardware for pairs of fire-rated doors.

Delete paragraph and subparagraph below if not applicable.  Indicate here or on Drawings if doors and transoms are rabbeted.  Verify that transom sizes and attachment method comply with fire ratings if any fire-rated doors with transoms are used.

Delete below if no outswinging exterior doors.  Before retaining, verify availability with manufacturers selected or delete and include with weather stripping in Division 8 Section "Door Hardware."

# 2.7	SHOP PRIMING

Delete this Article if factory-finished doors are required.  Factory fitting is recommended to minimize damage to shop-primed doors.

A.	Doors for Opaque Finish:  Shop prime faces and edges of doors, including cutouts, with one coat of wood primer specified in Division 9 Section "Painting."

Retain paragraph above or below, or both, as applicable.

# PART 3 - EXECUTION

# 3.1	EXAMINATION

A.	Examine doors and installed door frames before hanging doors.

1.	Verify that frames comply with indicated requirements for type, size, location, and swing characteristics and have been installed with level heads and plumb jambs.

2.	Reject doors with defects.

B.	Proceed with installation only after unsatisfactory conditions have been corrected.

# 3.2	INSTALLATION

A.	Hardware:  For installation, see Division 8 Section "Door Hardware" where field applied.

B.	Manufacturer's Written Instructions:  Install doors to comply with manufacturer's written instructions, referenced quality standard, and as indicated.

Delete subparagraph below if no fire-rated doors.

# 1.	Install fire-rated doors in corresponding fire-rated frames according to NFPA 80.

Delete first paragraph and subparagraphs below if all doors are factory fitted.  Factory fitting of fire-rated doors is preferred to job fitting because of limitations on trimming narrower stiles and rails.

C.	Job-Fitted Doors:  Align and fit doors in frames with uniform clearances and bevels as indicated below; do not trim stiles and rails in excess of limits set by manufacturer or permitted for fire-rated doors.  Machine doors for hardware.  Seal cut surfaces after fitting and machining.  Adjust doors as necessary if pre-hung.

1.	Clearances:  Provide 1/8 inch (3.2 mm) at heads, jambs, and between pairs of doors.  Provide 1/8 inch (3.2 mm) from bottom of door to top of decorative floor finish or covering.  Where threshold is shown or scheduled, provide 1/4 inch (6.4 mm) from bottom of door to top of threshold.

Delete subparagraph below if no fire-rated doors or if factory fitted.

a.	Comply with NFPA 80 for fire-rated doors.

# 2.	Bevel non-fire-rated doors 1/8 inch in 2 inches (3-1/2 degrees) at lock and hinge edges.

Subparagraph above is standard bevel; revise to suit Project if required.  See Evaluations.  Delete subparagraph below if no fire-rated doors or if factory fitted.  Fire doors can be trimmed only to a limited extent because of narrow stiles and rails.

# 3.	Bevel fire-rated doors 1/8 inch in 2 inches (3-1/2 degrees) at lock edge; trim stiles and rails only to extent permitted by labeling agency.

D.	Factory-Fitted Doors:  Align in frames for uniform clearance at each edge.

E.	Field-Finished Doors:  Refer to the following for finishing requirements:

1.	Division 9 Section "Painting."

# 3.3	ADJUSTING

A.	Operation:  Re-hang or replace doors that do not swing or operate freely.

B.	Finished Doors:  Replace doors that are damaged or do not comply with requirements.  Doors may be repaired or refinished if work complies with requirements and shows no evidence of repair or refinishing.

# END OF SECTION 08211