North Elevation

| Floor Level | Gross Area | Net Free Area |
| --- | --- | --- |
| Ground Floor | 2653.55 | 590.04 |
| First Floor | 2590 | 513.64 |
| Second Floor | 2590 | 513.64 |
| Third Floor | 2590 | 513.64 |
| Forth Floor | 2590 | 513.64 |
| Fifth Floor | 2590 | 513.64 |

East Elevation

| Floor Level | Gross Area | Net Free Area |
| --- | --- | --- |
| Ground Floor | 1220.76 | 403.15 |
| First Floor | 1208 | 342.70 |
| Second Floor | 1208 | 342.70 |
| Third Floor | 1208 | 342.70 |
| Forth Floor | 1208 | 342.70 |
| Fifth Floor | 1208 | 342.70 |

South Elevation

| Floor Level | Gross Area | Net Free Area |
| --- | --- | --- |
| Ground Floor | 2927.58 | 163.22 |
| First Floor | 2592.49 | 126.24 |
| Second Floor | 2592.49 | 679.53 |
| Third Floor | 2592.49 | 679.53 |
| Forth Floor | 2592.49 | 679.53 |
| Fifth Floor | 2592.49 | 679.53 |

West Elevation

| Floor Level | Gross Area | Net Free Area |
| --- | --- | --- |
| Ground Floor | 1291.87 | 470.19 |
| First Floor | 1208 | 463.8 |
| Second Floor | 1208 | 463.8 |
| Third Floor | 1208 | 404.7 |
| Forth Floor | 1208 | 463.8 |
| Fifth Floor | 1208 | 404.7 |

Combined Elevations

| Floor Level | Gross Area | Net Free Area | % Open |
| --- | --- | --- | --- |
| Ground Floor | 8093.76 | 1626.60 | 20% |
| First Floor | 7598.49 | 1546.38 | 20.3% |
| Second Floor | 7598.49 | 2099.67 | 27.6% |
| Third Floor | 7598.49 | 2040.57 | 26.8% |
| Forth Floor | 7598.49 | 2099.67 | 27.6% |
| Fifth Floor | 7598.49 | 2040.57 | 26.8% |

Linear Open Area

| Floor Level | Gross Length | Net Open Length | % Open |
| --- | --- | --- | --- |
| Ground Floor | 747’-8” | 193’-7 ¾” | 25.9% * |
| First Floor | 747’-8” | 293’-8 1/2 | 39% * |
| Second Floor | 747’-8” | 528’-3” | 70.6% |
| Third Floor | 747’-8” | 516’3” | 69% |
| Forth Floor | 747’-8” | 528’-3” | 70.6% |
| Fifth Floor | 747’-8” | 516’3” | 69% |

* See exception 406.3.3.1.  Openings provided on East and West elevations.

Interior Open Walls

This garage has no interior walls.  Typical structure between north ramp and south ramp greater then 20% open.