Copyright 1998, The American Institute of Architects (AIA)

SECTION 08711

DOOR HARDWARE

GENERAL

SUMMARY

This Section includes the following:

Commercial door hardware for the following:

Swinging doors.

Other doors to the extent indicated.

Cylinders for doors specified in other Sections.

Products furnished, but not installed, under this Section include the following.  Coordinating, purchasing, delivering, and scheduling remain requirements of this Section.

Delete subparagraph below if all door hardware for entrance doors is specified in this Section.

Cylinders for locks on aluminum entrance doors.

Delete below if removable-core key system is not specified.

SUBMITTALS

Product Data:  Include installation details, material descriptions, dimensions of individual components and profiles, and finishes.

Retain paragraph and subparagraphs below for electrified door hardware.

Retain one of two paragraphs below.  First is usually for plastic-laminate or acrylic armor, kick, mop, and stretcher plates.

Samples for Selection:  Manufacturer's color charts consisting of units or sections of units showing the full range of colors, textures, and patterns available for each type of door hardware indicated.

Delete paragraph above if colors and other characteristics are preselected and specified or scheduled.  Retain paragraph below with or without above.

Retain "Supplier Qualifications" Paragraph in "Quality Assurance" Article with paragraph below.

Door Hardware Schedule:  Prepared by or under the supervision of supplier, detailing fabrication and assembly of door hardware, as well as procedures and diagrams.  Coordinate the final Door Hardware Schedule with doors, frames, and related work to ensure proper size, thickness, hand, function, and finish of door hardware.

Format:  Comply with scheduling sequence and vertical format in DHI's "Sequence and Format for the Hardware Schedule."

Organization:  Organize the Door Hardware Schedule into door hardware sets indicating complete designations of every item required for each door or opening.

Delete subparagraph below if Door Hardware Schedule is not at end of Part 3.

Organize door hardware sets in same order as in the Door Hardware Schedule at the end of Part 3.

Content:  Include the following information:

Type, style, function, size, label, hand, and finish of each door hardware item.

Manufacturer of each item.

Fastenings and other pertinent information.

Location of each door hardware set, cross-referenced to Drawings, both on floor plans and in door and frame schedule.

Explanation of abbreviations, symbols, and codes contained in schedule.

Mounting locations for door hardware.

Door and frame sizes and materials.

Retain subparagraph below for electrified door hardware.

Delete subparagraph above or below, or both if early approval is not critical.  Sequence below fragments and extends review process.

Submittal Sequence:  Submit initial draft of final schedule along with essential Product Data to facilitate the fabrication of other work that is critical in the Project construction schedule.  Submit the final Door Hardware Schedule after Samples, Product Data, coordination with Shop Drawings of other work, delivery schedules, and similar information has been completed and accepted.

Retain "Supplier Qualifications" Paragraph in "Quality Assurance" Article with paragraph below.

Keying Schedule:  Prepared by or under the supervision of supplier, detailing Owner's final keying instructions for locks.  Include schematic keying diagram and index each key set to unique door designations.

Retain paragraph and subparagraph below for electrified door hardware.

Product Certificates:  Signed by manufacturers of electrified door hardware certifying that products furnished comply with requirements.

Certify that door hardware approved for use on types and sizes of labeled fire doors complies with listed fire door assemblies.

Retain paragraph below for locks, latches, delayed-egress locks, and closers if "Regulatory Requirements" Paragraph is retained in "Quality Assurance" Article.

Product Test Reports:  Based on evaluation of comprehensive tests performed by manufacturer and witnessed by a qualified testing agency, indicating current products comply with requirements.

Maintenance Data:  For each type of door hardware to include in maintenance manuals specified in Division 1.

Warranties:  Special warranties specified in this Section.

QUALITY ASSURANCE

Installer Qualifications:  An experienced installer who has completed door hardware similar in material, design, and extent to that indicated for this Project and whose work has resulted in construction with a record of successful in-service performance.

Supplier Qualifications:  Door hardware supplier with warehousing facilities in Project's vicinity and who is or employs a qualified Architectural Hardware Consultant, available during the course of the Work to consult with Contractor, Architect, and Owner about door hardware and keying.

Retain subparagraph below if required.

Scheduling Responsibility:  Preparation of door hardware and keying schedules.

Architectural Hardware Consultant Qualifications:  A person who is currently certified by the Door and Hardware Institute as an Architectural Hardware Consultant and who is experienced in providing consulting services for door hardware installations that are comparable in material, design, and extent to that indicated for this Project.

Delete subparagraph below if not required.

Source Limitations:  Obtain each type and variety of door hardware from a single manufacturer, unless otherwise indicated.

Delete subparagraph below if not required.

Delete paragraph and subparagraph below if not required.

Fire-Rated Door Assemblies:  Provide door hardware for assemblies complying with NFPA 80 that are listed and labeled by a testing and inspecting agency acceptable to authorities having jurisdiction, for fire ratings indicated, based on testing according to NFPA 252.

Revise below if positive-pressure testing is required.

Delete paragraph below if keying is not extensive or complex enough to justify a keying conference.  If retaining, coordinate with Division 1.  Identify specific participants not mentioned in Division 1.

Keying Conference:  Conduct conference at Project site to comply with requirements in Division 1 Section "Project Management and Coordination."  Incorporate keying conference decisions into final keying schedule after reviewing door hardware keying system including, but not limited to, the following:

Function of building, flow of traffic, purpose of each area, degree of security required, and plans for future expansion.

Preliminary key system schematic diagram.

Requirements for key control system.

Delete paragraph below if work of this section is not extensive or complex enough to justify a preinstallation conference.  If retaining, coordinate with Division 1.

Retain paragraph above if requirements in Division 1 are adequate for Project.  Retain paragraph below if additional requirements are necessary; include information about conference.  Identify specific participants not mentioned in Division 1.

DELIVERY, STORAGE, AND HANDLING

Inventory door hardware on receipt and provide secure lock-up for door hardware delivered to Project site.

Tag each item or package separately with identification related to the final Door Hardware Schedule, and include basic installation instructions with each item or package.

Deliver keys to manufacturer of key control system.

Delete paragraph above or below or revise to suit Project.  Retain below for high-security cylinders.

COORDINATION

Delete paragraph below if no recessed pivots or closers.

Delete paragraph below only if all door hardware preparation and installation will be performed at Project.

Templates:  Obtain and distribute to the parties involved templates for doors, frames, and other work specified to be factory prepared for installing door hardware.  Check Shop Drawings of other work to confirm that adequate provisions are made for locating and installing door hardware to comply with indicated requirements.

Delete below if no electrified door hardware requires connections.

WARRANTY

When warranties are required, verify with Owner's counsel that special warranties stated in this Article are not less than remedies available to Owner under prevailing local laws.  Coordinate with Division 1 Section "Warranties."

General Warranty:  Special warranties specified in this Article shall not deprive Owner of other rights Owner may have under other provisions of the Contract Documents and shall be in addition to, and run concurrent with, other warranties made by Contractor under requirements of the Contract Documents.

Special Warranty:  Written warranty, executed by manufacturer agreeing to repair or replace components of door hardware that fail in materials or workmanship within specified warranty period.  Failures include, but are not limited to, the following:

Structural failures including excessive deflection, cracking, or breakage.

Faulty operation of operators and door hardware.

Deterioration of metals, metal finishes, and other materials beyond normal weathering.

Verify available warranties in four paragraphs below and retain or insert number.

Warranty Period:  One year from date of Substantial Completion, unless otherwise indicated.

Retain paragraph below for electromagnetic and delayed-egress locks.

Delete two paragraphs below if no closers.  Verify with manufacturers selected.

Warranty Period for Manual Closers:  10 years from date of Substantial Completion.

MAINTENANCE SERVICE

Maintenance Tools and Instructions:  Furnish a complete set of specialized tools and maintenance instructions as needed for Owner's continued adjustment, maintenance, and removal and replacement of door hardware.

PRODUCTS

See Editing Instruction No. 3 in the Evaluations in Division 8 Section "Door Hardware" for selecting door hardware products.

Coordinate the following articles with Door Hardware Schedule at end of Part 3.  Delete door hardware products not required.

SCHEDULED DOOR HARDWARE

Delete this Article if door hardware allowance is used or if there is no Door Hardware Schedule.

General:  Provide door hardware for each door to comply with requirements in this Section and the Door Hardware Schedule at the end of Part 3.

Retain manufacturers' or BHMA designations below to correlate with those indicated in Door Hardware Schedule at end of Part 3.

Door Hardware Sets:  Provide quantity, item, size, finish or color indicated, and named manufacturer's products.

Retain subparagraph below for electrified door hardware.

Designations:  Requirements for design, grade, function, finish, size, and other distinctive qualities of each type of door hardware are indicated in the Door Hardware Schedule at the end of Part 3.  Products are identified by using door hardware designations, as follows:

Retain one of two subparagraphs below.

Named Manufacturer's Products:  Product designation and manufacturer are listed for each door hardware type required for the purpose of establishing minimum requirements.  Manufacturers' names are abbreviated in the Door Hardware Schedule.

Retain below for a nonproprietary specification based on referencing BHMA standards, with or without naming available manufacturers.

References to BHMA Standards:  Provide products complying with these standards and requirements for description, quality, and function.

HINGES

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Hinges:

Hager Companies (HAG).

McKinney Products Company; Div. of ESSEX Industries, Inc. (MCK).

Stanley Commercial Hardware; Div. of The Stanley Works (STH).

Continuous Geared Hinges:

Hager Companies (HAG).

McKinney Products Company; Div. of ESSEX Industries, Inc. (MCK).

Pemko Manufacturing Co., Inc. (PEM).

Zero International, Inc. (ZRO).

Delete paragraph and subparagraphs below if manufacturers' products are named in Door Hardware Schedule to specify hinges and pivots.

Delete paragraph below if only continuous geared hinges are required or if quantity is included in Door Hardware Schedule.

Quantity:  Provide the following, unless otherwise indicated:

Two Hinges:  For doors with heights up to 60 inches (1524 mm).

Three Hinges:  For doors with heights 61 to 90 inches (1549 to 2286 mm).

Four Hinges:  For doors with heights 91 to 120 inches (2311 to 3048 mm).

For doors with heights more than 120 inches (3048 mm), provide 4 hinges, plus 1 hinge for every 30 inches (750 mm) of door height greater than 120 inches (3048 mm).

Add sizes not listed and delete sizes not required.  Delete paragraph and tables below if only continuous geared hinges are required or if sizes are in Door Hardware Schedule.

The following is a guide for hinge size and type required for this project.

# Manufacturer 		     Interior:

1-3/4” Doors	Stanley 		FBB179-4 1/2"

up to 3’-0” wide	Hager 		BB1279-4 1/2"

McKinney 		TA-TB2714-4 1/2"

1-3/4” Doors	Stanley 		FBB168-4 1/2"

over 3’-0” wide	Hager 		BB1168-4 1/2"

McKinney 		T4A-T4B3786-4 1/2"

Template Requirements:  Except for hinges and pivots to be installed entirely (both leaves) into wood doors and frames, provide only template-produced units.

Delete paragraph below if requirements are indicated in Door Hardware Schedule.

Delete paragraph and subparagraphs below if only continuous geared hinges are required.

Hinge Options:  Comply with the following where indicated in the Door Hardware Schedule or on Drawings:

Hospital tips below are used in locations where additional cleanliness and safety are required.

Add requirement for decorator tips if required.  Types include oval, ball, steeple, urn, and acorn tips.

Nonremovable Pins:  Provide set screw in hinge barrel that, when tightened into a groove in hinge pin, prevents removal of pin while door is closed; for the following applications:

Retain one or both subparagraphs below.

Outswinging exterior doors.

Outswinging corridor doors with locks.

Corners:  Square.

Delete subparagraph and associated subparagraphs below if not required.  Electrified functions are available only for full-mortise, pivot-reinforced, and pivot hinges and for continuous geared hinges.

Continuous-Geared Hinges:  Minimum 0.120-inch- (3.0-mm-) thick, hinge leaves with minimum overall width of 4 inches (100 mm); fabricated to full height of door and frame.  Finish components after milling and drilling are complete.  Fabricate hinges to template screw locations.

Fasteners:  Comply with the following:

Machine Screws:  For metal doors and frames.  Install into drilled and tapped holes.

Wood Screws:  For wood doors and frames.

Threaded-to-the-Head Wood Screws:  For fire-rated wood doors.

Screws:  Phillips flat-head screws; machine screws (drilled and tapped holes) for metal doors, wood screws for wood doors and frames.  Finish screw heads to match surface of hinges.

MORTISED LOCKS AND LATCHES

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Mechanical Locks and Latches:

Best Lock Corporation (BLC).

Corbin Russwin Architectural Hardware; Div. of Yale Security Inc. (CR).

Sargent Manufacturing Company; Div. of ESSEX Industries, Inc. (SGT).

Schlage Lock Company; an Ingersoll-Rand Company (SCH).

Delete paragraph and subparagraphs below if manufacturers' products are named in Door Hardware Schedule to specify locks and latches.

Delete first four paragraphs below if grade is always indicated in door hardware sets.  Insert function requirements with each if an allowance is used to specify door hardware.

Mortise Locks:  Stamped steel case with steel or brass parts; BHMA Grade 1; Series 1000.

Provide one of the following manufacturers and designs:

Best H Series

Corbin/Russwin ML2000 Series

Sargent 8200 Series

Schlage L9000 Series

Lock Trim:  Comply with the following:

Most levers in subparagraph below are cast.

Lever:  Cast.

Most knobs in subparagraph below are wrought.

Escutcheon (Rose):  Forged.

Dummy Trim:  Match lever lock trim and escutcheons.

Lockset Designs:  Provide the lockset design designated below or, if sets are provided by another manufacturer, provide designs that match those designated:

Best, 14 design

Subparagraph below is an example that uses one type of lock.  Revise to suit lock type specified for Project.  Retain first option if BHMA standards are used to specify door hardware and lock design is indicated on Drawings.

Corbin/Russwin, Newport design

Sargent,  LNL design

Schlage,  06A design

Lock Functions: Lock functions as indicated in the hardware schedule shall be as follows:

FUNCTION	     SARGENT	   SCHLAGE	CORBIN/RUSSWIN	BEST

A			  04		       80			57			  EW

B			  05		       50			51			   E

C			  15		       10			10			   N

D			  37		       70			55			   J

E			  16		       60			42		 	   F

F			  65		       40			30			  LF

Lock Throw:  Comply with testing requirements for length of bolts to comply with labeled fire door requirements, and as follows:

Mortise Locks:  Minimum 3/4-inch (19-mm) latchbolt throw.

Deadbolts:  Minimum 1-inch (25-mm) bolt throw.

Backset:  2-3/4 inches (70 mm), unless otherwise indicated.

EXIT DEVICES

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Precision Hardware, Inc. (PH).

Sargent Manufacturing Company; Div. of ESSEX Industries, Inc. (SGT).

Von Duprin; an Ingersoll-Rand Company (VD).

Products:  All exit devices for this project shall be one of the following:

Precision Olympian Series

The 80 Series exit device by Sargent & Co.

98 Series by Von Duprin Division

Delete paragraph and subparagraph below if manufacturers' products are named in Door Hardware Schedule to specify exit devices.

Standard:  BHMA A156.3.

Delete subparagraph below if grade is always indicated in door hardware sets.

BHMA Grade:  Grade 1.

Certified Products:  Provide exit devices listed in BHMA's "Directory of Certified Exit Devices."

Retain one of first two paragraphs below, or both.  Only fire exit devices may be used for fire doors.  NFPA 80 distinguishes between panic exit hardware and fire exit hardware.  See the Evaluations in Division 8 Section "Door Hardware."

Panic Exit Devices:  Listed and labeled by a testing and inspecting agency acceptable to authorities having jurisdiction, for panic protection, based on testing according to UL 305.

UL test below includes operational test of 100,000 cycles.  BHMA A156.3 requires 250,000 cycles for Grade 1 and 100,000 cycles for Grade 2.

Fire Exit Devices:  Complying with NFPA 80 that are listed and labeled by a testing and inspecting agency acceptable to authorities having jurisdiction, for fire and panic protection, based on testing according to UL 305 and NFPA 252.

Electric Latch Retraction Exit Devices:  Provide hardware package consisting of Sargent exit device No. 56-80 Series, electric hinge, and No. 3510 power supply. Equivalent package by other listed manufacturers will be acceptable. Proximity readers by others.

Retain paragraph below if exit device levers, knobs, and pulls are required to match lockset and latchset designs.

Outside Trim:  Pull with cylinder; material and finish to match locksets, unless otherwise indicated.

Match design for locksets and latchsets, unless otherwise indicated.

Include below if physical abuse is a design consideration.

Through Bolts:  For exit devices and trim on fire-rated wood doors.

The following functions shall be required where specified:

FUNCTION	VON DUPRIN		SARGENT			     PRECISION

A			CD99NL-OP		 16-8804			1103CD x 1123-38

B			CD99EO			 16-8810			1101CD x 1123-38

C			99L					8813ET		 		1108 x 39L x 1123-38

D			99L-BE				8815ET		 		1108A x 39L x 1123-38

E			99EO-F				12-8810		   	FL-1101 x 1123-38

F			99L-F				12-8813ET	    		FL-1108 x 39L x 1123-38

G			99L-F-BE			12-8815ET		 	FL-1108A x 39L x 1123-38

H			CD9927EO			16-8710			1201CD x 1123-38

I			9927L				8713ET		   		1208 x 39L x 1123-38

J			9927L-BE			8715ET		   		1208A x 39L x 1123-38

K			CD9927EO x LBR	16-PP/PR8710		1201CDx1123-38xLBR

L			9927L x LBR		 PP/PR8713ET	  	1208x39Lx1123-38xLBR

M			9927L-BE x LBR	 PP/PR8715ET	  	1208Ax39Lx1123-38xLBR

N			9927EO-F			12-8710			FL-1201 x 1123-38

O			9927L-F			12-8713ET	  		FL-1208x39Lx1123-38

P			9927L-F-BE		12-8715ET		  	FL-1208Ax39Lx1123-38

Q			9927EO-F x LBR	12-PP/PR8710		FL-1201x1123-38xLBR

R			9927L-F x LBR		12-PP/PR8713ET	FL-1208x39Lx1123-38xLBR

S		      9927-L-F-BExLBR	12-PP/PR8715ET	FL-1208Ax39Lx1123-38xLBR

T			EL9927-TL			56-8710-306

U			EL99NL-OP		56-8804

CYLINDERS AND KEYING

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

Cylinders for Interior Doors:  Same manufacturer as for locks and latches.

Retain subparagraph above or subparagraph and list of manufacturers below.  Above significantly reduces competition and may result in higher costs.

Cylinders for Exterior Doors:

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Best Lock Corporation (BLC).

High Security Grand Master by Corbin Russwin.

Medeco High Security Locks, Inc. (MED).

Sargent Signature Series by Sargent Manufacturing Company.

Primus by Schlage Lock Company.

Key Control Systems:

Key Control Systems, Inc. (KCS).

Telkee, Inc.

Delete paragraph and subparagraphs below if manufacturers' products are named in Door Hardware Schedule to specify cylinders and key control systems.

Standards:  Comply with the following:

Cylinders:  BHMA A156.5.

Key Control System:  BHMA A156.5.

Delete paragraph below if grade is always indicated in door hardware sets.

Cylinder Grade:  BHMA Grade 1.

Cylinders:  Manufacturer's standard tumbler type, constructed from brass or bronze, stainless steel, or nickel silver, and complying with the following:

Five pins in subparagraph below are not available for high-security cylinders.

Number of Pins:  Six and seven.

Retain applicable types from three subparagraphs below.

Mortise Type:  Threaded cylinders with rings and straight- or clover-type cam.

Rim Type:  Cylinders with back plate, flat-type vertical or horizontal tailpiece, and raised trim ring.

Construction Keying:  Comply with the following:

Retain one of two subparagraphs below.

Construction Master Keys:  Provide cylinders with feature that permits voiding of construction keys without cylinder removal.  Provide 10 construction master keys.

Construction Cores:  Provide construction cores that are replaceable by permanent cores.  Provide 10 construction master keys.

Keying System:  Unless otherwise indicated, provide a factory-registered keying system complying with the following requirements:

Retain one of four subparagraphs below.

Master Key System:  Cylinders are operated by a change key and a master key.

Retain subparagraph below if required.

Keyed Alike:  Key all cylinders to the same change key.

Cylinders shall be master keyed.

Keys:  Provide nickel-silver keys complying with the following:

Delete subparagraph below if key does not require special marking.

Stamping:  Permanently inscribe each key with a visual key control number and include the following notation:

Notation:  Information to be furnished by Owner.

Quantity:  In addition to one extra blank key for each lock, provide the following:

Retain subparagraphs below corresponding to type of keying system selected above.

Cylinder Change Keys:  Three.

Master Keys:  Five.

Key Control System:  BHMA Grade 1 system, including key-holding hooks, labels, two sets of key tags with self-locking key holders, key-gathering envelopes, and temporary and permanent markers.  Contain system in metal cabinet with baked-enamel finish.

Retain one of three subparagraphs below to suit Project.  First is for minimum of 600 hooks; second is for up to 1200 hooks.

Wall-Mounted Cabinet:  Cabinet with hinged-panel door equipped with key-holding panels and pin-tumbler cylinder door lock.

Revise subparagraph below if required.

Capacity:  Able to hold keys for 150 percent of the number of locks.

Revise subparagraph below if cross-index system is not prepared by manufacturer.

Cross-Index System:  Set up by key control manufacturer, complying with the following:

Retain one subparagraph below.

Card Index:  Furnish four sets of index cards for recording key information.  Include three receipt forms for each key-holding hook.

STRIKES

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Electric Strikes:

Adams Rite Manufacturing Co. (ARM).

Folger Adam Security Inc. (FAS).

Hanchett Entry Systems, Inc. (HES).

Locknetics Security Engineering; a Harrow Company (LSE).

Precision Hardware, Inc. (PH).

Rutherford Controls Inc.; Div. of Fritz Fuss (RC).

Security Door Controls (SDC).

Trine Products Company (TP).

Von Duprin, Inc.; an Ingersoll-Rand Company (VD).

Delete paragraph and subparagraphs below if manufacturers' products are named in Door Hardware Schedule to specify strikes.

Standards:  Comply with the following:

Strikes for Bored Locks and Latches:  BHMA A156.2.

Strikes for Mortise Locks and Latches:  BHMA A156.13.

Dustproof Strikes:  BHMA A156.16.

Strikes:  Provide manufacturer's standard strike with strike box for each latch or lock bolt, with curved lip extended to protect frame, finished to match door hardware set, unless otherwise indicated, and as follows:

Delete three subparagraphs below if not required.

Flat-Lip Strikes:  For locks with three-piece antifriction latchbolts, as recommended by manufacturer.

Extra-Long-Lip Strikes:  For locks used on frames with applied wood casing trim.

Aluminum-Frame Strike Box:  Provide manufacturer's special strike box fabricated for aluminum framing.

Dustproof Strikes:  BHMA Grade 1.

Electric Strikes:  BHMA Grade 1, UL listed as a burglary protection device and fire door accessory.

In particular the electric strikes shall carry a listing under the category of "single point locks or latches" for use with single swing fire doors having a 3-hour (A) rating or less.

Provide a non-fail safe type solenoid actuated by a 24 VAC or DC current and face plate shall be in US 26D finish.

Manufacture of corrosion resistant metals with a cast stainless steel case and working parts, and stainless steel springs.

Provide horizontal adjustment for misalignment, and shall be reversible and capable of accepting locksets specified in the lock or exit devise section of the specification.

Electric strikes shall fit a cutout in the frame not less than 9" high x 1 3/8" wide with a frame face cutout of 1 1/2" wide and 3 3/4" high.

Provide electric strikes on doors indicated to have access control. See electrical.

Delete below if grade is always indicated in door hardware sets.

OPERATING TRIM

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Baldwin Hardware Corporation (BH).

Burns Manufacturing Incorporated (BM).

Don-Jo Mfg., Inc. (DJO).

Ives:  H. B. Ives (IVS).

Rockwood Manufacturing Company (RM).

Stanley Commercial Hardware; Div. of The Stanley Works (STH).

Delete paragraph below if manufacturers' products are named in Door Hardware Schedule to specify operating trim.

Standard:  Comply with BHMA A156.6.

Materials:  Fabricate from stainless steel, unless otherwise indicated.

Include below if referencing BHMA standards in Door Hardware Schedule to indicate operating trim requirements; delete if naming manufacturers' products.

Door Pulls:  1inch diameter by 10 inches long.

Rockwood	111

Burns		26C

Quality		163-10"

Push/Pull Bars:  1inch diameter.

Rockwood	BF11147 x T1006 Mounting

Burns		BF26C x 442 x Sim. Mounting as Above

Quality		BF482 x Sim. Mounting as Above

CLOSERS

Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Surface-Mounted Closers:

LCN Closers; an Ingersoll-Rand Company (LCN).

Sargent Manufacturing Company; Div. of ESSEX Industries, Inc. (SGT).

Delete paragraph below if manufacturers' products are named in Door Hardware Schedule to specify closers.

Standards:  Comply with the following:

Closers:  BHMA A156.4.

Delete first two paragraphs below if grade is always indicated in door hardware sets.

Surface Closers:  BHMA Grade 1.

Certified Products:  Provide door closers listed in BHMA's "Directory of Certified Door Closers."

Delete paragraph below if not required.

Retain paragraph below if needed.

Size of Units:  Unless otherwise indicated, provide the following.  Provide factory-sized closers, adjustable to meet field conditions and requirements for opening force.

LCN:

Exterior: 4040 Series

Interior:  4010 Series

Sargent:

Exterior: 281

Interior:  281

PROTECTIVE TRIM UNITS

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Metal Protective Trim Units:

Burns Manufacturing Incorporated (BM).

Hager Companies (HAG).

Ives:  H. B. Ives (IVS).

Rockwood Manufacturing Company (RM).

Delete paragraph below if manufacturers' products are named in Door Hardware Schedule to specify protective trim units.

Standard:  Comply with BHMA A156.6.

Materials:  Fabricate protection plates from the following:

Retain materials below to suit Project.  If retaining more than one, indicate location of each on Drawings or by repeating material requirements with each type of protective plate.

Stainless Steel:  0.050 inch (1.3 mm) thick; beveled top and 2 sides.

Fasteners:  Provide manufacturer's standard exposed fasteners for door trim units consisting of either machine or self-tapping screws.

Americans with Disabilities Act Accessibility Guidelines appendix recommends protection plates be sized 2 inches (51 mm) less than door width.

Fabricate protection plates as follows:

Push Plates: 16" high by 8" wide.

Kick Plates: 10" high by 1-1/2" less than door width for single doors and 1" less than door width for pairs of doors. Kick plates shall be applied to push side of all doors where noted.

STOPS AND HOLDERS

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Stops and Bumpers:

Burns Manufacturing Incorporated (BM).

Glynn-Johnson; an Ingersoll-Rand Company (GJ).

Hager Companies (HAG).

Ives:  H. B. Ives (IVS).

Rockwood Manufacturing Company (RM).

Delete paragraph and subparagraphs below if manufacturers' products are named in Door Hardware Schedule to specify stops and holders.

Standards:  Comply with the following:

Stops and Bumpers:  BHMA A156.16.

Mechanical Door Holders:  BHMA A156.16.

Door Silencers:  BHMA A156.16.

Delete first four paragraphs below if grade is always indicated in door hardware sets.

Wall Stops:  BHMA Grade 1.  Wall type bumpers with concealed type flange shall be used where ever possible and shall be one of the following:

Ives - 407 1/2

Door Controls - 3211T

Rockwood - 409

Floor Stops: Where wall type bumpers cannot be used, provide dome type, floor mounted stops of the proper height as follows:

Ives - 436, 438

Door Controls - 3310X, 3320X

Rockwood - 440, 442

Do not mount floor stops where they will impede traffic.

Exterior doors striking masonry and doors specified to have door stops and holders, shall have cast bronze wall or floor type door stops with hook or staple type holders to selectively hold doors in open position. The following will be acceptable:

Ives - 445, 446

Door Controls - 3237X, 3347X

Rockwood - 473, 477

Provide matching finishes for hardware units at each door or opening, to the greatest extent possible, and except as otherwise indicated. Reduce differences in color and textures as much as commercially possible where the base metal or metal forming process is different for individual units of hardware exposed at the same door or opening. In general, match items to the manufacturer's standard finish for the latch and lock set (or push-pull units if no latch-lock sets) for color and texture.

Retain paragraph below unless silencers are specified with wood door frames in Division 6 Section "Interior Architectural Woodwork."

Delete below if silencers are specified with metal door frames in another Division 8 Section.

Silencers for Metal Door Frames:  BHMA Grade 1; neoprene or rubber, minimum diameter 1/2 inch (13 mm); fabricated for drilled-in application to frame.

DOOR GASKETING

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

See Editing Instruction No. 1 in the Evaluations in Division 8 Section "Door Hardware" for cautions about naming products and manufacturers.

Door Gasketing:

National Guard Products, Inc. (NGP).

Pemko Manufacturing Co., Inc. (PEM).

Reese Enterprises, Inc. (RE).

Zero International, Inc. (ZRO).

Door Bottoms:

National Guard Products, Inc. (NGP).

Pemko Manufacturing Co., Inc. (PEM).

Reese Enterprises, Inc. (RE).

Zero International, Inc. (ZRO).

Delete paragraph below if manufacturers' products are named in Door Hardware Schedule to specify door gasketing.

Standard:  Comply with BHMA A156.22.

Weatherstripping:  Provide continuous weather-strip gasketing on exterior doors, No. A626A by National Guard Products or approved substitute.  Provide door bottom sweep No. 95WH by National Guard Products or approved substitute.  Provide meeting stile gaskets No. 600A by National Guard Products or approved substitute.

Perimeter Gasketing:  Apply to head and jamb, forming seal between door and frame.

Meeting Stile Gasketing:  Fasten to meeting stiles, forming seal when doors are closed.

Door Bottoms:  Apply to bottom of door, forming seal with threshold when door is closed.

Fire Seals: Provide No. 9440 by National Guard Products or approved substitute. Color as selected by the Architect.

THRESHOLDS

Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

See Editing Instruction No. 1 in the Evaluations in Division 8 Section"Door Hardware" for cautions about naming products and manufacturers.

Hager Companies (HAG).

National Guard Products, Inc. (NGP).

Pemko Manufacturing Co., Inc. (PEM).

Reese Enterprises, Inc. (RE).

Zero International, Inc. (ZRO).

Delete below if manufacturers' products are named in Door Hardware Schedule to specify thresholds.

Standard:  Comply with BHMA A156.21.

Provide No. 896 with door bottom sweep No. 95WH by National Guard Products or approved substitute.

If needed, add requirements for access control devices, such as digital keypads, proximity sensors, switch devices, etc.

FABRICATION

Delete paragraph and subparagraph below if cost is prime consideration or if visibility of manufacturer's name on items is not objectionable.

Manufacturer's Nameplate:  Do not provide manufacturers' products that have manufacturer's name or trade name displayed in a visible location (omit removable nameplates) except in conjunction with required fire-rated labels and as otherwise approved by Architect.

Manufacturer's identification will be permitted on rim of lock cylinders only.

Base Metals:  Produce door hardware units of base metal, fabricated by forming method indicated, using manufacturer's standard metal alloy, composition, temper, and hardness.  Furnish metals of a quality equal to or greater than that of specified door hardware units and BHMA A156.18 for finishes.  Do not furnish manufacturer's standard materials or forming methods if different from specified standard.

Fasteners:  Provide door hardware manufactured to comply with published templates generally prepared for machine, wood, and sheet metal screws.  Provide screws according to commercially recognized industry standards for application intended.  Provide Phillips flat-head screws with finished heads to match surface of door hardware, unless otherwise indicated.

Delete or modify subparagraph below for low-cost work and where visual quality is unimportant.  Coordinate with Division 8 Section "Wood Doors."

Concealed Fasteners:  For door hardware units that are exposed when door is closed, except for units already specified with concealed fasteners.  Do not use through bolts for installation where bolt head or nut on opposite face is exposed unless it is the only means of securely attaching the door hardware.  Where through bolts are used on hollow door and frame construction, provide sleeves for each through bolt.

NFPA 80 requires locks, latches, surface-mounted top and bottom bolts, and fire exit hardware to be secured with machine screws or through bolts.

Steel Machine or Wood Screws:  For the following fire-rated applications:

Mortise hinges to doors.

Strike plates to frames.

Closers to doors and frames.

Steel Through Bolts:  For the following fire-rated applications, unless door blocking is provided:

Surface hinges to doors.

Closers to doors and frames.

Surface-mounted exit devices.

Spacers or Sex Bolts:  For through bolting of hollow metal doors.

Fasteners for Wood Doors:  Comply with requirements of DHI WDHS.2, "Recommended Fasteners for Wood Doors."

FINISHES

Standard:  Comply with BHMA A156.18.

Protect mechanical finishes on exposed surfaces from damage by applying a strippable, temporary protective covering before shipping.

Appearance of Finished Work:  Variations in appearance of abutting or adjacent pieces are acceptable if they are within one-half of the range of approved Samples.  Noticeable variations in the same piece are not acceptable.  Variations in appearance of other components are acceptable if they are within the range of approved Samples and are assembled or installed to minimize contrast.

Provide the following finishes:

Butts and Hinges:  				26D

Continuous Gear Hinges		28

Locks & Lock Trim:  			26D

Exit Devices:  					32D

Door Controls - Closers:  		Sprayed Alum. Finish

Mortise Locks & Latches:  		26D

Door Stops						26D/32D

Weatherstripping				Aluminum

Threshold						Aluminum

Kickplates						32D

Pulls							32D

EXECUTION

EXAMINATION

Examine doors and frames, with Installer present, for compliance with requirements for installation tolerances, labeled fire door assembly construction, wall and floor construction, and other conditions affecting performance.

Examine roughing-in for electrical power systems to verify actual locations of wiring connections before electrified door hardware installation.

Proceed with installation only after unsatisfactory conditions have been corrected.

PREPARATION

NFPA 80 restricts on-site door preparation to that required for surface-applied door hardware, function holes for mortise locks, holes for labeled viewers, undercutting of doors, and protection plates.

Steel Doors and Frames:  Comply with DHI A115 series.

Surface-Applied Door Hardware:  Drill and tap doors and frames according to SDI 107.

Wood Doors:  Comply with DHI A115-W series.

INSTALLATION

Mounting Heights:  Mount door hardware units at heights indicated in following applicable publications, unless specifically indicated or required to comply with governing regulations:

Standard Steel Doors and Frames:  DHI's "Recommended Locations for Architectural Hardware for Standard Steel Doors and Frames."

Install each door hardware item to comply with manufacturer's written instructions.  Where cutting and fitting are required to install door hardware onto or into surfaces that are later to be painted or finished in another way, coordinate removal, storage, and reinstallation of surface protective trim units with finishing work specified in Division 9 Sections.  Do not install surface-mounted items until finishes have been completed on substrates involved.

Set units level, plumb, and true to line and location.  Adjust and reinforce attachment substrates as necessary for proper installation and operation.

Drill and countersink units that are not factory prepared for anchorage fasteners.  Space fasteners and anchors according to industry standards.

Key Control System:  Place keys on markers and hooks in key control system cabinet, as determined by final keying schedule.

Delete paragraph below if electrified door hardware is not required.  Verify acceptable location for power supplies with authorities having jurisdiction.

Thresholds:  Set thresholds for exterior and acoustical doors in full bed of sealant complying with requirements specified in Division 7 Section "Joint Sealants."

FIELD QUALITY CONTROL

Delete this Article if not required.

Revise paragraph below if Contractor engages consultant.

Independent Architectural Hardware Consultant:  Owner will engage a qualified independent Architectural Hardware Consultant to perform inspections and to prepare inspection reports.

Independent Architectural Hardware Consultant will inspect door hardware and state in each report whether installed work complies with or deviates from requirements, including whether door hardware is properly installed and adjusted.

ADJUSTING

Initial Adjustment:  Adjust and check each operating item of door hardware and each door to ensure proper operation or function of every unit.  Replace units that cannot be adjusted to operate as intended.  Adjust door control devices to compensate for final operation of heating and ventilating equipment and to comply with referenced accessibility requirements.

Subparagraph below is from Americans with Disabilities Act Accessibility Guidelines.

Door Closers:  Adjust sweep period so that, from an open position of 70 degrees, the door will take at least 3 seconds to move to a point 3 inches (75 mm) from the latch, measured to the leading edge of the door.

Below will increase cost but is recommended as a good investment on substantial projects.

Six-Month Adjustment:  Approximately six months after date of Substantial Completion, Installer shall perform the following:

Examine and readjust each item of door hardware as necessary to ensure function of doors, door hardware, and electrified door hardware.

Consult with and instruct Owner's personnel on recommended maintenance procedures.

Replace door hardware items that have deteriorated or failed due to faulty design, materials, or installation of door hardware units.

CLEANING AND PROTECTION

Clean adjacent surfaces soiled by door hardware installation.

Clean operating items as necessary to restore proper function and finish.

Provide final protection and maintain conditions that ensure door hardware is without damage or deterioration at time of Substantial Completion.

DEMONSTRATION

Possibly delete this Article for small projects.

Engage a factory-authorized service representative to train Owner's maintenance personnel to adjust, operate, and maintain door hardware and door hardware finishes.

DOOR HARDWARE SCHEDULE

Delete this Article if a schedule is not required.

Coordinate door hardware in Door Hardware Schedule with materials specified in Part 2.

Develop schedule of sets to suit Project.  Do not duplicate requirements inserted in Part 2.  Remove brackets [] and boldfacing from Section Text selected, and remove <insert notes> after editing schedule.  Insert quantities where [#] is indicated.  Refer to a completed example in the Evaluations in Division 8 Section "Door Hardware" for an explanation of how to use schedules.

Revise item name and insert description where indicated to suit Project.

Hanging devices below include hinges, pivot hinges, floor closers, and sliding and folding door tracks and hangers.

Securing devices (inactive leaf) below include flush bolts, surface bolts, removable mullions, exit devices, dummy trim, two-point locks, cremone bolts, door position switches, electric strikes, and magnetic locks.

Securing devices (active leaf) below include locksets, latchsets, deadlocks, exit devices, two- or three-point locks, cylinders, electric strikes, door position switches, magnetic locks, electronic locking devices, and Dutch-door bolts.

Operating trim below includes door pulls, push plates, and push and pull bars.

Accessories for pairs of doors below include coordinators, removable mullions, and astragals.

Closing devices below include door closers, mounting brackets, and overhead stops and holders.

Protective trim units below include armor, kick, mop, and stretcher plates; and door edge protection.

Stops and holders below include floor stops and holders, wall stops and holders, and electromagnetic holders.

Accessories below include thresholds, weather stripping, door gasketing, and astragals.

Miscellaneous items below include door silencers, room numbers, room nameplates, door knockers, cardholders, letter box plates, and smoke- or fire-detection devices.

Miscellaneous items listed that should be added at end of Door Hardware Schedule include key control cabinets and software, electromechanical door hardware not otherwise listed (e.g., power supplies), Drawings, manuals, computers, printers, and wire.

The hardware sets listed below indicate the items of hardware required for each opening.  It is the bidders responsibility to accurately furnish the proper quantities, items, sizes, weights and functions as required by the plans and specifications.  If an opening has, through error, been omitted from the following hardware sets, it shall be the bidders responsibility to supply hardware of equivalent quality and quantity, as that which is specified for a comparable opening.

## HW1

Doors	07, 14

Exit Device (function A)

Pull

Closer (cush n stop)

Floor Stop

Door Bottom Sweep

Balance of hardware by aluminum door supplier.

## HW2

Doors	08

Exit Device (function U) with power supply

Pull

Closer (cush n stop)

Floor Stop

Door Bottom Sweep

Electrified Hinges.  Coordinate with access control card reader.

Balance of hardware by aluminum door supplier.

## HW3

Doors	11 & 12

Exit Devices (function I)

Offset Pulls

Closers (cush n stop)

Floor Stops

Door Bottom Sweeps

Balance of hardware by aluminum door supplier.

## HW4

Doors	12

Exit Device (function I)

Exit Device (function T) with power supply

Offset Pulls

Closers (cush n stop)

Floor Stops

Door Bottom Sweeps

Balance of hardware by aluminum door supplier.

## HW5

Doors	23

Continuous Gear Hinge

Exit Device (function U) with power supply

Closer

Kickplate

Threshold

Pull

Electrified Hinges.  Coordinate with access control card reader.

## HW6

Doors	10

Hinges

Lockset (function F)

Door Stop

Silencers

## HW7

Doors 	04, 05, 13, 20, 21, 22, 25, 26, 27, 30, 31, 32, 40, 41, 42, 50, 51, 52, 60, 61, 62

Hinges

Closer

Exit Device (function F)

Kickplate

Door Stop

Fire Seals

## HW8

Doors 	06

Hinges

Closers

Exit Devices (function F)

Magnetic Hold Opens

Kickplates

Door Stops

Fire Seals

## HW9

Doors	09

Hinges

Closer

Locksets (function D)

Door Stop

Fire Seals

## HW10

Doors	01, 02, 03, 15

Hinges

Closer

Lockset (function A)

Threshold

Weatherstripping

Door Bottom Sweep

Insert additional requirements and sequence of operation in schedule above for electrified door hardware if required.

END OF SECTION