PROP - 02163

ADDENDA ITEMS

January 24, 2005

ANDERSON STREET

- The phase line shown on Sheet C3 is for the owners use. Work is required on both sides of the link to blend in the grading and utilities.

- For building #3 extend the 2 ½ “ water line to the building and use it for domestic service. Delete the split of the 4” water at the building.

- For buildings 2 and 3, add tapping sleeve and gate valve for the 4” taps to the existing water main.

- Attached is an updated legend

- Add drip strip on the south side of Building 2 under the gas meter 15’ +/-.

CUMBERLAND AVENUE

- Replace the entire sidewalk towards Cumberland Avenue with brick sidewalk. The entire sidewalk will be disturbed when the shoring system is installed.