# SECTION 01050 – FIELD ENGINEERING

# PART I – GENERAL

  - RELATED DOCUMENTS

A.	Site drawings produced by Pinkham and Greer Consulting Engineers, foundation/basement plan drawings produced by TFH Architects PA and Structural Design Consulting, building drawings produced by TFH Architects, mechanical drawings produced by TFH Architects, electrical and lighting drawings produced by TFH Architects.  Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification Sections apply to all sections.

  - SUMMARY

- This Section specifies administrative and procedural requirements necessary for field-engineering services including, but not necessarily limited to, the following:

  - Land survey layout work.

- Related Sections:  The following Sections contain requirements that relate to this Section:

  - Division 1 Section “Coordination” for procedures for coordinating field engineering with other construction activities.

  - Division 1 Section “Submittals” for submitting Project record surveys.

  - Division 1 Section “Contract Closeout” for submitting final property survey with Project Record Documents and recording of Owner-accepted deviations from lines and levels.

  - SUBMITTALS

- Certificates:  Submit a certificate signed by the land surveyor or professional engineer certifying the location and elevation of improvements.

- Initial Property Survey of Existing Conditions:  To be provided by the Owner.

- Project Record Documents:  Submit a record of Work performed and record survey data as required under provisions of  “Submittals” and “Project Closeout” Sections.

  - QUALITY ASSURANCE

- Surveyor Qualifications:  Engage a land surveyor registered in the state where the Project is located, to perform required land-surveying services.

PART 2 – PRODUCTS 	(not applicable)

# PART 3 – EXECUTION

  - EXAMINATION

- Identification:  The Owner’s survey will identify existing control points and property line corner stakes.

- Verify layout information shown on the Drawings, in relation to the property survey and existing benchmarks, before proceeding to lay out the Work.  Locate and protect existing benchmarks and control points.  Preserve permanent reference points during construction.

  - Do not change or relocate benchmarks or control points without prior written approval.  Promptly report lost or destroyed reference points or requirements to relocate reference points because of necessary changes in grades or locations.

  - Promptly replace lost of destroyed Project control points.  Base replacements on the original survey control points.

- Establish and maintain a minimum of 2 permanent benchmarks on the site, referenced to data established by survey control points.

  - Record benchmark locations, with horizontal and vertical data, on Project Record Documents.

- Existing Utilities and Equipment:  The existence and location of underground and other utilities and construction indicated as existing are not guaranteed.  Before beginning site work, investigate and verify the existence and location of underground utilities and other construction.

  - Prior to construction, verify the location and invert elevation at points of connection of sanitary sewer, storm sewer and water-service piping.

  - PERFORMANCE

- Work from lines and levels established by the property survey.  Establish benchmarks and markers to set lines and levels at each story of construction and elsewhere as needed to locate each element of the Project.  Calculate and measure required dimensions within indicated or recognized tolerances.  Do not scale Drawings to determine dimensions.

  - Advise entities engaged in construction activities of marked lines and levels provided for their use.

  - As construction proceeds, check every major element for line, level and plumb.

- Surveyor’s Log:  Maintain a surveyor’s log of control and other survey work.  Make this log available for reference.

  - Record deviations from required lines and levels, and advise the Architect when deviations that exceed indicated or recognized tolerances are detected.  On Project Record Drawings, record deviations that are accepted and not corrected.

  - On completion of foundation walls, major site improvements and other work requiring field-engineering services, prepare a certified survey showing dimensions, locations, angles and elevations of construction and site work.

- Site Improvements:  Locate and lay out site improvements, including pavements, stakes for grading, fill and topsoil placement, utility slopes and invert elevations.

- Building Lines and Levels:  Locate and lay out batter boards for structures, building foundations, column grids and locations, floor levels and control lines and levels required for mechanical and electrical work.

- Exiting Utilities:  Furnish information necessary to adjust, move or relocate existing structures, utility poles, lines, services or other appurtenances located in or affected by construction.  Coordinate with local authorities having jurisdiction.

# END OF SECTION 01050