Copyright 1999, The American Institute of Architects (AIA)

# SECTION 06200 - FINISH CARPENTRY (INTERIOR)

This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

# PART 1 - GENERAL

1.1	RELATED DOCUMENTS

A.	Site drawings produced by Pinkham and Greer Consulting Engineers, foundation/basement plan drawings produced by TFH Architects PA and Structural Design Consulting, building drawings produced by TFH Architects, mechanical drawings produced by TFH Architects, electrical and lighting drawings produced by TFH Architects.  Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification Sections apply to all sections.

1.2	SUMMARY

A.	This Section includes the provision and installation of items provided by the General Contractor of the following:

Edit list below to suit Project and to distinguish finish carpentry from items made from wood but specified in other Division 6 Sections, such as "Paneling" or architectural woodwork Sections.

- Interior standing and running trim.

- Stair railing.

B.	Related Sections include the following:

List below only products, construction, and equipment that the reader might expect to find in this Section but are specified elsewhere.

Delete last option in first subparagraph below if structural wood is not exposed to view.

1.	Division 6 Section "Rough Carpentry" for furring, blocking, and other carpentry work not exposed to view.

2.	Division 6 Section "Interior Architectural Woodwork" for interior woodwork not specified in this Section.

3.	Division 7 Section "Vinyl Siding".

- Division 9 Section "Painting" for priming and backpriming of finish carpentry.

  - SUBMITTALS

A.      General:  Submit each item in this Article according to the Conditions of the Contract and

Division 1 Specification Sections if not provided under Division 13.

Delete paragraph and subparagraphs below if not required or supplement with list of products.

B.	Samples for Verification:

1.	For each species and cut of lumber and panel products with nonfactory-applied finish, with 1/2 of exposed surface finished, 50 sq. in. (300 sq. cm) for lumber and 8 by 10 inches (203 by 250 mm) for panels.

Insert specific model code organization below or revise if report must be from another source.

1.4	QUALITY ASSURANCE

A.	Installer Qualifications:  Engage an experienced Installer who has completed finish carpentry similar in material, design and extent to that indicated for this Project and with a record of successful in-service performance.

Delete below if no fire-retardant-treated materials or products are required.

1.5	DELIVERY, STORAGE, AND HANDLING

A.	Upon receipt continue to protect materials against weather and contact with damp or wet surfaces.  Stack lumber, plywood, and other panels.  Provide for air circulation within and around stacks and under temporary coverings.

Delete below if no interior work.

1.6	PROJECT CONDITIONS

A.	Environmental Limitations:  Do not deliver or install interior finish carpentry until building is enclosed and weatherproof, wet work in space is completed and nominally dry, and HVAC system is operating and maintaining temperature and relative humidity at occupancy levels during the remainder of the construction period.

Delete paragraph above if no interior work; below if no exterior work.

B.	Weather Limitations:  Proceed with installation only when existing and forecasted weather conditions permit work to be performed according to manufacturer's written instructions and warranty requirements and at least one coat of specified finish to be applied without exposure to rain, snow, or dampness.

# PART 2 - PRODUCTS

2.1	SOURCE

See Editing Instruction No. 1 in the Evaluations for cautions about naming manufacturers and products.

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Product Requirements."

A.	Local lumber supplier.

  - MATERIALS

Delete standards in this Article for materials not used.

A.	Lumber:  DOC PS 20 and applicable grading rules of inspection agencies certified by the American Lumber Standards' Committee Board of Review.

B.	Inspection agencies:  Inspection agencies, and the abbreviations used to reference them, include the following:

- NELMA – Northeastern Lumber Manufacturers Association.

- NHLA – National Hardwood Lumber Association.

- NLGA – National Lumber Grades Authority.

C.	Grade stamps:  Provide lumber with each piece factory marked with grade stamp of inspection agency evidencing compliance with grading rule requirements and identifying grading agency, grade, species, moisture content at time of surfacing, and mill.

D.	Softwood Plywood:  DOC PS 1, “U.S. Product Standard for Construction and Industrial Plywood.”

2.3 	FINISH CARPENTRY

A.    				Work includes:

Carpentry work which is exposed to view, is non-structural, and is not specified elsewhere.

Wood base:  ½” x 3 ½: base molding; clear pine or poplar; select from standard profiles.  Provide throughout including bathrooms where base is to be held up ¼” to receive caulking. Prime finish.  Back prime all wet locations.

B.   	Interior trim, typical: ½” x 2 ½” clear pine or poplar.  All surfaces to be primed and painted finish. Provide at window and door casings, wood window stools and aprons.

C.      Stair: Stairway; plywood composite treads; poplar risers, poplar or clear pine handrail.  All interior stairs to have closed stringers, all treads to be 1 1/4” plywood to receive finish flooring as shown on drawings.

D.		Base, casings, chair rails, mounting blocks:  clear pine or poplar.

2.4     	 INTERIOR ARCHITECTURAL WOODWORK

A.    	All cabinetry shall meet or exceed AWI and/or CSA standards.   Wood architectural cabinets; hardwood panels set in hardwood frames, wood face frame with plywood box. Drawer glides with roller bearings; Adjustable shelves; Solid drawer faces; natural finish; door & drawer pulls.  Cuisitel wood series style 101 (solid). Or approved equal.

B.       Kitchen Cabinets: see Section 12356.  Natural maple finish.

C.      Bathroom Vanity:  see Section 12345.  5/8” Melamine construction on moisture resistant particle board, color by Architect.

D.      Shelving: Vinyl coated steel wire shelving (white) or white painted wood #2 pine or Melamine covered with particle board core.  Provide and install except where access to utility chase is required.

E.      Countertop: post formed plastic laminate with integrated 4” backsplash.  Provide in kitchen and bathrooms.

F.	Furnish stair hand rails 1-1/2” round hardwood with supports at 48” o.c. and 12” horizontal returns at each end unless otherwise indicated on drawings

# 2.5	STAIRS AND RAILINGS

A.	Interior Stairs:

- Treads: ¾” plywood .

2.		Risers:    ¾” plywood.

Select subparagraph above for clear finished risers; subparagraph below for painted risers.

Revise subparagraph below if clear finished trim is used.

# 2.6	MISCELLANEOUS MATERIALS

Delete materials not required.

A.	Fasteners for Interior Finish Carpentry:  Nails, screws, and other anchoring devices of type, size, material, and finish required for application indicated to provide secure attachment, concealed where possible.

Delete subparagraph below if not required.

1.	Where finish carpentry materials are exposed in areas of high humidity, provide fasteners and anchorages with hot-dip galvanized coating complying with ASTM A 153/A 153M.

B.	Sealants:  Comply with requirements in Division 7 Section "Joint Sealants" for materials required for sealing siding work.

# 2.7	FABRICATION

Add specific values for moisture content if available and required for Project.  Obtaining material with moisture content below the regularly available industry standards is difficult.

A.	Wood Moisture Content:  Comply with requirements of specified inspection agencies and with manufacturer's written recommendations for moisture content of finish carpentry at relative humidity conditions existing during time of fabrication and in installation areas.

# PART 3 - EXECUTION

# 3.1	EXAMINATION

A.	Examine substrates, with Installer present, for compliance with requirements for installation tolerances and other conditions affecting performance.  Proceed with installation only after unsatisfactory conditions have been corrected.

# 3.2	PREPARATION

A.	Clean substrates of projections and substances detrimental to application.

B.	Before installing finish carpentry, condition materials to average prevailing humidity in installation areas for a minimum of 24 hours, unless longer conditioning is recommended by manufacturer.

Delete below if no painted exterior lumber.  Revise to include interior work in high-humidity areas if required.

C.	Prime lumber all surfaces for exterior applications to be painted, including both faces and edges.  Cut to required lengths and prime ends.  Comply with requirements in Division 9 Section "Painting."

# 3.3	INSTALLATION, GENERAL

# A.	Do not use materials that are unsound, warped, improperly treated or finished, inadequately seasoned, or too small to fabricate with proper jointing arrangements.

Delete subparagraph below if no manufactured units.

# B.	Install finish carpentry level, plumb, true, and aligned with adjacent materials.  Use concealed shims where necessary for alignment.

1.	Scribe and cut finish carpentry to fit adjoining work.  Refinish and seal cuts as recommended by manufacturer.

2.	Countersink fasteners, fill surface flush, and sand where face fastening is unavoidable.

Revise tolerances in first subparagraph below to suit Project.

3.		Install to tolerance of 1/8 inch in 96 inches (3 mm in 2438 mm) for level and plumb.  Install adjoining finish carpentry with 1/32-inch (0.8-mm) maximum offset for flush installation and 1/16-inch (1.5-mm) maximum offset for reveal installation.

Subparagraph below, based on NFPA 101 requirements, is an example only.  Revise if more stringent tolerances are required.  Coordinate with framing requirements for stairs in Division 6 "Rough Carpentry" Section.

4.		Coordinate finish carpentry with materials and systems in or adjacent to it.  Provide cutouts for 5/4 wood mounting blocks to accommodate mechanical and electrical items that penetrate siding.  Blocks to align with clapboard coursing with a width suitable to accommodate the mouting of the fixture or device. Wrap blocking with .032” thick aluminum.

# 3.4	STANDING AND RUNNING TRIM INSTALLATION

A.	Do not install any trim that has not been thoroughly primed on all sides.  Install with minimum number of joints practical, using full-length pieces from maximum lengths of lumber available.  Do not use pieces less than 24 inches (610 mm) long, except where necessary.  Stagger joints in adjacent and related standing and running trim. Plane backs of casings to provide uniform thickness across joints, where necessary for alignment. Wrap all exposed trim with .032” thick aluminum

# 3.5	STAIR AND RAILING INSTALLATION

Descriptive requirements below only cover basic stair and railing installation; for best results, supplement with complete details.

A.	Internal treads and risers to be completed in factory installation to th extent possible:  Secure treads and risers by gluing and nailing to rough carriages.  Secure treads and risers to wall stringers, glue and nail into place.

B.	Railings:  Secure wall rails with galvanized steel brackets on 5/4 x 3” x 8” mounting blocks.  Fasten freestanding railings to newel posts and to trim at walls with countersunk-head stainless steel screws.  Flash as required.

# 3.6	ADJUSTING

A.	Replace finish carpentry that is damaged or does not comply with requirements.  Finish carpentry may be repaired or refinished if work complies with requirements and shows no evidence of repair or refinishing.  Adjust joinery for uniform appearance.

# 3.7	CLEANING

A.	Clean finish carpentry on exposed and semi exposed surfaces.

# 3.8	PROTECTION

A.	Provide final protection and maintain conditions that ensure finish carpentry is without damage or deterioration at the time of Substantial Completion.

# END OF SECTION 06200