Copyright 1996 , The American Institute of Architects (AIA)

# SECTION 07460 - SIDING

This Section uses the term Architect.  Change this term as necessary to match the actual term used to identify the design professional as defined in the General and Supplementary Conditions.

# PART 1 - GENERAL

# 1.1	RELATED DOCUMENTS

A.	Site drawings produced by Pinkham and Greer Consulting Engineers, foundation/basement plan drawings produced by TFH Architects PA and Structural Design Consulting, building drawings produced by TFH Architects, mechanical drawings produced by TFH Architects, electrical and lighting drawings produced by TFH Architects.  Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification Sections apply to all sections.

# 1.2	SUMMARY

A.	This Section includes delivery, storage, installation of vinyl siding, trim and soffits.

Adjust list below to suit Project.

1.	Vinyl siding.

- Vinyl soffit.

- Miscellaneous clips, moldings and flashings.

B.	Related Sections include the following:

List below only products, construction, and equipment for this Project that the reader might expect to find in this Section but are specified elsewhere.  Verify that Section titles listed below are correct for this Project's Specifications because Section titles may have changed since this Section was updated.

1.	Division 6 Section "Rough Carpentry" for sheathing and air-infiltration barrier.

2.	Division 6 Section "Finish Carpentry" for exterior wood trim.

3.	Division 7 Section "Sheet Metal Flashing and Trim" for flashing, gutters, and other sheet metal work.

4.	Division 7 Section "Joint Sealants" for field-applied sealants.

# 1.3	SUBMITTALS

A.	Provide product data for each type of product specified.  Include identification of materials; dimensions of individual components; installation instructions; and available profiles, textures, and colors.

B.	Provide samples for Initial Selection:  Manufacturer's sample finishes showing the full range of colors, profiles, and textures available.

Delete above if colors and other characteristics are preselected and specified or scheduled.  Retain below with or without above.

C.	Samples for Verification:  Provide full-size units of each type of siding and trim indicated; in sets for each color, texture, and pattern specified

# 1.	12-inch- (300-mm-) long-by-actual-width sample of siding.

Select subparagraph above or below.

Insert specific model code organization below or revise if report must be taken from another source.

# 1.4	QUALITY ASSURANCE

A.	Installer Qualifications:  Engage an experienced installer who has completed siding installations similar in material, design, and extent to that indicated for Project that has resulted in construction with a record of successful in-service performance.

# 1.5	DELIVERY, STORAGE, AND HANDLING

A.	Store materials in a dry, well-ventilated, weather tight place.  Comply with manufacturer's written instructions for storage, handling, and protection.

# 1.6	PROJECT CONDITIONS

A.	Weather Limitations:  Proceed with siding installation only if existing and forecasted weather conditions permit siding to be installed according to manufacturer's written instructions and if substrate is completely dry.

# 1.7	WARRANTY

When warranties are required, verify with the Owner's counsel that special warranties stated in this Article are not less than remedies available to the Owner under prevailing local laws.  Coordinate with Division 1 Section "Warranties."

A.	General Warranty:  The special warranty specified in this Article shall not deprive the Owner of other rights the Owner may have under other provisions of the Contract Documents and shall be in addition to, and run concurrent with, other warranties made by the Contractor under requirements of the Contract Documents.

B.	Special Project Warranty:  Submit a written warranty, executed by siding manufacturer, agreeing to repair or replace siding that fails in materials or workmanship within the specified warranty period.  Failures include, but are not limited to, cracking, deforming, fading, or otherwise deteriorating beyond normal weathering.  Fading is defined as loss of color, after cleaning with product recommended by manufacturer, of more than 4 color-difference units as measured according to ASTM D 2244.

Below is an example only.  Revise warranty to period required and verify availability with warrantor.

1.	Warranty Period:  20 years from date of Substantial Completion.

# 1.8	ADDITIONAL MATERIALS

Extra materials may not be allowed for publicly funded projects.

A.	Furnish additional materials described below that match products installed, are packaged with protective covering for storage, and are identified with labels describing contents.

Revise below as required.  Replace percentage with a specific number of units and replace unit with an expanded description of each unit.

1.	G.C. to provide sufficient quantity to complete the project and furnish full lengths of siding in a quantity equal to 2 percent of amount installed.

# PART 2 - PRODUCTS

# 2.1	MANUFACTURERS

# A.	Available Manufacturers:  Subject to compliance with requirements, manufacturers offering products that may be incorporated into the Work include, but are not limited to, the following:

Retain above for nonproprietary or below for semiproprietary Specification.  Refer to Division 1 Section "Materials and Equipment."

# B.	Manufacturers:  Subject to compliance with requirements, provide products by one of the following:

See Editing Instruction No. 1 in the Evaluations for cautions about naming products and manufacturers.

1.	Vinyl Siding:  CertainTeed Corp.; Vinyl Building Products Group (monogram) series or equal by:

a.	Bird Vinyl Products.

b.	CertainTeed Corp.; Vinyl Building Products Group.

c.	Crane Plastics.

d.	Gentek Building Products.

e.	Georgia-Pacific Corp.

f.	Heartland Building Products.

g.	Royal Building Products.

- Wolverine Technologies, Inc.

- Alcoa Home Exteriors, Inc.

# 2.2	SIDING

Because of the variety of types and appearances available, selecting specific products is recommended.  Modify this Article to specify actual siding selected.  Pattern selections are the most commonly available types; other styles are also available.

A.	Formed Vinyl Siding:  Solid vinyl siding and accessories complying with ASTM D 3679.

Select 1 or more of 15 subparagraphs below or revise.

- Horizontal Pattern:  8-inch (203-mm) exposure in double 4-inch (101-mm) style.

- Maintain a minimum of .044 thickness.

- Smooth brush finish (not wood grain).

- Full ¾” clapboard base.

# 2.3	SOFFIT

A.	Vinyl Soffit:  Solid vinyl soffit and accessories complying with ASTM D 4477.

Select 1 of 6 subparagraphs below or revise.

1.	Pattern:  10 hidden vent triple 3-1/3” profile in matte finish.  ‘Ventura’ line by Alcoa.

# 2.4	ACCESSORIES

A.	Siding Accessories:  Provide starter strips, edge trim, window head flashing, corner cap, and other items as recommended by manufacturer for building configuration; match type of siding.

B.	Fasteners:  Non-corrosive siding nails, in sufficient length to penetrate a minimum of 1 inch (25 mm) into substrate.  Provide pre-finished fasteners in color to match siding where face nailing is unavoidable.

# 2.5	COLORS AND TEXTURES

A.	Where manufacturer's standard products are indicated, provide siding and accessories complying with the following requirements (minimum of 16 color choices):

Retain one requirement below.  If retaining second requirement, indicate colors and textures on a separate schedule.

1.	Provide Architect's selections from manufacturer's full range of colors and textures for siding and accessories of type indicated.  Accessories may be required to match siding or to be of a different color or texture as selected by Architect.

# PART 3 - EXECUTION

# 3.1	EXAMINATION

A.	Examine substrates for compliance with requirements for substrates, installation tolerances, and other conditions affecting performance of siding.  Do not proceed with installation until unsatisfactory conditions have been corrected.

# 3.2	PREPARATION

A.	Clean substrates of projections and substances detrimental to application.

B.	Coordinate installation with flashings and other adjoining construction to ensure proper sequencing.

# 3.3	INSTALLATION

A.	General:  Comply with siding manufacturer's written installation instructions applicable to products and applications indicated, unless more stringent requirements apply.  Center nails in elongated nailing slots without binding siding to allow for thermal movement.  Overlap joints to shed water away from direction of prevailing wind.

B.	Install vinyl siding, soffit, and accessories according to ASTM D 4756.

Siding below is available from wolverine technologies.

1.	Install siding in continuous lengths with minimum number of seams.

# 3.4	ADJUSTING AND CLEANING

A.	Remove and replace damaged, improperly installed, or otherwise defective siding materials with new materials complying with specified requirements.

B.	Clean finished surfaces according to siding manufacturer's written instructions and maintain in a clean condition during construction.

# END OF SECTION 07460