Code references are NFPA 2006 edition

Fire Alarm system required

101-31.3.4.1.1    Apartment buildings with more than three stories or with more than 11 dwelling units, other than those meeting 31.3.4.1.2 or 31.3.4.1.3, shall be provided with a fire alarm system in accordance with Section 9.6, except as modified by 31.3.4.2 through 31.3.4.5.2.

Fire door assemblies required

8.3.4.2*   The fire protection rating for opening protectives in fire barriers, fire-rated smoke barriers, and fire-rated smoke partitions shall be in accordance with Table 8.3.4.2.

Fire doors to be self-closing

8.3.3.3    Unless otherwise specified, fire doors shall be self-closing or automatic-closing in accordance with 7.2.1.8.

101-31.2.9 Emergency Lighting.   Emergency lighting in accordance with Section 7.9 shall be provided in all buildings with more than 12 dwelling units, or of more than 3 stories in height, unless every dwelling unit has a direct exit to the outside of the building at grade level.

Smoke alarms required

101-31.3.4.5.1    In buildings other than those equipped throughout with an existing, complete automatic smoke detection system, approved single-station smoke alarms shall be installed in accordance with 9.6.2.9, as modified by 31.3.4.5.2, outside every sleeping area in the immediate vicinity of the bedrooms and on all levels of the dwelling unit, including basements.

Smoke alarms to be maintained

4.6.12.1    Whenever or wherever any device, equipment, system, condition, arrangement, level of protection, fire-resistive construction, or any other feature is required for compliance with the provisions of this Code, such device, equipment, system, condition, arrangement, level of protection, fire-resistive construction, or other feature shall thereafter be continuously maintained in accordance with applicable NFPA requirements or requirements developed as part of a performance-based design, or as directed by the authority having jurisdiction.

Street numbers required

1-10.12.1.1*   New and existing buildings shall have approved address numbers placed in a position to be plainly legible and visible from the street or road fronting the property.

Boiler protection required

101-31.3.2.1.1    The areas described in Table 31.3.2.1.1 shall be protected as indicated.