# SECTION 07421

CONCEALED FASTENER METAL WALL pANEL SYSTEM

# PART 1 – GENERAL

# 1.1	Related documents

A.	The drawings and provisions of the General Conditions, Supplementary Conditions and the sections included under Division 1 Specification Sections, apply to this section.

# 1.2	SUMMARY

A.	This section includes concealed fastener profiled wall panels to be used as exterior and/or interior wall cladding.  Includes all associated flashings, foam closures, formed aluminum trim, extruded aluminum trim, subgirts, sealants and fasteners as required to complete the installation of the panel system.

# 1.3	Performance REQUIREMENTS

A.	Structural performance: provide exterior/interior wall cladding assemblies capable of withstanding the effects of load and stresses from dead loads, wind loads, snow loads and normal thermal movement without evidence of permanent defects of assemblies or components.

- Dead load: As required by applicable building code.

- Live Load: As required by applicable building code.

- Wind Load: Uniform pressure (velocity pressure) of (Insert Design Criteria) lb/sq ft. (Insert Design Criteria), acting inward or outward.

- Thermal Movements: Provide assemblies that allow for thermal movements resulting from the following maximum changes (range) in ambient and surface temperatures by preventing buckling, opening of joints, overstressing of components and other detrimental effects:

  - Temperature Change (range): 120 deg F (67 deg C), ambient; 180 deg F (100 deg C), material surfaces.

- This system wall panel system, as specified by 2006 International Building Code – 1403.2, must an air and water resistant barrier.  The design of the air and water resistant barrier shall be completed by a qualified air and water membrane specialist.*

- Sealed joints shall allow free and silent movement of panels during expansion and contraction while preventing uncontrolled penetration of moisture.

- Manufacturing and installation shall prevent deformation of exposed surfaces.

D.	Design panel system to accommodate substructure tolerance of +0 to -1/8 inch.

- Not Permitted: Vibration harmonics; wind whistles; noises caused by thermal movement; thermal movement transmitted to other building elements; loosening, weakening or fracturing of attachments or components of system.

- Structural Performance / Uniform Load Deflection Test:  Provide panel system which has been tested in accordance with ASTM E330 at a design pressure of at least 60 psf without deformation or failures of structural members.  Maximum allowable deflection of span: L/180.

- Panels shall be tested in accordance with ASTM E1592 structural testing at load span of at least 5’-0” o.c. and shall perform at a design pressure of pressure of no less than 35 psf without deformation or failures of structural members.

- Air Infiltration: Panel system shall not have air infiltration rate more than 0.06 cfm per sq. ft. of fixed wall area when tested in accordance with ASTM E283 at static air pressure differential of 6.24 psf.

- Static Water Penetration: Panel system shall have no water penetration as defined by in test method when tested in accordance with ASTM E331.  The ASTM E331 test shall be conducted at inward static pressure differential of not less than 15.0 psf.

- Dynamic Water Penetration: Panel system shall have been tested in accordance with AAMA 501 and shall have passed with no uncontrolled water leakage at 15.00 psf dynamic pressure differential, with water application rate of 5 gallons/hr/sqft.

  - Common wall system construction for this product consists of wall panels installed over a layer of DensGlass® Gold substrate by G-P Gypsum, with a layer of Tyvek® Commercial Wrap® by DuPont Company.  Assemblies using alternate materials are possible dependent on building type and location.

# 1.4	SUBMITTALS

- Product Data:  Manufacturer's product literature for the concealed fastener profiled wall panel system as specified.

- Shop Drawings:  For exterior/interior concealed fastener profiled panels and accessories.  Include plans; elevations; sections and details.

- Quality Assurance Submittals:  Submit the following:

- Certificates:  Product certificates signed by manufacturer certifying materials comply with the specified performance characteristics and criteria, and physical requirements.

- Samples for initial selections:  Manufacturer’s color charts showing the full range of colors available for units with factory-applied color finishes.

- Samples for verification:  Provide color samples of selected color.  Samples shall involve normal color and texture variations, include sample sets showing the full range of variations expected.

- Affidavit certifying that the material meets the requirements specified.

# 1.5	QUALITY ASSURANCE

- Professional Engineer Qualifications: A professional engineer who is legally qualified to practice in the jurisdiction where the project is located and who is experienced in providing engineering services of kind indicated.

- Manufacturer Qualifications:  Minimum of 5 years experience in manufacturing roll formed wall panel systems similar to those specified.

- Installer Qualifications:  Acceptable to manufacturer.

# 1.6	delivery, storage & handling

- General:  Comply with Division 1 Product Requirements Sections.

- Ordering:  Comply with manufacturer’s ordering instructions, and lead-time requirements to avoid construction delays.

- Delivery:  Deliver materials in manufacturer’s original, unopened, undamaged containers with identification labels intact.

- Store materials in accordance with manufacturer’s recommendations.

- Handle materials carefully to avoid damage to materials and finishes.

# 1.7	Project conditions

- Field Measurements:  Verify actual supporting and adjoining construction by field measurements before fabrication, and indicate recorded measurements on final shop drawings.  Coordinate construction to ensure that panels fit properly to supporting and adjoining construction and coordinate schedule with construction progress to avoid delaying the work.

- Established dimensions:  Where field measurements can not be made without delaying the work, guarantee dimensions and proceed with fabrication of panels corresponding to the established dimensions.

# 1.8	WARRANTY

- Project warranty refers to Conditions of the Contract for project warranty provisions.  Manufacturer’s warranty: submit, for Owner’s acceptance, manufacturer’s standard warranty documents executed by authorized company official.  Manufacturer’s warranty is in addition to, and not a limitation of, other rights owner may have under Contract Documents.

- The Contractor shall warrant the materials to be free of faults and defects in accordance with the General Conditions, except that the warranty shall be extended by paint manufacturer's standard multi-year warranty.  The warranty shall be in writing and shall be signed by the manufacturer.

## Materials Manufacturers: Repair or replace defective materials for a period of two (2) years.

- Panel System Installer: Repair or replace products or components which fail due to faulty workmanship for a period of two (2) years.

## Coil Anodized Finish: Coatings Manufacturer and applicator to warrant coil anodized finish for a period of twenty (20) years after the Effective Date, the factory applied finish applied by the applicator.

- No visible peeling or cracking for a period of twenty years.  This excludes any cracking due to brake bends or other forming operations performed on components after the anodized finish has been applied.

- No chalking for a period of twenty years.  This only applies to any powdery residue formed by the breakdown of the anodized finish.  It does not apply to any foreign residue deposited on the surface of the anodized finish by the surrounding atmosphere (soot, dust, etc.).

- No significant visible fading for a period of twenty years.

# PART 2 – PRODUCTS

# CONCEALED FASTENER PROFILED WALL PANELS

- General:  Provide factory-formed metal wall panels designed to be field assembled and mechanically attaching panels to supports using concealed fasteners in interlocking side laps.  Include accessories required for weathertight installation.

# 2.2	MANUFACTURER

- Manufacturers: Subject to compliance with requirements, provide products manufactured by:

- Firestone Building Products, 1001 Lund Blvd., Anoka, MN 55330

Phone 800-426-7737, Fax 763-576-9596, www.firestonebpco.com

  - Delta Series concealed fastener wall panels.

  - Alternate systems by other manufacturers/fabricators are to be submitted to the architect not less than 7 working days prior to bid.

# 2.3	Materials

- Panel system shall be Delta Series panels manufactured by Firestone Metal Products.

- Delta Series panel profile(s) shall be CFP-16TP.  As defined on the contact documents.

  - Panels shall be 7/8 inches in depth and coverage shall be 16 inches.

  - The panels shall have an interlocking side lap feature which conceals the fasteners and is installed using clips to allow for thermal movement.  Clips shall be designed to hold the panel ½” minimum from exterior sheathing to create a drainage plane and ventilation cavity.  Load span tables must include evaluation of clip and side joint interaction.

  - The panels shall have factory applied sealant concealed within the interlocking joint.

  - Panels shall have common interlocking side joints to allow for multiple panel profile combinations.

  - Exposed panel fasteners are unacceptable.

- Aluminum Face Sheet: ASTM B209, Aluminum Association specification sheet 3003-H14/3105-H14 for painted finish, 5005-H34 for anodized finish].

- Thickness:  0.040 inch.

- Texture: Panels shall be [smooth][non-directions stucco embossed]

- Copper Panels:  Architectural Grade Sheet, ASTM B370

- Thickness:  20 ounce.

# 2.4	Fabrication

- Tolerances

- Form panels in longest practical lengths, true to shape, accurate in size, square, and free from distribution or manufacturing defects.

- Bend lines, breaks, and angles shall be sharp and true, and surfaces shall be free from warp or buckle.

- Material surfaces shall be free of scratches or marks caused during fabrication.

- Panel shearing length to be: +/- 1/16”.

- Ensure that entire project is manufactured from single color coil paint run to ensure color uniformity.

- Provide factory applied strippable plastic film for protection during fabrication and installation.

# 2.5	Accessories

- All fasteners shall be non-corrosive type, as recommended by the panel manufacturer.  Provide self-tapping screws and other suitable fasteners designed to withstand building design loads.

- Provide panel clips designed to engage into panel flange, providing for a minimum ½” drainage plane and ventilation cavity.

- Weather Resistant Membrane:  Use of air and water barrier is required with wall panel system, as specified in section [insert specification section].

- Flashing: Unless noted otherwise, shall be same material and gauge as for panel where exposed.

- Fasteners shall be minimum #14 diameter, self-tapping, with hex head.

  - Fasteners to be either cadmium plated carbon steel or series 300 stainless steel with bonded neoprene washers.

  - Fastener type, size and spacing to be engineered according to specific project conditions.

- Panel Sealants:

- Hidden Sealant Tape:  Pressure-sensitive, gray isobutylene compound sealant tape with release-paper backing.  Provide permanently elastic, non-sag, non-toxic, non-staining tape 1/8” (3mm) thick and 1” (25mm) wide.

- Hidden Joint Sealant:  ASTM C90; elastomeric polyurethane, polysulfide, or silicone sealant; of type, grade, class, and use classifications required to seal joints in metal wall panels and remain weathertight; and as recommended in writing by metal wall panel manufacture.

- Non-Skinning Butyl Sealant:  ASTM C734 Non-hardening, non-drying, non-oxidizing butyl rubber-based sealant.

- Accessory Attachment Tape: Pressure-sensitive 1/8” (3mm) thick and 1” (25mm) wide VHB tape.

- Subgrits: Provide G90 galvanized steel of gauge and spacing required for panel structural requirements, as recommended by the panel manufacturer and in accordance with approved shop drawings.  To avoid galvanic reaction, separate dissimilar metals.

- Foam Closure Strips:  Closed-cell, expanded, cellular, rubber or cross-linked, polyolefin-foam or closed-cell laminated polyethylene; minimum 1 inch (25mm) thick, flexible closure strips; cut or pre-molded to match metal wall panel profile.  Provide closure strips where indicated or necessary to ensure weathertight construction.

- Metal Closure Strips:  Unless noted otherwise, shall be same material and gauge as for panel.

# 2.6	Finishes, general

- Comply with NAAMM’s Metal Finishes Manual for architectural metal products for recommendations for applying and designating finishes.

# 2.7	Finishes

- Class I, Clear Anodic Finish: AA-M12C22A41 (Mechanical finish: nonspecular as fabricated; Chemical Finish: etched, medium matte; Anodic Coating: Architectural   Class I, clear coating 0.018 mm or thicker) complying with AAMA 607.1.

- Class I, Color Anodic Finish: AA-M12C22A42/A44 (Mechanical finish: nonspecular as fabricated; Chemical Finish: etched, medium matte; Anodic Coating: Architectural Class I integrally colored or electrolytically deposited color coating 0.018 mm (or thicker) complying with AAMA 606.1 or AAMA 608.1.

- Color:  Selected by Architect/Engineer from manufacturer’s standard colors.

- Color: Match Architect’s sample.

# PART 3 – EXECUTION

# 3.1	preparation

- Coordinate setting drawings, diagrams, templates, instructions, and directions for installation.  Panel substructure shall be level and plumb.  Coordinate delivery of such items to project site.

# 3.2 	INSTALLATION

- General:  Install meal wall panels according to manufacture’s written instructions in orientation, sizes and locations indicated on drawings.

- Erect panel level and plumb, in proper alignment in relation to substructure framing and established lines; follow SMACNA Architectural Sheet Metal manual and standard practices.

- Panels shall be erected in accordance with approved shop drawings.

- Panel anchorage shall be structurally sound and per engineering recommendations.

- Where aluminum materials come in contact with dissimilar materials, an isolation shim or tape shall be installed at fastening locations.

- Install weather resistant membrane in accordance with manufacturer's instructions.

- Completed system shall be free from over bending, deforming, stretching, distortion, waves, and buckles.

- Install gaskets, joint fillers and sealants where indicated and where required for weathertight performance of metal wall panel assemblies.  Provide types of gaskets, fillers and sealants indicated or if not indicated, types as recommended by metal wall panels manufacture.

- Seal side joints where recommended by metal wall panel manufacture.

- Prepare joints and apply sealants to comply with the requirements in Division07 Section “Joint Sealants”.

# 3.3 	cleaning and protecting

- Clean exposed surfaces of panels that are not protected by temporary covering to remove fingerprints and soil during construction period.

- Clean exposed surfaces with water and a mild soap or detergent not harmful to finishes.  Thoroughly rinse surfaces and dry.

- Protect panels from damage during construction.  Use temporary protective coverings where needed as approved by the panel manufacturer.

- Clean and touch up minor abrasions in finish with air-dried coating that matches color and gloss, and is compatible with, factory–applied finish coating.

- Remove panels damaged beyond repair and replace with new panels to match adjacent undamaged panels.

- Remove protective film immediately after installation.

# END OF SECTION