SECTION 09643

HARDWOOD FLOORING

1.01 SECTION INCLUDES

A. Engineered Wood Flooring

B. Maintenance materials.

C. Finish moldings

1.02 RELATED SECTIONS

A. Section: 03 10 00 - Concrete Forming

B. Section: 03 30 00 - Cast-in-place Concrete

C. Section: 06 10 00 - Rough Carpentry

1.03 REFERENCES

A. ASTM E84 - Test Method for Surface Burning Characteristics of Building Materials.

B. ASTM F1869 - Standard Test Method for Measuring Moisture Vapor Emission Rate of

Concrete Subfloor Using Anhydrous Calcium Chloride.

C. ASTM F710 - Practice for Preparing Concrete Floors. Concrete ph determination.

1.04 SUBMITTALS

A. Submit product data in accordance with Section (01 30 00) (01 33 00), including

manufacturer’s installation and maintenance instructions.

B. Submit three representative samples of the engineered hardwood flooring in the final color(s) or custom color(s), and species if desired as selected by the owner or their representative.

C. Installer Certification: Submit a list of at least three installations successfully completed within the past year requiring the same general degree of installation expertise.

D. Shop Drawings: Show floor pattern layout. Provide locations of any transition

moldings needed to satisfy the manufacturers recommended installation on long runs of

product to provide for expansion and contraction for approval.

1.05 QUALITY ASSURANCE

A. Installer: Shall be experienced in the wood and/or vinyl tile flooring industry and shall

have a minimum of five (5) years experience in the installation of similar products.

2.01 PRODUCTS

A. Options will be provided to owner as follows:

Tier 1 (6 units)

203, 204, 205, 303, 304 and 305

Owners to select from the following Porcelanosa wood floor options: Tortona Fiera, Fonte and Strada

Tier 2 (16 Units)

201, 202, 206, 301, 302, 306, 401, 402, 403, 404, 406, 501, 502, 503, 504

506

Owners to select from the following Porcelanosa wood floor options:  Tortona Walnut, Mini Eden White, Sand and Wenge

Tier 3 (2 Units)

601, 602

Product TBD -Provide allowance for installation and carry $10 per square foot

material cost

B. 	Solid Wood stair treads to match species and finish of wood floors to be provided at

all stairs inside the units, provide finish sample for approval before  fabrication.

3.0 INSTALLATION

Install floors in accordance with manufacturer’s recommendation.

Confirm that moisture content of concrete slab is within manufacturers recommended levels before installing flooring

3.04 PROTECTION

A. Protect finished floor from abuse by other trades using heavy Kraft paper or equivalent. Keep traffic out of spaces and areas where flooring is being installed until adhesive has set. Light foot traffic after 10-12 hours. Normal traffic after 24 hours.

3.05 CLEANING  AND MAINTENANCE

A. Prior to turning the floor over to the owner, it shall be thoroughly cleaned by sweeping, vacuuming or dust mopping to remove debris.

END OF SECTION