SECTION 09680

CARPET

1. 	GENERAL

1.1	REFERENCES:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

  - DESCRIPTION OF WORK:

- Installation of “Roberts Strips” for carpeting.

- Installation of Carpeting as shown on plans or noted in these Specifications.

1.3	QUALITY ASSURANCE

A.	Finished installation shall comply with fire test specified in applicable Building Code.

B.	Architect/Engineer shall review first finished space for workmanship.  Accepted space shall 				serve as project standard.

C.	All carpets will meet UM44De

D.	Carpet to meet CRI Low Emission Label Standard.

1.4 	SUBMITTALS

A.	Submittals under this Section shall include:

1.	Manufacturer's specifications and installation instructions on all specified products.

2. 	Samples:  one piece, 18" x 18", of each color and type of carpet provided.

B.	Deliver to Owner, neatly packaged and labeled, all usable carpet scraps over 2 sq. ft. or 8 in. 			in least dimensions: 1 percent of each type and color of carpet provided, in 12 ft. wide rolls; 			and 1 percent of each type of edge strip provided, in standard lengths.

C.  	Provide written maintenance program.

2. 	PRODUCTS

2.1 	CARPET shall be as follows:

- Corridors:  Carpet tile TBD carry installation and  $38/yard material allowance

- Stairwells:  Broadloom Carpet TBD carry installation and $32/yard material allowance

- Lounge:  Carpet tile TBD carry installation and  $38/yard material allowance

- In Units as indicated on plan. Provide 28oz 3/8” hair and jute pad

1	Options will be provided to owner as follows:

Tier 1 (6 units)

203, 204, 205, 303, 304 and 305

Owners to select from the following: Durkan Mona Vista MH329 color 731 Surfside, 711 Baja and 948 Basin.

Tier 2 (16 Units)

201, 202, 206, 301, 302, 306, 401, 402, 403, 404, 406, 501, 502, 503, 504

506

Owners to select from the full colorline of Durkan Mono Vista MH329

Tier 3 (2 Units)

601, 602

Product TBD -Provide allowance for installation and carry $42 per square yard material cost

2.2 	CARPET must carry stamp confirming conformance to above and submitted to Architect for approval.

  - Volatile Organic Compound (VOC) emissions from adhesives and sealants must not exceed VOC limits of South Coast Air Quality Management District Rule #1168 AND sealants used as fillers must meet the requirements of the Bay Area. Air Quality Management District Regulation 8, Rule 51

3.  	EXECUTION:

3.1 	JOB CONDITIONS:

A.	Examine Subfloor for dampness, loose material, excessive irregularity, oily or waxy areas impeding adhesion, or other conditions which would prevent proper installation.  Verify that no incompatible curing compound has been used on newly-poured concrete.  	Commencement of work constitutes acceptance of subfloor.

B. 	Allow newly-poured concrete to cure as long as possible before installation of carpet, a minimum of 7 days, 28 days preferable.  Perform bond and moisture tests in accordance with carpet manufacturer's instructions, to verify that concrete is sufficiently cured, dried and then sealed.

C.	Broom-clean or vacuum surfaces to receive carpet, before beginning installation.  Apply primer-sealer to plywood or concrete sub-floor, if recommended by carpet or adhesive 	manufacturer.

D. 	Before proceeding with complete installation of carpet, install a representative sample area 			of each type of carpet provided over each type of substrate, to test for compatibility of 				adhesive to substrate at glue-down installation, and verify general appearance of finished 				installation.  If sample is securely bonded after 72 hours, final installation may proceed.

3.2  	INSTALLATION

A. 	Install carpet by direct glue-down in public areas, carpet in units to be installed over pad

B. 	Field measure each space to receive carpet.  Do not scale drawings.  Before beginning 					installation, verify that floor telephone and electrical outlets have been installed.

C.	At glue-down installations, apply manufacturer's recommended adhesive in accordance with 			manufacturer's instructions, observing proper safety precautions.  Apply adhesive in a 					uniform film with a steel trowel and proper size notches for correct coverage.  Avoid 					applying excess quantities so that adhesive bleeds through joints.  Apply adhesive only in 				area which dries or films over.  Avoid soiling adjacent walls and floors with adhesive.  					Promptly remove any spillage.  Broom or roll carpet to remove air bubbles and insure bond.

D. 	Install carpet wall to wall unless noted otherwise.  Fit carpet neatly into breaks, recesses, 				closets and alcoves, against bases, around pipes and penetrations, under saddles and 					thresholds, and around permanent cabinets and equipment.  Install Schluter metal strip 				wherever carpet edge does not abut vertical surface, of appropriate configuration to provide 			smooth transition to adjacent material.  Allowable variation from level for finished 					installation: 1/4 in. from level in any direction when tested with 10 ft. straight-edge.

E. 	Seams shall be flat, free from puckering, without twists, free from frayed edges.  Coat edges 			with seam adhesive at glue-down installation, hot-melt tape at cushion, and as recommended 			by manufacturer.  Patterns at seams shall match exactly.  Cut raw edges on a slight angle 				with surface yarns extending outward over backing material so that surface yarns mingle 				neatly at seams.

F. 	Seams shall be in accordance with approved seaming shop drawings and samples.  No seams 			will be accepted perpendicular to openings such as doors, stairs, and entries.  Seams at doors 			shall be centered directly under doors.  Seam at corridor change of direction shall follow 				inner wall line across corridor.

G.	Provide removable cut-out pieces over flush equipment requiring access such as telephone 			and power outlets.  Cut-outs shall be neatly edged and securely held in place with double-				edged tape all around.

H. 	Remove adhesive spots from carpet immediately with solvent.  Trim loose pieces of face 				yarn with sharp scissors.  Upon completion of installation, remove rubbish, 	selvages, 					wrapping paper, small scraps, etc., and vacuum with commercial-type vacuum cleaner.  				Remove soiling, by shampoo if necessary.  Cover finished work with kraft paper or 					polyethylene until Substantial Completion.

- At completion of job, remove protective paper, vacuum or shampoo again if required.

END OF SECTION