Lee Urban- Director of Planning and Development

Aaron Shapiro- Director of Housing and Neighborhood Services

# Michael J. Nugent- Manager of Inspection Services

November 17, 2004

## RE:  Summary of CO inspection – 284 Fore St.

## CBL:  029-K-003

## PERMIT:  04-0954

A conditional Certificate of Occupancy is requested for the following areas in the building:

- First floor garage & Fore St. lobby

- Lower level garage & egress for hotel/office to Franklin Art.

- Second floor unoccupied space

- Third floor unoccupied space

- Fourth floor offices/unoccupied space on south side

- Fifth floor offices

The following list is required to be completed for a conditional Certificate of Occupancy:

- Fire penetrations in stair wells @ pipes

- Check for smoke requirement @ top of stair wells

- Audio-visual in the 4th fl. Break room (no strobes)

- Fire penetrations @ 5th fl. Above drop ceiling @ fire walls

- Exit sign required at rear egress to direct to Franklin Art.

- All construction debris removed @ egresses, interior & exterior

- Guardrail needed @ Fore St. pedestrian walkway near garage entrance