| 6. FIRE RESISTIVE REQUIREMENTS |  |  |
| --- | --- | --- |
| Construction Type: 3A | Noncumbustable / Combustible -Protected | Existing structure |
| Occupancy: A-3 | Restaurant |  |
| A. Exterior Bearing Walls Table 602, pg. 64 | No rating required, non-combustible with 30’-0” or more separation on all sides | Existing structure |
| B. Interior Bearing Walls Table 602, pg. 64 | 1 hour | 1 hour |
| C. Exterior Non-bearing Walls Table 602, pg. 64 | No rating required, non-combustible with 30’-0” or more separation on all sides. | Greater than 30’ separation. |
| D. Fire Walls and Party Walls Table 707.1, pg. 2 | 2 hour | N/A |
| E. Structural Members Supporting Walls Table 602, pg. 64 | 1 hour | 1 hr. |
| F. Partitions - Non-Bearing Table 602, pg. 64 | No rating required |  |
| G. Floor Construction Table 602, pg. 64 | 1 hour | 1 hour |
| H. Roof Construction Table 602, pg. 64 | No rating required |  |
| K. Interior Stair Enclosure Table 602, pg. 64; 1014.11, pg. 122 | 1 hour - where serving fewer than four stories. |  |
| J. Interior Wall and Ceiling Finishes Table 803.4, pg. 86 | Class II - in corridors providing exit access Class III - in rooms or enclosed spaces | N/A - (shell building only) Interior by tenant |
| K. Corridors Table 602, pg. 64; 1011.4, pg. 116; Table 1011.4, pg. 117 | 1 hr. | 1 hr. |