| 10. CORRIDOR REQUIREMENTS |  |  |
| --- | --- | --- |
| A. Width 1011.3, pg. 116 | 44" min. for occ. load greater than 50. 36" min. for occ. load 50 or less | 47" min. provided. |
| B. Height 1204.1, pg. 145; 1204.1.2, pg. 145 | Ceiling height of not less than 7 feet measured to the lowest projection from the ceiling. | 7’-6” min. provided |
| C. Projections 1011.1.4, pg. 116; 1022.2.1, pg. 131 | Doors when fully opened shall not reduce required width by more than 7". Doors in any position shall not reduce the required width by more than 1/2. Handrails shall not project into required width more than 3-1/2". | Provided. |
| D. Dead End 1011.2, pg. 114 | 20'-0" max. | No dead end corridor is greater than 20'-0". |
| 11. SPRINKLERS |  |  |
| 904.9, pg. 93; 904.10, pg. 93 | Required in accordance with NFPA 13R or approved NFPA 13. | Provided with automatic sprinkler system throughout. |
| 12. ATTICS |  |  |
| A. Access 1211.2, pg. 147 | Access shall be provided to ‘attic’ spaces by an opening not less than 22 inches by 30 inches. | Provided |
| B. Draft Stops 721.7.1.1, pg. 84 | Not required in R-2 construction where fully sprinkled. |  |
| C. Roof Vents 1210.1, pg. 146 | Required where ceilings are applied directly to the underside of rafters. | Provided |
| 13. SINGLE-PLY ROOF COVERING |  |  |
| 1507.5, pg. 153 | Minimum 1/4" per foot slope. | ¼” per foot provided |
| 14. Historic Structures |  |
| BOCA 3406.1 pg.338 | Compliance: The provisions of this code relating to the construction, repair, alteration, addition, restoration and movement of structures shall not be mandatory for existing buildings and structures identified and classified by the federal, state, or local government authority as historic buildings where such buildings are judged by the code official to be safe and in the interest of public health, safety and welfare regarding any proposed construction, alteration, repair, addition, and relocation. |