## 15 January 2014

Mr. Matt Provencal, Associate A.I.A.

Mark Mueller Architects,

100 Commercial Street, Suite 205,

Portland, Maine 04101

# RE: The Capacity to Handle Wastewater Flows, from a Proposed Residential Reuse, at 46 Market Street.

Dear Mr. Provencal:

Either the existing combined sewer pipe, located in Market Street, or the existing combined sewer pipe, located in Exchange Street, has adequate capacity to transport, while The Portland Water District sewage treatment facility, located off Marginal Way, has adequate capacity to treat, the total net increase in anticipated wastewater flows of 392 GPD, from this proposed project.

Anticipated Wastewater Flows from the Proposed Residential Units:

5 Proposed Residential Units @ 120 gpd per Unit 			  = 600 GPD

Less Wastewater Flows from Previous Tenants			  = 208 GPD

Total Net Increase in Proposed Wastewater Flows for this Project          = 392 GPD

In order to offset any increase in sanitary flows, the City combined sewer overflow (C.S.O.) abatement consent agreement (with the U.S.E.P.A., and with the Maine D.E.P.) requires C.S.O. abatement, as well as storm water mitigation, from all projects.  If the City can be of further assistance, please call 874-8832.

Sincerely,

CITY OF PORTLAND

Frank J Brancely, B.A., M.A.

Senior Engineering Technician

FJB

CC:         Jeffrey Levine, Director, Department of Planning, and Urban Development, City of Portland

Barbara Barhydt, Development Review Services Mgr., Dep’t.  of Planning, and Urban Development, City of Portland

Helen Donaldson, Planner, Department of Planning, and Urban Development, City of Portland

David Margolis-Pineo, Deputy City Engineer, City of Portland

Michael Farmer, P.E., Project Engineer, City of Portland

Bradley A. Roland, P.E., Environmental Projects Engineer, City of Portland

John Emerson, Wastewater Coordinator, City of Portland

Rhonda Zazzara, Field Inspection Coordinator, City of Portland

Jane Ward, Administrative Assistant, City of Portland

C:\Frank’s\Capacity Letters\Market Street 46