Details for the exterior deck for the Vignola / Cinque Terre Restaurant:

- 2 x 8 pressure treated ledger bolted to the brick wall

- Ledger bolted to existing masonry using ¾” galvanized all thread rod epoxied with 8” embedment into existing masonry wall.

- Cut pavement to allow for (4) 8” sonar tubes to be installed – backfill black top cold patch material around new tubes

- Install Simpson post brackets to sonar tubes for 4” x 4” pressure treated posts

- Install double 2 x 6 rim joists on outside perimeter of new posts - Level with wall mounted ledger

- Install 2 x 6 floor joists to face of ledger and rim using Simpson hangers 16” O C

- Install decking to flooring joists

- Install three stair stringers onto rim joist using Simpson hangers

- Height of deck is 27” off existing grade and finished floor of deck is at same elevation minus 3/8” finished interior floor– (4) 6 ¾”risers x11” treads (includes the ¾” decking applied to stringers)

- Allow the 4 x 4 posts to run above the decking to allow for installation of hand railing

- Install 1 x 4 pressure treated top and bottom rails with 1” x 1” wood balusters spaced less than 4”  between

- Install metal handrail and attach to 4 x 4 posts

- Install all posts and joists using coated (galvanized) fasteners