SECTION 01500

TEMPORARY FACILITIES

1. 	GENERAL

1.1	DESCRIPTION OF REQUIREMENTS:  Provide temporary services and facilities ready 	for use when first needed to avoid delay in the work.  Maintain, expand and modify as 	needed.  Do not remove until no 	longer needed, or replaced by authorized use of 	permanent facilities.

1.2 	USE CHARGES:  Usage charges for temporary services or facilities are not chargeable to 	the Owner or Architect/Engineer.

1.3 	REGULATIONS:  Comply with requirements of local laws and regulations governing 	construction and local industry standards, in the installation and maintenance of temporary 	services and facilities.

1.4	STANDARDS:  Comply with the requirements of NFPA Code 241, "Building 	Construction and Demolition Operations", the ANSI-A10 Series standards for "Safety 	Requirements for Construction and Demolition", and the NECA National Joint Guideline 	NJG-6 "Temporary Job Utilities and Services".

1.5	INSPECTIONS:  Inspect and test each service before placing temporary utilities in use.  	Arrange for inspections and tests by governing authorities, and obtain certifications and 	permits for use.

1.6 	SUBMITTALS:  	Submit copies of reports and permits required or necessary for 	installation and operation, including reports of tests, inspections and meter readings 	performed on temporary utilities, and permits and easements necessary for installation, use 	and operation.

1.7 	MATERIALS AND EQUIPMENT

A.  	Provide materials and equipment that are suitable for the intended use.

B.  	Provide new materials and equipment for temporary services and facilities; if 				acceptable to the Architect/Engineer, used materials and equipment that are 				undamaged may be used.

1.8 	INSTALLATION

A.  	Use qualified tradesmen for installation.

B.  	Locate temporary services and facilities where they will serve the project adequately 		and result in minimum interference with the work.

1.9 	TEMPORARY UTILITY INSTALLATION

A.  	Engage, or make arrangements with, the local utility company to make connections 			to existing service.

B.  	Arrange with the companies and existing users for an acceptable time when service 			can be interrupted to make connections.

C.  	Establish a service implementation and termination schedule.  As early as possible 			change to use of permanent service, to enable removal of the temporary utility and 			eliminate possible interference with completion of the work.

D.  	Provide adequate capacity at each stage of construction.  Prior to availability at the 			site, provide, trucked-in services for start up of construction operations.

E.  	Obtain and pay for easements required to bring temporary utilities to the site, where 			the Owner's easement cannot be utilized for that purpose.

1.10	ELECTRIC POWER SERVICE

A.  	Provide weathertight, grounded temporary electrical service-entrance and distribution 		system, with ground-fault circuit interrupters and ground-fault interrupter features of 		proper types, sizes, electrical ratings and characteristics to fulfill project 					requirements.

B. 	Comply with applicable requirements of NEMA, NECA and UL standards and 			governing regulations.

C.  	Install temporary lighting of adequate illumination levels to perform the work 				specified.

D.  	Comply with NEC pertaining to installation of temporary wiring service and 				grounding.  Provide meters, transformers, and overcurrent protective devices at main 		distribution panel for power and light circuitry.  Provide disconnects for equipment 			circuits.

E.  	Connect service to local power company main supply in the manner directed by 			utility company officials.  Pay usage charges for electricity used by entities 				authorized to perform the work at the site.

1.11	POWER DISTRIBUTION SYSTEM

A.  	Provide circuits of proper sizes, characteristics, and ratings for each use indicated.

B.  	Install wiring overhead, and risers vertically where least exposed to damage.

C.  	Provide rigid steel conduit to protect wiring on grade, floors, decks or other areas 			exposed to possible damage.

D.  	Provide 20 amp, 4-gang receptacle outlets, equipped with ground-fault circuit 				interrupters, reset button and pilot light, spaced that a 100 foot extension cord can 			reach each area of work.  Use only grounded extension cords; use "hard- service" 			cords where exposed to abrasion and traffic.

E.  	Provide warning signs at power outlets that are other than 110/120 volt.  Provide 			outlets of proper NEMA configuration to prevent insertion of 110/120 volt plugs into 		higher voltage outlets.

1.12	TEMPORARY LIGHTING

A.  	Provide general service incandescent lamps of wattage required for adequate 				illumination.

B.  	Protect lamps with guard cages or tempered glass enclosures, where exposed to 			breakage.

C.  	Provide exterior type fixtures where exposed to weather or moisture.

D.  	Provide one 200-watt incandescent lamp per 1000 square feet of floor area for 			general construction lighting, one 100-watt incandescent lamp every 50 feet in 			corridors, and one lamp per story, located to illuminate each landing and flight in 			stairways.

E.  	Install temporary lighting to fulfill security and protection requirements, without 			having to operate the entire temporary lighting system.

1.13 	TEMPORARY TELEPHONES

A.  	Install telephone for each temporary office and first aid station.

B.  	At each telephone location post a list of operational and emergency telephone 				numbers.

1.14	TEMPORARY HEAT

A.  	Provide temporary heat where needed for performance of work, for curing or drying 		of recently installed work or for protection of work in place from adverse effects of 			low temperatures or high humidity.

B.  	Provide UL or FM tested and labeled heating units known to be safe and without 			adverse effect upon work in place or being installed.  Coordinate with ventilation 			requirements to produce the ambient condition.

C.  	Maintain a minimum temperature of 45 deg. F (7 deg. C) in permanently enclosed 			portions of the building and areas where finished work has been installed.

D.  	Except where use of the permanent heating system is available and authorized, 			provide properly vented self-contained LP gas or fuel oil heaters with individual 			space thermostatic control for temporary heat.  Do not use open burning or 				salamander type heating units.

1.15 	FIELD OFFICES

A.  	Provide standard prefabricated or mobile units, or the equivalent job-built field 			offices of sufficient size to accommodate required office personnel at the site.

B.  	Provide insulated, weathertight units with lockable entrances.

C.  	Provide vented space heater, capable of maintaining an indoor temperature of 68 deg. 		F (20 deg. C).

1.16	SANITARY FACILITIES

A.  	Sanitary facilities toilets.  General Contractor may use existing toilets in basement for his use during construction.

B.  	Comply with governing regulations including safety and health codes for the type, 			contractor may use existing toilet in basement.

C.  	Supply toilet tissue, paper towels, paper cups and similar disposable materials as 			appropriate for each facility.  Provide covered waste containers for used material.

D   	Provide drinking water fountains where and when piped potable water, approved by 		local authorities, is reasonably accessible from permanent or temporary lines.  				Otherwise, provide containerized tap-dispenser bottled-water type drinking water 			units.

1.17 	FIRST AID SUPPLIES

A.  	Comply with governing regulations and recognized recommendations within the 			construction industry.

1.18	DEWATERING FACILITIES AND DRAINS

A. 	For temporary drainage and dewatering facilities and operations not directly 				associated with performance of work included under other sections, comply with 			dewatering requirements of applicable Division-2 sections.  Where feasible, utilize 			the same facilities.

B.  	Maintain the site, excavations and construction free of water.

C.  	Dispose of rainwater in a lawful manner which will not result in flooding and project 		or adjoining property, nor endanger either permanent work or temporary facilities.

1.19 	TEMPORARY ENCLOSURE

A.  	Provide temporary enclosure of materials, equipment, work in progress and 				completed portions of the Work to provide protection from exposure, foul weather, 			other construction operations, and similar activities.

B.  	Provide enclosures where temporary heat is needed and the permanent building 			enclosure is not completed, and there is no other provision for containment of heat.  			Coordinate with ventilating and material drying or curing requirements to avoid 			dangerous conditions.

C.  	Provide temporary enclosures by installing waterproof, fire- resistant, UL labeled 			tarpaulins with a flame-spread rating of 15 or less, using a minimum of wood 				framing.  Use translucent nylon reinforced laminated polyethylene tarpaulins to 			admit the maximum amount of daylight.  Individual openings of 25 square feet or 			less may be closed with plywood or similar materials.

D.  	Close openings through the floor or roof decks and other horizontal surfaces with 			substantial load-bearing wood-framed or similar construction.

1.20	COLLECTION AND DISPOSAL OF WASTES

A.  	Establish a system for daily collection and disposal of waste materials.  Do not hold 			collected materials longer than 7 days.

B.  	Handle waste materials that are hazardous, dangerous, or unsanitary separately from 		other waste by containerizing.

C.  	Burying or burning of waste materials on the site or washing waste material down 			sewers will not be permitted.

1.21	MISCELLANEOUS SERVICES AND FACILITIES:  Design, construct, and maintain 	miscellaneous services and facilities as needed to accommodate performance of the  work, 	including temporary stairs, ramps, ladders, staging, shoring, scaffolding, temporary 	partitions, waste chutes and similar items.

1.22 	SECURITY AND PROTECTION FACILITIES INSTALLATION

A.  	Provide a neat and uniform appearance in security and protection facilities acceptable 		to the Architect/Engineer and the Owner.

B.  	Maintain site in a safe, lawful and publicly acceptable manner.

C.  	Take necessary measures to prevent erosion.

D.  	Except for utilization of permanent fire protection facilities, as soon as available, do 			not change over to use of permanent facilities until substantial completion.

1.23 	TEMPORARY FIRE PROTECTION

A.  	Until fire protection needs may be fulfilled by permanent facilities, install and 				maintain temporary fire protection of the types needed to protect against losses.

B.  	Comply with recommendations of NFPA Standard 10.

C.  	Locate fire extinguishers where most effective; provide not less than one on each 			floor at or near each stairwell.

D.  	Provide type "A" fire extinguishers for temporary offices and spaces where there is 			minimal danger of electrical or flammable liquid fires, and type  "ABC" dry 				chemical extinguishers elsewhere.

E.  	Store combustible materials in containers in fire-safe locations.

F.  	Review fire prevention and protection needs with local fire department officials and 			establish procedures to be followed in the event of fire.  Instruct personnel in 				procedures and post warnings and information.

G.  	Maintain unobstructed access to fire extinguishers, temporary fire protection 				facilities, stairways and other access routes.

H.  	Prohibit smoking in hazardous areas.

I.  	Provide supervision of welding operations, combustion type temporary heating units, 		and similar sources of ignition.

J.  	At temporary water outlets provide hoses of sufficient length to reach construction 			areas.  Hang hoses with a warning sign, indicating that hoses are for fire protection 			purposes and are not to be removed.

K.  	At the earliest feasible date complete installation of the permanent fire protection 			facility, including connected services, and place into operation and use.  Instruct key 		personnel at the site on how to use facilities which may not be self-explanatory.

1.24	BARRICADES, WARNING SIGNS AND LIGHTS

A.  	Comply with recognized standards and code requirements for erection of substantial, 		barricades where needed to prevent accidents.

B.  	Paint with appropriate colors and warning signs to inform personnel at the site and 			the public, of the hazard being protected against.

C.  	Provide lighting where needed, including flashing red lights where appropriate.

1.25 	SECURITY ENCLOSURE AND LOCKUP

A.  	Where materials and equipment must be temporarily stored, and are of substantial 			value or attractive for possible theft, provide a secure lockup.

1.26 	ENVIRONMENTAL PROTECTION

A.  	Conduct construction activities, and by methods that comply with environmental 			regulations, minimize the possibility that air, waterways and subsoil might be 				performance of work at the site.

B.  	Avoid the use of tools and equipment which produce harmful noise.

C.  	Restrict the use of noise making tools and equipment to hours of use that will 				minimize complaints.

1.27 	OPERATION, TERMINATION AND REMOVAL

A.  	Limit availability of temporary services and facilities to essential and intended uses 			to minimize waste and abuse.  Do not permit temporary installations to be abused or 		endangered.

B.  	Operate and maintain temporary services and facilities in good operating condition 			and in a safe and efficient manner until removal is authorized.  Do not overload 			services or facilities.  Protect from damage by freezing temperatures and similar 			elements.

C.  	Do not allow unsanitary conditions, public nuisances or hazardous conditions to 			develop or persist on the site.

D.  	Maintain operation of temporary enclosures, heating, cooling, humidity control, 			ventilation and similar facilities on a 24- hour basis where required to achieve 				indicated results and avoid the possibility of damage to the Work or to temporary 			facilities.

E.  	Prevent water filled piping from freezing.  Maintain markers for underground lines.  			Protect from damage during excavation.

F.  	Remove each temporary service and facility promptly when need has ended, or when 		replaced by use of a permanent facility, but no later than substantial completion.  			Complete, or, if necessary, restore permanent work delayed because of interference 			with the temporary service or facility.  Repair damaged work, clean exposed surfaces 		and replace work which cannot be repaired.

G.  	At substantial completion, clean and renovate permanent services and facilities that 			have been used to provide temporary services and facilities during the construction 			period.

END OF SECTION