SECTION 07200

INSULATION AND VAPOR BARRIERS

1.	GENERAL:

1.1  	GENERAL PROVISIONS:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2  	DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet the requirements of the Specifications.  The work covered by this section of Specifications consists of the following:

1.  	Installation of rigid insulation on inside foundation wall and sill sealer, where shown on 				Drawings (done by others).

2.  	Installation of rigid insulation, fiberglass batts, sound insulation in exterior walls, interior walls, ceilings and floors where shown on Drawings.

3. 	Vapor barriers to be installed as shown.

2.	PRODUCTS:

2.1  	SLAB AND FOUNDATION WALL INSULATION:  sizes as shown on Drawings.  Type Sm Styrofoam insulation by Dow Chemical, or approved equal.

  - BATT INSULATION TYPE:  Fiberglass by Owens-Corning- Fiberglass, or approved equal.  See wall type for interior walls, 6 ” in Exterior Walls, 12” in attic Ceilings.

  - Cavity Wall Sheathing Insulation:  ½” Celotex Insulation Board.

2.4  	MOISTURE PROTECTION:  6 mil. clear polyethylene film in walls and ceilings where shown on drawings. See concrete for vapor barrier under slab.

3.  	EXECUTION:

3.1  	RIGID INSULATION 2” x 48” deep and 4” min. below grade.  1” foil faced urethane in roof framing, see drawings.

3.2 	FIBERGLASS INSULATION

A.	Fiberglass batts in exterior walls between floors shall be fluffed to full nominal depth and shall 	be stuffed in around window unit frame to fill gap between frame and rough opening studs.  Secure wall batts at top of cavity with wire screws.

3.3  	MOISTURE PROTECTION:  A continuous 8-mil. vapor barrier shall be installed on all exterior walls and roofs, as part of the work of this Section.  Vapor barrier on walls shall be 8' wide to minimize horizontal joints.  All joints in vapor barrier shall be taped, and all vapor barrier free edges shall be taped to substrate.  Minimum lap at joints to be 8" including lap at wall/ceiling (cap 8" each surface).  Adhear Vapor Barrier to steel Truss with silicone.

END OF SECTION