SECTION 07900

JOINT SEALERS

1. 	GENERAL:

1.1	REFERENCES:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2	DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet requirements of these Specifications.  The work covered by this section of Specifications includes the following items:

A. 	Caulking on windows, doors and exterior wall for water tightness.

B.  	General Caulking to patch, fill, and repair in building interior.

C.  	Acoustical caulking at top and bottom of party and unit/corridor walls.

D.	Caulking for brick expansion joints.

2.   	PRODUCTS:

2.1	CAULKING MATERIAL

A.	For item 1.2 A:  Silicone Spectrum 2.

B.	For item 1.2 B:  Tremco Latex 834.

C.	For item 1.2 C:  Tremco Acoustical Sealant.

D.	For item 1.2 D:  Tremco Elastom Eric Spectrum 3.

3.  	EXECUTION:

3.1	ALL POTENTIAL INFILTRATION cracks & joints to be caulked.  Caulking shall be done only by workmen who are thoroughly experienced in this work.  Exterior caulking shall be applied around all windows, doors, vents, utilities, at top of foundation, and any other infiltration "crack".

3.2	NOTE:  Apply caulking under corner boards and window, door trim as trim applied.  Apply caulking under flange as window is installed.

3.3	INTERIOR CAULKING shall be applied to seal all penetrations through top plates of interior walls, (due to electrical or plumbing), and at tubs, showers, counter tops, bottom of party walls GWB, and other as shown on Drawings.

3.4	IN GENERAL, caulking to be done prior to (in conjunction with) siding installation.  See Drawings for any additional applications.  Joints and spaces to be caulked shall be dry and free from dust.  Finished caulking "bead" shall be neat and smooth, free of gaps and sags and run continuously.  Complete all caulking work and allow to stand for the manufacturer's recommended time period before painting.  Prime if required before finish coat of paint is applied.

END OF SECTION