SECTION 08600

WINDOWS

1. 	GENERAL;

1.1	REFERENCES:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2	DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet the requirements of these Specification.  The work covered by this section of specifications consists of the following:

A.  	Furnishing and installing all windows as shown on Drawings, complete with all window 			hardware, operators and other accessories, including corner flashing pieces.

B.  	Furnishing window screens.

C.  	Adjusting the windows for smooth and faultless operation.

2. 	PRODUCTS:

2.1	SINGLE HUNG AND FIXED GLASS WINDOWS shall be aluminum with paint finish P.P.G. to match existing style & type, with insulated glazing; window color to be black.  Every operable window to have screens.  Screens to be packaged independently of windows.

2.2  	ALL DIMENSIONS shall be as shown on Drawings, Contractor to field verify or from manufacturer's information.

2.3  	WINDOWS to be Traco TR-9100 single hung side loan thermal aluminum window panning or exterior to cover existing wood.

3. 	EXECUTION:

3.1 	WINDOWS shall be installed by workmen experienced in this kind of work.  Set window frames plumb, level and square, within clearance limits of the respective openings.  Fasten frames securely to the wall framing.  Window frames and other installation materials shall be handled carefully at all times and shall be protected from all possible sources of damage such as dampness, dirt, mortar, etc.  Units shall be stacked standing on edge on wood strips to prevent contact with ground.  Installation of windows shall strictly follow the manufacturer's recommendations.

3.2 	CAULK windows as required in other sections and on drawings.  Install corner flange closures and caulk as window is installed.

3.3   AFTER the windows are installed, they shall be checked for smooth operation and adjusted as necessary.  Install screens.  Leave all installed windows and screens clean, tight and weatherproof.

END OF SECTION