Job Information

Unit Information

Cooling Information

Heating Information

Motor/Electrical Information*

12 1/2-25 Ton Packaged Unitary Cooling Rooftop - Dedicated

MECA 2008

Tag

AC-1

Quantity

1

Model number

Airflow Configuration

Horizontal

Three Phase Cooling Capacity

181C: 15 T, Hi. Eff.

Electrical Characteristics

208-230/60/3

Trane communications interface (TCI)

Design airflow

6000 cfm

Elevation

Min. unit operating weight

1838.0 lb

Max. unit operating weight

2285.0 lb

Electrical Characteristics

208-230/60/3

0.50 in H2O

ESP

Indoor mtr operating power

2.03 bhp

Indoor rpm

592 rpm

Indoor motor power

2.09 kW

SEER/EER @ ARI

11.5 EER

IPLV @ ARI

13.3 IPLV

MCA

74.00 A

MOP

90.00 A

MCA for 230 or 415 w/elec heat

0.00 A

MOP for 230 or 415 w/elec heat

0.00 A

Compressor motor 1 RLA

31.50 A

Compressor motor 2 RLA

16.90 A

Evaporator fan FLA

10.60 A

Condenser fan FLA

3.20 A

Condenser fan count

2.00 Each

Cooling EDB

80.00 F

Cooling EWB

67.00 F

Ambient temp

95.00 F

Cooling LDB

59.79 F

Cooling LWB

57.49 F

Gross total capacity

189.04 MBh

Gross sensible capacity

142.09 MBh

Gross latent capacity

46.94 MBh

Net total capacity

181.89 MBh

Net sensible capacity

134.95 MBh

Net sensible heat ratio

0.74 %

Evaporator face area

26.00 sq ft

Evaporator face velocity

231 ft/min

Electric Heaters

No Electric Heater

FIOPS Electric Heaters

No Electric Heaters

Output htg capacity

Output htg capacity w/fan

Heating EAT

Heating LAT

Heating delta T

Net sensible heat ratio w/reheat on

Cooling LDB w/reheat

Standard Factory Installed Options

Dehumidification Information

Reheat Capacity (MBH)

Cooling LDB w/reheat

Net sensible heat ratio w/reheat on

Reheat Temp Rise

Dew Point Temp

56.02 F

Evap Coil Leaving Air Temp (DB)

Evap Coil Leaving Air Temp (WB)

Leaving Unit Rel Humid w/Reheat

Moisture Removal (gal/hr)

Dew Point Temp

Evap Coil Leaving Air Temp (DB)

58.16 F

Evap Coil Leaving Air Temp (WB)

56.86 F

TFH181

* Electrical values provided are estimated only and are subject to change without notice and may differ from nameplate values.

Field installed low or high static drive kits may be needed.  Please check the fan performance tables in the product catalog for application ranges.

3/31/2008

Product Version

2002.11.12.1

N:\2800 to 2899 Jobs\2806 MECA 2008\Calculations\2806.psd

Job Information

Unit Information

Cooling Information

Heating Information

Motor/Electrical Information*

12 1/2-25 Ton Packaged Unitary Cooling Rooftop - Dedicated

MECA 2008

Tag

AC-2

Quantity

1

Model number

Airflow Configuration

Horizontal

Three Phase Cooling Capacity

150E: 12.5 ton Std.Eff. R410A

Electrical Characteristics

208-230/60/3

Trane communications interface (TCI)

Design airflow

4500 cfm

Elevation

Min. unit operating weight

1489.0 lb

Max. unit operating weight

1891.0 lb

Electrical Characteristics

208-230/60/3

0.50 in H2O

ESP

Indoor mtr operating power

2.20 bhp

Indoor rpm

815 rpm

Indoor motor power

1.64 kW

SEER/EER @ ARI

11.0 EER

IPLV @ ARI

11.5 IPLV

MCA

63.00 A

MOP

80.00 A

MCA for 230 or 415 w/elec heat

0.00 A

MOP for 230 or 415 w/elec heat

0.00 A

Compressor motor 1 RLA

22.40 A

Compressor motor 2 RLA

22.40 A

Evaporator fan FLA

10.60 A

Condenser fan FLA

3.20 A

Condenser fan count

2.00 Each

Cooling EDB

80.00 F

Cooling EWB

67.00 F

Ambient temp

95.00 F

Cooling LDB

60.03 F

Cooling LWB

56.39 F

Gross total capacity

154.00 MBh

Gross sensible capacity

104.00 MBh

Gross latent capacity

50.00 MBh

Net total capacity

147.07 MBh

Net sensible capacity

97.07 MBh

Net sensible heat ratio

0.66 %

Evaporator face area

17.50 sq ft

Evaporator face velocity

257 ft/min

Electric Heaters

No Electric Heater

FIOPS Electric Heaters

No Electric Heaters

Output htg capacity

Output htg capacity w/fan

Heating EAT

Heating LAT

Heating delta T

Net sensible heat ratio w/reheat on

Cooling LDB w/reheat

Standard Factory Installed Options

Dehumidification Information

Reheat Capacity (MBH)

Cooling LDB w/reheat

Net sensible heat ratio w/reheat on

Reheat Temp Rise

Dew Point Temp

53.94 F

Evap Coil Leaving Air Temp (DB)

Evap Coil Leaving Air Temp (WB)

Leaving Unit Rel Humid w/Reheat

Moisture Removal (gal/hr)

Dew Point Temp

Evap Coil Leaving Air Temp (DB)

58.60 F

Evap Coil Leaving Air Temp (WB)

55.83 F

TFH150

* Electrical values provided are estimated only and are subject to change without notice and may differ from nameplate values.

Field installed low or high static drive kits may be needed.  Please check the fan performance tables in the product catalog for application ranges.

3/31/2008

Product Version

2002.11.12.1

N:\2800 to 2899 Jobs\2806 MECA 2008\Calculations\2806.psd