Copyright 1998, The American Institute of Architects (AIA)

SECTION 01500

TEMPORARY FACILITIES AND CONTROLS

This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

      - RELATED DOCUMENTS

        - Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification Sections, apply to this Section.

      - SUMMARY

        - This Section includes requirements for temporary facilities and controls, including temporary utilities, support facilities, and security and protection facilities.

        - Temporary utilities include, but are not limited to, the following:

Adjust list below to suit Project.

Heating and cooling facilities.

Ventilation.

Electric power service.

Lighting.

Telephone service.

Internet service.

        - Support facilities include, but are not limited to, the following:

Adjust list below to suit Project.

Project identification and temporary signs.

Field offices.

Storage and fabrication sheds.

Lifts and hoists.

Construction aids and miscellaneous services and facilities.

        - Security and protection facilities include, but are not limited to, the following:

Adjust list below to suit Project.

Perimeter enclosure fence for the site.

Security enclosure and lockup.

Barricades, warning signs, and lights.

Temporary enclosures.

Fire protection.

Related Sections include the following:

List below only products, construction, and equipment that the reader might expect to find in this Section but are specified elsewhere.

Division 1 Section "Submittal Procedures" for procedures for submitting copies of implementation and termination schedule and utility reports.

Division 1 Section "Execution Requirements" for progress cleaning requirements.

Retain subparagraph above or below.  Coordinate with materials specified in "Materials" Article in Part 2.

Divisions 2 through 16 for temporary heat, ventilation, and humidity requirements for products in those Sections.

      - USE CHARGES

Retain paragraph and subparagraphs below to prevent extra cost charges to Owner.

        - General:  Cost or use charges for temporary facilities are not chargeable to Owner or Architect and shall be included in the Contract Sum.  Allow other entities to use temporary services and facilities without cost, including, but not limited to, the following:

Revise list below to suit Project.  Add other known entities using temporary services and facilities.

Owner's construction forces.

Occupants of Project.

Architect.

Construction observer

Testing agencies.

Personnel of authorities having jurisdiction.

Delete paragraph below for projects constructed under multiple contracts.

Retain paragraph below only if water service is available on-site and Owner will pay for water used by all construction activities.

Delete paragraph below for projects constructed under multiple contracts where water service is not available on-site or Owner will not permit free use of water from existing system.

        - Water Service: Utilize existing water service at the janitor closet. Provide 3/4" heavy-duty rubber hoses with shut-off nozzle.

Retain paragraph below only if electric power service is available on-site and Owner will permit tapping into existing system without charge.

Delete paragraph below for projects constructed under multiple contracts where electric power is not available on-site or Owner or utility will not permit tapping into existing system.

        - Electric Power Service: Utilize existing electrical serve at utility closet on each renovated floor. Include necessary meters, transformers, overload protected disconnects, automatic ground-fault interrupter and main distribution switch gear.

        - Fuel, power and other utility charges incurred for testing and start-up of equipment shall be paid for by the Contractor as part of the work.

      - SUBMITTALS

Cold-Weather Procedures: Detailed description of methods, materials, and equipment to be used to comply with cold-weather requirements to protect install concrete and masonry.

Besides water, electricity, and sewer service indicated above, insert use-charge requirements for other utilities needed.

Insert requirements for submitting installation Drawings of critical temporary utilities if required.

      - QUALITY ASSURANCE

If Owner has made environmental-impact commitments, attach copies or indicate where they may be examined.

        - Standards: Comply with ANSI A10.6, NECA's "Temporary Electrical Facilities," and NFPA 241.

First subparagraph below may avoid unnecessary use of high-cost labor.

Trade Jurisdictions:  Assigned responsibilities for installation and operation of temporary utilities are not intended to interfere with trade regulations and union jurisdictions.

Electric Service:  Comply with NECA, NEMA, and UL standards and regulations for temporary electric service.  Install service to comply with NFPA 70.

        - Tests and Inspections:  Arrange for authorities having jurisdiction to test and inspect each temporary utility before use.  Obtain required certifications and permits.

        - The Contractor is responsible for the implementation, monitoring, and maintenance of job site safety program for the duration of the contract.

      - PROJECT CONDITIONS

Revise paragraph and subparagraph below to minimize temporary use of permanent utilities, or insert exceptions to provisions.  Discourage attempts to delay activation of standpipes and sprinklers.

        - Temporary Utilities:  At earliest feasible time, when acceptable to Owner, change over from use of temporary service to use of permanent service.

Retain subparagraph below to impose responsibility for maintenance and protection of permanent services and facilities used to provide temporary service and facility.

Temporary Use of Permanent Facilities:  Installer of each permanent service shall assume responsibility for operation, maintenance, and protection of each permanent service during its use as a construction facility before Owner's acceptance, regardless of previously assigned responsibilities.

        - Conditions of Use:  The following conditions apply to use of temporary services and facilities by all parties engaged in the Work:

Keep temporary services and facilities clean and neat.

Relocate temporary services and facilities as required by progress of the Work.

        - Restrict use of noise-making tools and equipment to hours that will minimize complaints from persons or tenants near the site.  Construction noise from machinery, equipment, construction traffic, hammering and similar loud noises shall be restricted to the hours of 8:00 a.m. to 5:00 p.m.  Obey State and local noise ordinances.

PRODUCTS

      - MATERIALS

        - General:  Provide new materials.  Undamaged, previously used materials in serviceable condition may be used if approved by Architect.  Provide materials suitable for use intended.

Delete materials not required.  Add materials to suit Project.

If Specification Sections in paragraph below are not included in Project, add requirements here.

        - Lumber and Plywood: Comply with requirements in Division 6 Section "Rough Carpentry."

        - Tarpaulins:  Fire-resistive labeled with flame-spread rating of 15 or less.

        - Water:  Potable.

EQUIPMENT

Delete equipment below not required.  Add equipment to suit Project.

        - General:  Provide equipment suitable for use intended.

Revise paragraph and subparagraphs below to add stricter requirements when conditions warrant.  Retain all three options in paragraph below if type of construction is Contractor's option.

        - Field Offices: To be located within renovated area with lockable entrances, and serviceable finishes; heated and air conditioned.

        - Fire Extinguishers:  Hand carried, portable, UL rated.  Provide class and extinguishing agent as indicated or a combination of extinguishers of NFPA-recommended classes for exposures.

Comply with NFPA 10 and NFPA 241 for classification, extinguishing agent, and size required by location and class of fire exposure.

Delete paragraph below if fixtures connected to previously installed water and sewer service must be used.

Retain first option in paragraph below if potable water is accessible from permanent or temporary lines.  If potable water is not available, retain second option.

        - Drinking-Water Fixtures: Containerized, tap-dispenser, bottled-water drinking-water units, including paper cup supply.

Revise paragraph and subparagraphs below to suit Project.  Liquid-propane-gas or fuel-oil heaters are commonly used.  Steam or hot-water heaters, gas-fired space heaters, or electric unit heaters are also used.

        - Heating Equipment:  Owner authorizes use of the permanent heating system.

Usually retain first subparagraph below.  Gasoline-burning and salamander-type heating units are usually prohibited.

Use of gasoline-burning space heaters, open-flame heaters, or salamander-type heating units is prohibited.

        - Electrical Outlets: Properly configured, NEMA-polarized outlets to prevent insertion of 110- to 120-V plugs into higher-voltage outlets; equipped with ground-fault circuit interrupters, reset button, and pilot light.

        - Power Distribution System Circuits: Where permitted and overhead and exposed for surveillance, wiring circuits, not exceeding 125-V ac, 20-A rating, and lighting circuits may be nonmetallic sheathed cable.

        - Lamps and Light Fixtures: Provide general service incandescent lamps of wattage required for adequate illumination. Provide guard cages or tempered-glass enclosures where exposed to breakage. Provide exterior fixtures where exposed to moisture.

        - Security Fence: Perimeter security fencing shall be minimum 4 feet high, Tensar fencing with post set to adequately support fence and maintain position. Provide access and entry control gates for vehicle traffic and workers as necessary.

EXECUTION

INSTALLATION, GENERAL

        - Locate facilities where they will serve Project adequately and result in minimum interference with performance of the Work.  Relocate and modify facilities as required.

        - Provide each facility ready for use when needed to avoid delay.  Maintain and modify as required.  Do not remove until facilities are no longer needed or are replaced by authorized use of completed permanent facilities.

      - TEMPORARY UTILITY INSTALLATION

General: Engage appropriate local utility company to install temporary service or connect to existing service.  Where utility company provides only part of the service, provide the remainder with matching, compatible materials and equipment.  Comply with utility company recommendations.

Arrange with utility company, Building owner, and existing users for time when service can be interrupted, if necessary, to make connections for temporary services.

Provide adequate capacity at each stage of construction.  Before temporary utility is available, provide trucked-in services.

Obtain easements to bring temporary utilities to Project site where Owner's easements cannot be used for that purpose.

Add provisions for work not in the Contract but served by temporary facilities if required.

Paragraph below includes typical requirements.  Delete for climates where low winter temperatures are uncommon.

        - Heating and Cooling:  Provide heating and cooling required by construction activities for curing or drying of completed installations or for protecting installed construction from adverse effects of low temperatures or high humidity.  Select equipment from that specified that will not have a harmful effect on completed installations or elements being installed.

Retain subparagraph below if a minimum temperature in enclosed portions of building is required to forestall possibility of damage to completed construction.

Maintain a minimum temperature of 50 deg F (10 deg C) in permanently enclosed portions of building for normal construction activities, and 65 deg F (18.3 deg C) for finishing activities and areas where finished Work has been installed.  Maintain higher minimum temperatures before, during, and after installations of materials and finishes as specified in the individual Sections of Divisions 2 through 16.

Prior to operation of permanent equipment for temporary heating purposes, verify that installation is approved for operation, equipment is lubricated and filters are in place.  Provide and pay for operation, maintenance, and replacement of filters and worn or consumed parts.

        - Ventilation and Humidity Control: Provide temporary ventilation required by construction activities for curing or drying of completed installations or for protecting installed construction from adverse effects of high humidity.  Select equipment from that specified that will not have a harmful effect on completed installations or elements being installed.  Coordinate ventilation requirements to produce ambient condition required and minimize energy consumption.

Insert gas or other utility services if required for Project.

Revise paragraph and subparagraphs below to suit Project; include special power loads, such as continued operation of existing facility, while power changeover is being made.

Retain subparagraph below if Owner is unwilling to permit use of building's existing electric service.

Retain paragraph and subparagraphs above or paragraph below.  Delete below if facilities are not available or their use is not permitted even if available.

        - Temporary Lighting:

Install and operate temporary lighting that will fulfill security and protection requirements without operating the entire system. Provide temporary lighting that will provide adequate illumination for construction operations and traffic conditions. A minimum of 80 foot candles shall be supplied at mid-height of surfaces for taping, painting and finish work.

Revise paragraph and subparagraphs below to suit Project.

        - Telephone and Internet Service:  Provide temporary telephone and internet service throughout construction period for use by contractor.

Delete subparagraph below if not required.

At each telephone, post a list of important telephone numbers.

Revise list below to suit Project.  See Evaluations.

Police and fire departments.

Ambulance service.

Contractor's home office.

Architect's office.

Engineers' offices.

Prudential's office.

Principal subcontractors' field and home offices.

Retain four subparagraphs below if required to suit Project.  See Evaluations.

Provide an answering machine on superintendent's telephone.

Internet Services: Provide internet service throughout construction period at the field office.

If Project requires food and beverage service facilities, insert provisions here.

SUPPORT FACILITIES INSTALLATION

        - General:  Comply with the following:

Locate field offices, storage sheds, and other temporary facilities and support facilities for easy access.

Review first subparagraph below with Owner's insurance carrier.  Revise to suit Project.

Maintain support facilities until near Substantial Completion.  Remove before Substantial Completion.  Personnel remaining after Substantial Completion will be permitted to use permanent facilities, under conditions acceptable to Owner.

Retain paragraph and subparagraphs above or below.  Retain above if temporary roads and paved areas are not in same location as permanent roads or paved areas.  See Evaluations.

Traffic controls in paragraph below may or may not be necessary, depending on Project.

        - Project Identification and Temporary Signs: Prepare Project identification and other signs in sizes indicated.  Install signs where indicated to inform public and persons seeking entrance to Project.  Do not permit installation of unauthorized signs.

Revise subparagraphs below to suit Project.  Delete if not required.  If required, insert a list of necessary signs and add Project-specific provisions, such as special graphics and special lighting.  See Evaluations.

Engage an experienced sign painter to apply graphics for Project identification signs.  Comply with details indicated. Include name of project, and names of Owner, Architect and Contractor.

Prepare temporary signs to provide directional information to construction personnel and visitors.

Add references to approved disposal methods to paragraph below.  Cross-reference Sections that specify handling of special waste materials.  See Evaluations.

Retain first paragraph below for large projects.

        - Contractor’s Field Office:  Provide field office for use as a common facility by all personnel engaged in construction activities; of sufficient size to accommodate required office personnel and meetings of 10 persons at Project site.  Keep office clean and orderly.  Pay utility costs for field office for the duration of the project.

Furnish and equip office as follows:

Revise subparagraph below by adding items of furniture as needed.

Desk and four chairs, four-drawer file cabinet, a plan table, a plan rack, and bookcase.

Retain subparagraph below for large projects with long construction periods.

Revise subparagraph below to suit Project; requirements are minimal.

Provide a room of not less than 240 sq. ft. (22.5 sq. m) for Project meetings.  Furnish room with conference table, 8 folding chairs, and 4-foot- (1.2-m-) square tack board.

Expand paragraph below to suit Project.

        - Storage and Fabrication Sheds:  Provide sheds sized, furnished, and equipped to accommodate materials and equipment involved, including temporary utility services.  Sheds may be open shelters or fully enclosed spaces within building or elsewhere on-site.

Review first subparagraph below with Owner's insurance carrier.  Revise to suit Project.

Delete paragraph below for low-rise construction of less than three stories.

        - Lifts and Hoists:  Provide facilities for hoisting materials and personnel.  Truck cranes and similar devices used for hoisting materials are considered "tools and equipment" and not temporary facilities.

Paragraph below is simplest method of specifying temporary elevator usage.  If provisions must be contained in this Section, transfer provisions from Division 14 Sections for elevators and cross-reference this Section.

Retain paragraph above or paragraph and subparagraph below.  Delete below if elevators are not available or their use is not permitted even if available.  Indicate location of Owner's existing elevators in Division 1 Section "Work Restrictions" or show on Drawings.

Retain paragraph above or paragraph and subparagraph below.  Delete below if stairs are not available or their use is not permitted even if available.  Indicate location of Owner's existing stairs in Division 1 Section "Work Restrictions" or show on Drawings.

Individual Project circumstances may require use of other construction aids and miscellaneous facilities, such as scaffolds, platforms, swing stages, ramps and bridges, incidental sheeting and shoring, and demolition waste chutes.  Add requirements to suit Project.  See Evaluations.

SECURITY AND PROTECTION FACILITIES INSTALLATION

        - Environmental Protection: Provide protection, operate temporary facilities, and conduct construction in ways and by methods that comply with environmental regulations and that minimize possible air, waterway, and subsoil contamination or pollution or other undesirable effects.  Avoid using tools and equipment that produce harmful noise.  Restrict use of noisemaking tools and equipment to hours that will minimize complaints from persons or tenants near Project site.

Insert local code references for environmental protection.  Consider indicating hours when noisemaking activities are prohibited.

Retain paragraph below because enclosure fence does not always provide adequate security against theft and vandalism.

        - Security Enclosure and Lockup: Install substantial temporary enclosure around partially completed areas of construction.  Provide lockable entrances to prevent unauthorized entrance, vandalism, theft, and similar violations of security.

        - Barricades, Warning Signs, and Lights: Comply with standards and code requirements for erecting structurally adequate barricades.  Paint with appropriate colors, graphics, and warning signs to inform personnel and public of possible hazard.  Where appropriate and needed, provide lighting, including flashing red or amber lights.

Review subparagraph below with Owner's insurance carrier.  Revise to suit Project.

Delete paragraph and subparagraphs below where covered walkways are not required and area is sufficient to conduct operations, including delivery of materials.  Include installation details on Drawings.

Retain paragraph and subparagraphs below.  Temporary enclosures are required on most projects at some time during construction.  Revise to suit Project.

        - Temporary Enclosures: Provide temporary enclosures for protection of construction, in progress and completed, from construction operations, and similar activities.

Paragraph and subparagraphs below specify currently accepted requirements.  Revise to suit local conditions.  See Evaluations.

        - Temporary Fire Protection: Until fire-protection needs are supplied by permanent facilities, install and maintain temporary fire-protection facilities of types needed to protect against reasonably predictable and controllable fire losses.  Comply with NFPA 241.

Review subparagraphs and associated subparagraphs below with Owner's insurance carrier.  Revise to suit Project.

Provide fire extinguishers, installed on walls on mounting brackets, visible and accessible from space being served, with sign mounted above.

Field Offices: Class A stored-pressure water-type extinguishers.

Other Locations:  Class ABC dry-chemical extinguishers or a combination of extinguishers of NFPA-recommended classes for exposures.

Locate fire extinguishers where convenient and effective for their intended purpose; provide not less than one extinguisher on each floor at or near each usable stairwell.

Store combustible materials in containers in fire-safe locations.

Maintain unobstructed access to fire extinguishers, fire hydrants, temporary fire-protection facilities, stairways, and other access routes for firefighting.  Prohibit smoking in hazardous fire-exposure areas.

Supervise welding operations, combustion-type temporary heating units, and similar sources of fire ignition.

Permanent Fire Protection: At earliest feasible date in each area of Project, complete installation of permanent fire-protection facility, including connected services, and place into operation and use.  Instruct key personnel on use of facilities.

Develop and supervise an overall fire-prevention and first-aid fire-protection program for personnel at Project site.  Review needs with local fire department and establish procedures to be followed.  Instruct personnel in methods and procedures.  Post warnings and information.

Provide hoses for fire protection of sufficient length to reach construction areas.  Hang hoses with a warning sign stating that hoses are for fire-protection purposes only and are not to be removed.  Match hose size with outlet size and equip with suitable nozzles.

Retain subparagraph above or below.

When fire-suppression sprinkler systems or other permanent fire-protection systems are used, insert specific requirements.

OPERATION, TERMINATION, AND REMOVAL

First paragraph below is important if allowances for metered use of temporary facilities have been established.

        - Supervision:  Enforce strict discipline in use of temporary facilities.  To minimize waste and abuse, limit availability of temporary facilities to essential and intended uses.

        - Maintenance:  Maintain facilities in good operating condition until removal.  Protect from damage caused by freezing temperatures and similar elements.

Maintain operation of temporary enclosures, heating, cooling, humidity control, ventilation, and similar facilities on a 24-hour basis where required to achieve indicated results and to avoid possibility of damage.

Prevent water-filled piping from freezing.  Maintain markers for underground lines.

Snow removal: Provide snow removal necessary to do the work and maintain access to materials and temporary facilities.

        - Flooring Protection: Protect flooring against mars, marks, indentations, and other damage from construction operations and placement of equipment and fixtures during construction period.  Use protection methods indicated or recommended by flooring manufacturer.

Cover flooring with undyed, untreated building paper at high traffic areas until inspection for Substantial Completion.

Do not move heavy and sharp objects directly over flooring.  Place plywood or hardboard panels over flooring and under objects while they are being moved.  Slide or roll objects over panels without moving panels.

        - Restoration of Roadways and Pavement: Roadways, pavements and curbs that are broken, damaged, settled, or otherwise defective as a result of receiving, handling, storage of materials or the performance of any work under this Contract, shall be fully restored to the satisfaction of the authorities having jurisdiction.

Delete paragraph below if not required.

Revise first paragraph below if it does not represent desired arrangement.

        - Termination and Removal: Remove each temporary facility when need for its service has ended, when it has been replaced by authorized use of a permanent facility, or no later than Substantial Completion.  Complete or, if necessary, restore permanent construction that may have been delayed because of interference with temporary facility.  Repair damaged Work, clean exposed surfaces, and replace construction that cannot be satisfactorily repaired.

Materials and facilities that constitute temporary facilities are the property of Contractor.  Owner reserves right to take possession of Project identification signs.

Consider inserting specific removal requirements, as illustrated below.

At Substantial Completion, clean and renovate permanent facilities used during construction period.  Comply with final cleaning requirements in Division 1 Section "Closeout Procedures."

Review final draft of this Section with Owner.  Advise Owner that any exceptions to its provisions might translate into costs borne by Owner.

END OF SECTION 01500