Copyright 2002, The American Institute of Architects (AIA)

SECTION 05500

METAL FABRICATIONS

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

RELATED DOCUMENTS

A.	Drawings and general provisions of the Contract, including General and Supplementary 				Conditions and Division 1 Specification Sections, apply to this Section.

SUMMARY

A.	This Section includes the following:

Steel framing and supports for the following:

a.	Steel framing and supports for mechanical and electrical equipment.

b.	Steel framing and supports for applications where framing and supports are not 			specified in other Sections.

Rough hardware.

B.	Products finished, but not installed, under this Section include the following:

List below only products, construction, and equipment that the reader might expect to find in this Section but are specified elsewhere.

Tube Steel Supports.

Anchor Bolts.

C.	Related Sections include the following:

1.	Division 6, section "Rough Carpentry" for metal framing anchors.

2.	Division 6, section "Finish Carpentry."

SUBMITTALS

A.	General:  Submit in accordance with Section 01330.

B.	Product date for the following:

1.	Paint products.

C.	Shop drawings:  Show fabrication and installation details for railings and metal fabrications.

1.	Include plans, elevations, sections, and details of metal fabrications and their 							connections.  Show anchorage and accessory items.

2.	Provide templates for anchors and bolts specified for installation under other Sections.

3.	For installed products indicated to comply with design loads, include structural analysis 				data signed and sealed by the qualified professional engineer responsible for their 					preparation.

D.	Welding certificates: Signed by Contractor certifying that welders comply with requirements 			specified under "Quality Assurance" article.

1.04	QUALITY ASSURANCE

A.	Fabricator Qualifications: Firm experienced in producing metal fabrications similar to those				indicated for this Project with a record of successful in-service performance, and with sufficient 			production capacity to produce required units without delaying the Work.

B. 	Welding: Qualify procedures and personnel according to the following:

1.	AWS d1.1, "Structural Welding Code--Steel."

2.	AWS D1.3, "Structural Welding Code--Sheet Steel."

1.05	COORDINATION

A.	Coordinate installation of anchorages for metal fabrications. Furnish setting drawings, tem				plates, and directions for installing anchorages, including sleeves, concrete inserts, anchor bolts, 		and items with integral anchors, that are to be embedded in concrete or masonry. Deliver such 			items to Project site for installation.

PRODUCTS

MANUFACTURERS

A.	In other Part 2 articles where titles below introduce lists, the following requirements apply to 			product selection:

1.	Products:  Submit to compliance with requirements; provide one of the products 						specified.

METALS - GENERAL

A.	Metal Surfaces:  Provide materials with smooth, flat services, unless otherwise indicated. For 			metal fabrications exposed to view in the completed Work, provide materials without seam 				marks, roller marks, rolled trade names, or blemishes.

FERROUS METALS

A.	Retain material types, qualities, and grades in this Article that are indicated in Specifications or on Drawings for each fabrication type.  Add or delete items to suit Project.

Steel Plates, Shapes, and Bars:  ASTM A 36/A 36M, standard weight (Schedule 40), unless 			another weight is indicated or required by structural loads.

1.	Black finish, unless otherwise indicated.

2.	Galvanized finish for exterior installations and where indicated.

B.	Round steel tubing and pipe are sized differently.  Tubing is designated by OD and wall thickness.  Pipe is designated by nominal pipe size and weight or schedule number.  See Evaluations.

Steel Pipe:  ASTM A 53/A 53M, standard weight (Schedule 40), unless another weight is 				indicated or required by structural loads.

1.	Black finish, unless otherwise indicated.

2.	Galvanized finish for exterior installations and where indicated.

FASTENERS

A.	Usually select Type 304 in paragraph below; select Type 316 if required for corrosive environments.

General:  Unless otherwise indicated, provide Type 304 stainless-steel fasteners for exterior use 		and zinc-plated fasteners with coating complying with ASTM B 633, Class Fe/Zn 5, at exterior 			walls.

A.	Delete remainder of this Article unless there are specific requirements for these types of fasteners.  Revise paragraph below if ASTM A 325 bolts are required for connecting miscellaneous steel framing and supports.

Steel Bolts and Nuts:  Regular hexagon-head bolts, ASTM A 307, Grade A (ASTM F 568M, Property Class 4.6); with hex nuts, 				ASTM A 563 (ASTM A 563M); and, where indicated, flat washers.

B.	Select Alloy Group 1 (A1) in first paragraph below for use with Type 304; select Alloy Group 2 (A4) for use with Type 316.

Stainless-Steel Bolts and Nuts:  Regular hexagon-head annealed stainless-steel bolts, nuts and, 			where indicated, flat washers; ASTM F 593 (ASTM F 738M) for bolts and ASTM F 594 (ASTM F 836M) for nuts, Alloy Group 1 (A1).

C.	Anchor Bolts: ASTM F 1554, Grade 36.

1.	Provide hot-dip or mechanically deposited, zinc-coated anchor bolts where item being 				fastened is indicated to be galvanized.

D.	Eyebolts:  ASTM A 489.

E.	Machine Screws: Flat Head, ASME B18.6.1.

F.	Lag Bolts:  ASME B18.2.1 (ASME B18.2.3.8M).

G.	Wood Screws:  Flat head, ASME B18.6.1.

H.	Plain Washers:  Round, ASME B18.22.1 (ASME B18.22M).

I.	Lock Washers:  Helical, spring type, ASME B18.21.1 (ASME B18.21.2M).

J.	Expansion Anchors:  Anchor bolt and sleeve assembly with capability to sustain, without 				failure, a load equal to six times the load imposed when installed in unit masonry and four 				times the load imposed when installed in concrete, as determined by testing according to 				ASTM E 488, conducted by a qualified independent testing agency.

1.	Material for Anchors in Interior Locations:  Carbon-steel components zinc-plated to 					comply with ASTM B 633, Class Fe/Zn 5.

2.	Subparagraph above and below are examples only.  Material above protects against 					corrosion in an indoor atmosphere; revise to suit other conditions after verifying 						availability of thicker coatings.  In subparagraph below, Alloy Group 1 (A1) refers to 				Type 304 and similar alloys, and Alloy Group 2 (A4) refers to Type 316 and similar 					alloys.

3.	Material for Anchors in Exterior Locations:  Alloy Group 1 (A1)  stainless steel bolts 						complying with ASTM F 593 (ASTM F 738M) and nuts complying with ASTM F 594 (ASTM F 836M).

MISCELLANEOUS MATERIALS

A.	Universal Shop Primer:  Fast-curing, lead- and chromate-free, anti-corrosive, universal 					modified alkyd primer complying with MPI#79.

B.	VOC limit in optional text below is the EPA limit for rust-preventive architectural coatings.

Use primer with a VOC content of 400 g/L or less to comply with the State of Maine 					Department of Environmental Protection Regulation, "Chapter 151: Architectural and Industrial 		Maintenance (AIM) Coatings."

C.	Delete first paragraph below if no galvanized fabrications.

Galvanizing Repair Paint:  High-zinc-dust-content paint for regalvanizing welds in steel, 				complying with SSPC-Paint 20.

D.	Bituminous Paint:  Cold-applied asphalt emulsion complying with ASTM D 1187.

Delete paragraph below if not required for concrete-filled bollards, footings for bollards, or wheel guards.

FABRICATION, GENERAL

A.	Shop Assembly:  Preassemble items in shop to greatest extent possible.  Disassemble units only 		as necessary for shipping and handling limitations.  Use connections that maintain structural 			value of joined pieces.  Clearly mark units for reassembly and coordinated installation.

B.	Form metal fabrications from materials of size, thickness, and shapes indicated but not less than 		needed to comply with performance requirements indicated.  Work to dimensions indicated or 			accepted on shop drawings, using proven details of fabrication and support.  Use type of 				materials indicated or specified for various components of each metal fabrication.

C.	Cut, drill, and punch metals cleanly and accurately.  Remove burrs and ease edges to a radius of 		approximately 1/32-inch (1 mm), unless otherwise indicated.  Remove sharp or rough areas on exposed 			surfaces.

D.	Form bent-metal corners to smallest radius possible without causing grain separation or 				otherwise impairing work.

E.	Form exposed work true to line and level with accurate angles and surfaces and straight edges.

F.	Weld corners and seams continuously to comply with the following:

1.	Use materials and methods that minimize distortion and develop strength and corrosion 				resistance of base metals.

2.	Obtain fusion without undercut or overlap.

3.	Remove welding flux immediately.

4.	At exposed connections, finish exposed welds and surfaces smooth and blended so no 				roughness shows after finishing and contour of welded surface matches that of adjacent 				surface.

G.	Form exposed connections with hairline joints, flush and smooth, using concealed fasteners 			where possible.  Where exposed fasteners are required, use Phillips flat-head (countersunk) 				screws or bolts, unless otherwise indicated.  Locate joints where least conspicuous.

H.	Fabricate seams and other connections that will be exposed to weather in a manner to exclude 			water.  Provide weep holes where water may accumulate.

I.	Cut, reinforce, drill, and tap metal fabrications as indicated to receive finish hardware, screws, 			and similar items.

J.	Provide for anchorage of type indicated; coordinate with supporting structure.  Space anchoring 		devices to secure metal fabrications rigidly in place and to support indicated loads.  Cut, 				reinforce, drill, and tap metal fabrications as indicated to receive finish hardware, screws, and 			similar items.

MISCELLANEOUS FRAMING AND SUPPORTS

A.	General:  Provide steel framing and supports for applications indicated that are not specified in 			other Sections as needed to complete the Work.

B.	Fabricate units from steel shapes, plates, and bars of welding construction, unless otherwise 			indicated. Fabricate to sizes, shapes, and profiles indicated and as necessary to receive adjacent 			construction retained by framing and supports. Cut, drill, and tap units to receive hardware, 				hangers, and similar items.

ROUGH HARDWARE

A.	Furnish bent or otherwise custom-fabricated, bolts, plates, anchors, hangers, dowels, and other 			miscellaneous steel and iron shapes as required for framing and supporting woodwork, and for 			anchoring or securing woodwork to concrete or other structures.  Straight bolts and other stock 			rough hardware items are specified in Division 6 Sections.

B.	Fabricate items to sizes, shapes, and dimensions required.  Furnish malleable-iron washers for 			heads and nuts that bear on wood structural connections, and furnish steel washers elsewhere.

FINISHES, GENERAL

A.	Comply with NAAMM's "Metal Finishes Manual for Architectural and Metal Products" for 			recommendations for applying and designating finishes.

B.	Finish metal fabrications after assembly.

STEEL AND IRON FINISHES

A.	Galvanizing:  Provide coating for iron and steel fabrications applied by the hot-dip process, 				0.05 - 0.09% nickel content, Deltagalv by Duncan Galvanizing or approved equal.  Provide 				thickness of galvanizing specified in referenced standards.  Hot-dip galvanize items as 					indicated to comply with applicable standard listed below:

1.	ASTM A 123/A 123M, for galvanizing both fabricated and unfabricated steel and iron 				products made of uncoated rolled, pressed, and forged shapes, plates, bars, and strip 					0.0299 inch thick or thicker.

2.	ASTM A 153/A 153M, for galvanizing steel and iron hardware.

B.	Preparation for Shop Priming:  Prepare uncoated ferrous-metal surfaces to comply with 				minimum requirements indicated below for SSPC surface preparation specifications and 				environmental exposure conditions of installed metal fabrications:

C.	Retain or revise both subparagraphs below to suit Project service conditions of installed work.  Insert other exposures and preparation requirements where applicable.  Refer to SSPC's painting manual.  Both subparagraphs apply to locations that would normally remain dry in service.

Exteriors (SSPC Zone 1B):  SSPC-SP 6/NACE No. 3, "Commercial Blast Cleaning."

Interiors (SSPC Zone 1A):  SSPC-SP 3, "Power Tool Cleaning."

D.	Shop Priming:  Apply shop primer to uncoated surfaces of metal fabrications, except those with 		galvanized finishes and those to be embedded in concrete, sprayed-on fireproofing, or masonry, 		unless otherwise indicated.  Comply with SSPC-PA 1, "Paint Application Specification No. 1: 			Shop, Field, and Maintenance Painting of Steel," for shop painting.

E.	Delete subparagraph below if not required.  Stripe painting adds cost but helps ensure that hard-to-reach areas, such as crevices, inside corners, and welds, are thoroughly coated and that sharp edges (which are vulnerable to chipping and are where the film may be thinner due to surface tension) receive adequate coverage.

Stripe paint corners, crevices, bolts, welds, and sharp edges.

EXECUTION

PREPARATION

A.	Coordinate and furnish anchorages, setting drawings, diagrams, templates, instructions, and 			directions for installing anchorages, including concrete inserts, sleeves, anchor bolts, and 				miscellaneous items having integral anchors that are to be embedded in concrete or masonry 			construction. Coordinate delivery of such items to Project site.

B.	Set sleeves in concrete with tops flush with finish surface elevations. Protect sleeves from water 		and concrete entry.

INSTALLATION, GENERAL

A.	Cutting, Fitting, and Placement:  Perform cutting, drilling, and fitting required for installing 			metal fabrications.  Set metal fabrications accurately in location, alignment, and elevation; with 			edges and surfaces level, plumb, true, and free of rack; and measured from established lines and 		levels.

B.	Fit exposed connections accurately together to form hairline joints. Do not weld, cut, or abrade 			surfaces of exterior units that have been hot-dip galvanized after fabrication and are intended 			for bolted or screwed field connections.

C.	Fastening to In-Place Construction:  Provide anchorage devices and fasteners where metal 				fabrications are required to be fastened to in-place construction.  Provide threaded fasteners for 			use with concrete and masonry inserts, toggle bolts, through bolts, lag bolts, wood screws, and 			other connectors.

Delete articles below not applicable to Project.  Insert others where needed to specify requirements applicable to a specific item not covered under general installation requirements above.

Delete paragraph below if bollards have metal caps.

ADJUSTING AND CLEANING

A.	Touchup Painting:  Immediately after erection, clean field welds, bolted connections, and 				abraded areas.  Paint uncoated and abraded areas with the same material as used for shop 				painting to comply with SSPC-PA 1 for touching up shop-painted surfaces.

B.	Retain paragraph and subparagraph above if touchup painting is included in this Section.  Retain first paragraph below if it is specified in Division 9 painting Sections.  Revise reference if another Division 9 Section, such as "High-Performance Coatings," is used.

Galvanized Surfaces:  Clean field welds, bolted connections, and abraded areas and repair 				galvanizing to comply with ASTM A 780.

END OF SECTION 05500