# SECTION 06200

# FINISH CARPENTRY

# PART 1 - GENERAL

# 1.01	RELATED DOCUMENTS

- Drawings and general provisions of Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

# 1.02	SUMMARY

- This Section includes the following:

  - Shelving & clothes rods

  - Window sills and aprons.

B.	Related Sections include the following

1.	Division 6 Section “Rough Carpentry” for blocking and other carpentry work not exposed to view.

2.	Division 6 Section “Architectural Woodwork” for shop-fabricated casework, countertops, and interior woodwork not specified in this Section.

3.	Division 9 Sections for sinks, plumbing fittings and venting connections installed in casework.

1.03	DEFINITIONS

- Inspection agencies and the abbreviations used to reference them, including the following:

1.	NELMA – Northeastern Lumber Manufacturers Association.

2.	NLGA – National Lumber Grades Authority

3.	WCLIB – West Coast Lumber Inspection Bureau

4.	WWPA – Western Wood Products Association

1.04	SUBMITTALS

- General:  Submit in accordance with Section 01330.

B.	Product Data:  For each type of process and factory fabricated product. Include construction details, material descriptions, dimensions of individual components and profiles, textures, and colors. Include construction and application details.

C.	Shop Drawings:  Show location of each item, dimensioned plans and elevations, large-scale details, attachment devices, and other components.

1.	Show details full size

2.	Show locations and sizes of blocking and hanging strips, including concealed blocking and reinforcement specified in other Sections.

# 1.05	QUALITY ASSURANCE

- Quality Standard:  Unless otherwise indicated, comply with Awes “Architectural Woodwork Quality Standards” for grades of interior architectural woodwork, construction, finishes, and other requirements.

- Installer Qualifications:  Engage an experienced installer who has completed finished carpentry similar in material, design, and extent to that indicated for this Project and with a record of successful in-service performance.

- Fire-Test-Response Characteristics:  Where fire-retardant materials are indicated, provide materials with specified fire-test-response characteristics as determined by a testing and inspecting agency acceptable to authorities having jurisdiction. Identify materials with appropriate markings of applicable testing and inspecting agency on surfaces of materials that will be concealed from view after installation. Materials shall meet the following requirements when tested in compliance with ASTM E84.

  - Flame Spread:  25 or less

  - Smoke Developed:  450 or less

  - DELIVERY, STORAGE, AND HANDLING

- Keep materials under cover, off ground and dry. Protect materials against weather and contact with damp or wet surfaces. Stack lumber, plywood and other panels. Provide for air circulation within and around stacks and under temporary coverings.

- Deliver interior finish carpentry only when environmental conditions meet requirements specified for installation areas. If finish carpentry must be stored in other than installation areas, store only where environmental conditions meet requirements specified for installation areas.

  - PROJECT CONDITIONS

A.	Environmental Limitations:  Do not deliver or install finish carpentry until building is enclosed and weatherproof, wet work in space is completed and nominally dry, and provisions are made to maintain temperature and relative humidity at occupancy levels during the remainder of the construction period.

B.	Weather Limitations:  Proceed with installation only when existing and forecasted weather conditions permit work to be performed according to manufacturer’s written instructions and warranty requirements and at least one coat of specified finish to be applied without exposure to rain, snow or dampness.

C.	Do not install finish carpentry materials that are wet, moisture damaged, or mold damaged.

Indications that materials are wet or moisture damaged include, but are not limited to discoloration, sagging or irregular shape. Indications that materials are mold damaged include, but are not limited to, fuzzy or splotchy surface contamination and discoloration.

  - COORDINATION

A.	Coordinate sizes and locations of framing, blocking, reinforcements, and other related units of Work specified in other Sections to ensure that interior architectural woodwork and casework can be supported and installed as indicated.

PART 2 – PRODUCTS

  - MANUFACTURERS

- In other Part 2 articles where titles below introduce lists, the following requirements apply to product selection:

  - Manufacturers: Subject to compliance with requirements, provide products by one of the manufacturers specified.

  - Products: Subject to compliance with requirements, provide one of the products specified.

  - MATERIALS – GENERAL

- Lumber: DOC PS 20 and applicable grading rules of inspection agencies certified by the American Lumber Standards’ Committee Board of Review.

- Softwood Plywood: DOC PS 1, Medium Density Overlay (MDO), “U.S. Product Standard for Construction and Industrial Plywood.”

- Hardwood Plywood: HPVA HP-1, 7 ply core, no voids, Grade A veneers, “Interim Voluntary Standard for Hardwood and Decorative Plywood.”

- Particleboard: ANSI A208.1, Grade M-2.

- Thermoset Decorative Panels (Melamine): Particleboard or medium-density fiberboard finished with thermally fused, melamine-impregnated decorative paper complying with LMS SAT-1, fused to core using average pressure of 320 psi and average temperature of 320 degrees Fahrenheit.

  - Provide PVC or polyester edge banding complying with LMA EDG-1 on components with exposed or semi-exposed edges.

  - SHELVING AND CLOTHES RODS

- Shelving for Storage Closets:

    - Shelves:  Thermoset decorative panels (melamine) on particleboard, ¾-inch thick minimum, with PVC edges on both faces and ends.

    - Shelf Brackets and Standards:  Twin slotted, heavy-duty, steel shelf standards and U-shaped, double prong, heavy-duty steel brackets, white powder coat finish.

    - Product:  Standard No. E3200 and bracket No. E3210; Knape & Vogt Mfg. Co.

B.	Coat Closet Shelving:  ¾ inch hardwood plywood or MDO with solid-wood front edge.

1.	Shelf Cleats: ¾ by 5 ½ inch boards with holes to receive clothes rods, of same species and 				grade indicated above for interior lumber trim for opaque finish.

C.	Clothes Rods:  1 ½ inch diameter, clear, kiln-dried hardwood rods.

1.	Rod Flanges: Clear, kiln-dried white maple turnings.

2.04	WINDOW SILLS

A.	Window Sills (Stools) and Aprons: Fabricate to AWI Custom Grade, from solid hardwood, in 			profile indicated for stain finish.

1.	Species: Walnut

2.       Provide stained sample prior to installation. Verify stain color with architect.

2.05	MISCELLANEOUS MATERIALS

A.	Fasteners for Interior Finish Carpentry: Nails, screws, and other anchoring devices of type, size, 			material, and finish required for application indicated to provide secure attachment, concealed 			where possible.

2.06	FABRICATION FOR WOOD PRODUCTS

A.	Quality Standards:  Unless otherwise indicated, comply with Awes "Architectural Woodwork 			Quality Standards."

B.	Wood Moisture Content:  Comply with requirements of specified inspection agencies and with 			manufacturer's written recommendations for moisture content of finish carpentry at relative 			humidity conditions existing during time of fabrication and in installation areas.

C.	Ease edges of lumber less than 1 inch in nominal thickness to 1/16-inch radius and edges of 			lumber 1-inch or more in nominal thickness to 1/8-inch radius.

PART 3 - EXECUTION

3.01	EXAMINATION

A.	Examine substrates, with Installer present, for compliance with requirements for installation 			tolerances and other conditions affecting performance. Proceed with installation only after 				unsatisfactory conditions have been corrected.

3.02	PREPARATION

A.	Clean substrates of projections and substances detrimental to application.

B.	Before installing finish carpentry and manufactured cabinetry, condition materials to average 			prevailing humidity in installation areas for a minimum of 24 hours, unless longer conditioning is 			recommended by manufacturer.

3.03	INSTALLATION - GENERAL

A.	Do not use materials that are unsound, warped, improperly treated or finished, inadequately 			seasoned, or too small to fabricate with proper jointing arrangements.

1.	Do not use manufactured units with defective surfaces, sizes, or patterns.

B.	Install finish carpentry level, plumb, true, and aligned with adjacent materials. Use concealed 			shims where necessary for alignment.

1.	Scribe and cut finish carpentry to fit adjoining work. Refinish and seal cuts as recommended 			by manufacturer.

2.	Countersink fasteners, fill surface flush, and sand where face fastening is unavoidable.

3.	Install to tolerance of 1/8-inch in 96 inches for level and plumb. Install adjoining finish 				carpentry with 1/32-inch maximum offset for flush installation and 1/16-inch maximum 				offset for reveal installation.

4.	Coordinate finish carpentry with materials and systems in or adjacent to it. Provide cutouts 				for mechanical and electrical items that penetrate finish carpentry.

5.	Refer to Division 9 Section "PAINTING" for final finishing of finish carpentry.

3.04	STANDING AND RUNNING INTERIOR WOOD TRIM INSTALLATION

A.	Install with minimum number of joints practical, using full-length pieces from maximum lengths 			of lumber available. Do not use pieces less than 24-inches long, except where necessary. Stagger 			joints in adjacent and related standing and running trim. Cope at returns and miter at corners to 			produce tight-fitting joints with full-surface contact throughout length of joint. Use scarf joints for 			end-to-end joints. Plane backs of casings to provide uniform thickness across joints, where 			necessary for alignment.

1.	Drill pilot holes in hardwood before fastening to prevent splitting. Fasten to prevent 					movement or warping. Countersink fastener heads on exposed carpentry work and fill holes.

3.05	SHELVING AND CLOTHES ROD INSTALLATION

A.	Cut shelf cleats at ends of shelves about ½ inch less than width of shelves and sand exposed ends 			smooth.

B.	Install shelf cleats by fastening to framing or backing with finish nails or trim screws, set below 			face and filled. Space fasteners not more than 16-inches o.c. Use 2 fasteners at each framing 			member or fastener location for cleats 4-inches nominal in width and wider.

1.	Apply a bead of multipurpose construction adhesive to back of shelf cleats right before 				installing. Remove adhesive tat is squeezed out immediately after fastening shelf cleats in 				place.

C.	Install standards for adjustable shelf brackets according to manufacturer's written instructions, 			spaced not more than 36-inches o.c. and within 6-inches of end of shelves. Fasten to framing 			members, blocking, or metal backing, or use toggle bolts or hollow wall anchors.

D.	Cut shelves to neatly fit openings with only enough gap to allow shelves to be removed and 			reinstalled. Install shelves, fully seated on cleats, brackets, and supports.

1.	Fasten shelves to cleats with finish nails or trim screws, set flush.

2.	Fasten shelves to brackets to comply with bracket manufacturer's written instructions.

3.06	ADJUSTING

A.	Replace finish carpentry that is damaged or does not comply with requirements. Finish carpentry 			may be repaired or refinished if work complies with requirements and shows no evidence of repair 		or refinishing. Adjust joinery for uniform appearance.

3.07	CLEANING

A.	Clean finish carpentry and manufactured casework on exposed and semi-exposed surfaces. Touch-			up factory applied finishes to restore damaged or soiled areas.

3.08	PROTECTION

A.	Provide final protection and maintain conditions that ensure finish carpentry and manufactured 			casework are without damage or deterioration at time of Substantial Completion.

END OF SECTION 06200