# SECTION 06400

# ARCHITECTURAL WOODWORK

# PART 1 - GENERAL

# 1.01	RELATED DOCUMENTS

- Drawings and general provisions of Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

# 1.02	SUMMARY

- This Section includes the following:

  - Custom interior standing and running trim.

  - Custom wood casework.

  - Plastic-laminate countertops.

  - Interior ornamental work.

  - Wood borrowed lites.

  - Shelving.

  - Shop finishing interior woodwork.

  - Solid surfacing countertop.

B.	Related Sections include the following

1.	Division 6 Section “Rough Carpentry” for wood furring, clocking, shims, and hanging strips required for installing woodwork and concealed within other construction before woodwork installation.

2.	Division 6 Section “Finish Carpentry” for stock standing and running trim, and interior carpentry exposed to view that is not specified in this Section.

3.	Division 9 Section "Painting" for field finishing of interior architectural woodwork, trim and wainscoting.

4.	Division 12 Section "Residential Casework" for manufactured cabinets and associated moldings and panels to match cabinets.

5.	Division 15 Sections for sink units mounted in countertops and for plumbing connections of appliances installed in casework.

6.	Division 16 Sections for conduit and connections installed in casework.

1.03	DEFINITIONS

A.	Interior architectural woodwork includes wood furring, blocking, shims, and hanging strips for 			installing woodwork items, unless concealed within other construction before woodwork 				installation.

B.	Exposed Surfaces of Casework: Surfaces visible when doors and drawers are closed, including 			visible surfaces in open cabinets or behind glass doors.

C.	Semi-exposed Surfaces of Casework: Surfaces behind opaque doors or drawer fronts, including 			interior faces of doors and interiors and sides of drawers. Bottoms of wall cabinets are defined as 			"semi-exposed".

D.	Concealed Surfaces of Casework: Surfaces not usually visible after installations, including 			sleepers, web frames, dust panels, bottoms of drawers, and ends of cabinets installed directly 			against and completely concealed by walls or other cabinets. Tops of wall cabinets and tall 			cabinets are defined as "concealed".

1.04	SUBMITTALS

- General:  Submit in accordance with Section 01330.

B.	Product Data:  For each type of product indicated, including cabinet hardware and accessories, and finishing materials and processes.

C.	Shop Drawings:  Show location of each item, dimensioned plans and elevations, large-scale details, attachment devices, and other components.

1.	Show details full size.

2.	Show locations and sizes of furring, blocking and hanging strips, including concealed blocking and reinforcement specified in other Sections.

3.	Show locations and sizes of cutouts and holes for plumbing fixtures, faucets, and other items installed in architectural woodwork and countertops.

D.	Samples for Verifications for the following:

1.	Lumber and transparent finish, 5-inches wide by 24-inches long for each species and cut, finished on one side and one edge.

2.	Wood-veneer-faced panel products with or for transparent finish, 8-inches by 10-inches, for each species and cut. Include at least one face-veneer seam and finish as specified.

3.	Lumber and panel products with shop-applied opaque finish, 50 sq. in. for lumber and 8-inches by 10-inches for panels, for each finish system and color, with exposed surface finished.

4.	Plastic-laminate-clad panel products, 8-inches by 10-inches, for each type, color, pattern, 				and surface finish.

5.	Exposed cabinet hardware and accessories, one unit for each type and finish.

# 1.05	QUALITY ASSURANCE

- Quality Standards:  Unless otherwise indicated, comply with “Architectural Woodwork Quality Standards” (AWI) for grades of interior architectural woodwork, construction, finishes, and other requirements.

1.	Contract Documents contain selections chosen from options in the Quality Standards as 			well as additional requirements beyond those of the Quality Standards. Comply with such 			selections and requirements in addition to the Quality Standards.

- Installer Qualifications:  Engage an experienced Installer who has completed architectural woodwork similar in material, design, and extent to that indicated for this Project and with a record of successful in-service performance.

- Fabricator Qualifications:  A firm experienced in producing architectural woodwork similar to that indicated for this Project and with a record of successful in-service performance, as well as sufficient production capacity to produce required units.

  - DELIVERY, STORAGE, AND HANDLING

- Protect woodwork during transit, delivery, storage, and handling to prevent damage, soiling, and deterioration.

- Deliver interior finish carpentry only when environmental conditions meet requirements specified for installation areas. If finish carpentry must be stored in other than installation areas, store only where environmental conditions meet requirements specified for installation areas.

  - PROJECT CONDITIONS

A.	Environmental Limitations:  Do not deliver or install finish carpentry until building is enclosed and weatherproof, wet work in space is completed and nominally dry, and provisions are made to maintain temperature and relative humidity at occupancy levels during the remainder of the construction period.

B.	Weather Limitations:  Proceed with installation only when existing and forecasted weather conditions permit work to be performed according to manufacturer’s written instructions and warranty requirements and at least one coat of specified finish to be applied without exposure to rain, snow or dampness.

C.	Do not install finish carpentry materials that are wet, moisture damaged, or mold damaged.

Indications that materials are wet or moisture damaged include, but are not limited to discoloration, sagging or irregular shape. Indications that materials are mold damaged include, but are not limited to, fuzzy or splotchy surface contamination and discoloration.

  - COORDINATION

A.	Coordinate sizes and locations of framing, blocking, reinforcements, and other related units of Work specified in other Sections to ensure that interior architectural woodwork and casework can be supported and installed as indicated.

PART 2 – PRODUCTS

  - MATERIALS

A.	General:  Provide materials that comply with requirements of the AWI quality standard for each 			type of woodwork and quality grade specified, unless otherwise indicated.

B.	Wood Species and Cut for Transparent Finish:  Walnut, plain sawn and sliced, unless otherwise 			noted.

C.	Wood Species for Opaque Finish:  Any closed-grain hardwood.

D.	Wood Products - Comply with the following:

1.	Medium-Density Fiberboard: ANSI A208.2, Grade MD-21, 45 lb. density.

2.	Particleboard: ANSI A208.1, Grade M-2.

a.	Provide water-resistant particleboard within 2'-0" of sinks.

3.	Hardwood Plywood and Face Veneers: HPVA HP-1, 7-ply core, no voids, Grade A 				veneers.

E.	Thermoset Decorative Overlay (Melamine): Particleboard complying with ANSI A208.1, Grade 			M-2, or medium-density fiberboard complying with ANSI A208.2, Grade MD, with LMA SAT-1, 			fused to core using average pressure of 320 psi and average temperature of 320 degrees 				Fahrenheit.

1.	Color: As indicated; if not indicated, as selected by Architect from manufacturer's full 				range of options.

F.	Clear Tempered Float Glass for Borrowed Lites:  ASTM C 1048, Kind FT, Condition A, Type 1, 			Class 1, Quality q3; manufactured by horizontal (roller hearth) process, with exposed edges 			seamed before tempering, 6mm thick, unless otherwise indicated.

G.	High-Pressure Decorative Laminate:  NEMA LD 3, grades as indicated, or if not indicated, as 			required by woodwork quality standard.

1.	Manufacturers: Wilsonart, Pionite.

2.	Colors, Patterns, and Finishes: As indicated on Interior Finish Legend.

H.	Edge-Banding for Melamine:  Rigid PVC extrusions, through color with satin finish, 3mm thick, 			with radiused edges. Hot melt adhesive application.

I.	Solid Surfacing Material, SS1:  Homogeneous solid sheets of filled plastic resign complying with 			material and performance requirements in ANSI Z124.3, for Type 6, without a pre-coated finish.

1.	Product:  Hanwha surfaces, Hanstone.

2.	Color, Pattern & Finish: As indicated on Interior Finish Legend.

J.	Solid Surfacing Material, SS2:  Homogeneous solid sheets of filled plastic resin complying with 			material and performance requirements in ANSI Z124.3, for Type 5 or Type 6, without a pre-			coated finish.

1.	Product:  Zodiaq Quartz Surfaces, DuPont Polymers.

2.	Color, Pattern, and Finish: As indicated on Interior Finish Legend.

  - CABINET HARDWARE

- Hardware Standard: Comply with BHMA A156.9 for items indicated by referencing BHMA numbers of items referenced to this standard.

- Adjustable Shelf Standards and Supports:

1.	Twin slotted, heavy duty, steel shelf standards and U-shaped, double prong, heavy duty 			steel brackets, and shelf rests/locators with fasteners; white powder finish, unless 				otherwise indicated.

a.	Bracket Size:  Varies as required for location; coordinated with Drawings.

b.	Product: Standard No. E3200 WH, Bracket No. E3210 WH, Shelf Locator 				No. E3235 - Knape & Vogt Manufacturing Co.

- Counter Supports:  Angle brackets formed from 1/8-inch steel with multiple ¼-inch mounting holes, noted at leg intersection to allow wire run clearance; capable of supporting 1,000 lbs. minimum, factory primed for field finishing.

1.	Size: Varies as required for condition; coordinate with Drawings.

2.	Product: Work Station Brackets: A&M Hardware, Inc., tel (888) 647-0200, E-mail:  			info@aandmhardware.com

- Grommets for Cable Passage through Countertops: Molded plastic grommets and matching plastic caps with slot for wire passage; size determined during Shop Drawing Review; color selected by Architect.

1.	Manufacturer: Doug Mockett and Col, Inc. tel (800) 523-1269 E-mail: info@mockett.com;

Outwater Plastics tel (800) 631-8375

  - INSTALLATION MATERIALS

- Furring, Blocking, Shims, and Hanging Strips:  Softwood or hardwood lumber, kiln-dried to less than 15 percent moisture content.

B.	Screws:  Select material, type, size, and finish required for each use. Comply with ASME B 18.6.1 		for applicable requirements.

    - For metal framing supports, provide screw as recommended by metal-framing manufacturer.

C.	Nails:  Select material, type, size, and finish required for each use. Comply with FS FF-N-105 for 			applicable requirements.

D.	Anchors:  Select material, type, size, and finish required for each substrate for secure anchorage. 			Provide nonferrous-metal or hot-dip galvanized anchors and inserts on inside face of exterior walls 		and elsewhere as required for corrosion resistance. Provide toothed-steel or lead expansion sleeves 			for drilled-in-place anchors.

E.	Glue:  Aliphatic or Phlenolic resin wood glue recommended by manufacturer for general 				carpentry use.

2.04	FABRICATION - GENERAL

A.	Interior Woodwork Grade:  Provide materials that comply with requirements of the AWI quality 			standard for each type of woodwork and quality grade indicated. When quality grade is not 			indicated, provide Custom quality grade.

B.	Wood Moisture Content:  Comply with requirements of referenced quality standard for wood 			moisture content in relation to ambient relative humidity during fabrication and in installation 			areas.

C.	Fabricate woodwork to dimensions, profiles, and details indicated. Ease edges to radius indicated 			for the following:

1.	Edges of Sold Wood (Lumber) Members ¾-inch thick or less: 1/16-inch.

2.	Edges of Rails and Similar Members more than ¾-inch thick: 1/8-inch.

D.	Complete fabrication, including assembly, finishing, and hardware application, to maximum extent 		possible, before shipment to project site. Disassemble components only as necessary for shipment 			and installation. Where necessary for fitting at site, provide ample allowance for scribing, 				trimming and fitting.

E.	Shop cut openings, to maximum extent possible, to receive hardware, appliances, plumbing 			fixtures, electrical work, and similar items. Locate openings accurately and use templates or 			roughing-in diagrams to produce accurately sized and shaped openings. Sand edges of cut-outs to 			remove splinters and burrs.

1.	Seal edges for openings in countertops with a coat of water-resistant varnish.

F.	Install glass to comply with applicable requirements in Division 8 Section "Glazing" and in 			FGMAs "Glazing Manual". For glass in wood frames, secure glass with removable stops.

2.05	CUSTOM INTERIOR STANDING AND RUNNING TRIM FOR TRANSPARENT FINISH

A.	Quality Standard:  Comply with AWI Section 300.

B.	Grade:  Custom, walnut

C.	Backout or groove backs of flat trim members and kerf backs of other wide, flat members, except 			for members with ends exposed in finished work.

D.	Assemble casings in plant except where limitations of access to place of installation require field 			assembly.

E.	Assemble moldings in plant to maximum extent possible. Miter corners in plant and prepare for 			field assembly with bolted fittings designed to pull connections together.

F.	Wood Species:  Any closed-grain hardware.

2.06	WOOD CASEWORK FOR TRANSPARENT FINISH

A.	Quality Standard:  Comply with AWI Section 400 requirements for wood cabinets.

B.	Grade:  Custom.

C.	Wood Species and Cut for Exposed Surfaces:  Walnut, plain sawn or sliced.

1.	Grain matching:  run and match grain vertically for fixed panels.

2.	Matching of veneer leaves:  book match.

3.	Veneer matching with panel face:  balance match.

D.	Panel Product for Exposed Surfaces:  Hardwood veneer plywood.

E.	Exposed Casework Shelves:  Hardwood veneer core plywood, 1-inch thick with solid hardwood 			edging. Hardwood edging shall be thick enough to resist shelf bowing for designated span. All 			shelves shall be same thickness.

2.07	WOOD CASEWORK FOR OPAQUE FINISH

A.	Quality Standard:  Comply with AWI Section 400 requirements for wood cabinets.

B.	Grade:  Custom.

C.	Species for Exposed Surfaces:  Any closed-grain hardwood.

D.	Panel Product for Exposed Surfaces:  Hardwood plywood.

E.	Exposed Casework Shelves:  Hardwood veneer core plywood, 1-inch thick with solid hardwood 			edging. Hardwood edging shall be thick enough to resist shelf bowing for designated span. All 			shelves shall be same thickness.

2.08	PLASTIC-LAMINATE COUNTERTOPS

A.	Quality Standard:  Comply with AWI Section 400 requirements for wood cabinets.

B.	Grade:  Premium.

C.	High-Pressure Decorative Laminate Grade:  HGS.

D.	Colors, Patterns and Finishes:  Provide materials and products that result in colors and textures of 			exposed laminate surfaces complying with the following requirements:

1.	Match Architect's sample..

E.	Grain Direction:  Parallel to cabinet fronts.

F.	Edge Treatment:  Varies with location; coordinate with Drawings.

1.	Wood Edge with Transparent Finish: Solid walnut for transparent finish over stain; stain as 				selected by Architect.

2.	Plastic Laminate Edge: Same as laminate cladding on horizontal surfaces.

G.	Core Material:  Particleboard

1.	Core Material at Sink: Moisture resistant particleboard.

H.	Balance Sheet:  Phenolic laminate applied to the reverse side of plastic laminate finish.

I.	ADA Sink Areas:  In countertops with stepped areas for ADA sinks, construct depressed area and 			vertical sides with plywood substrate.  Face edge of tops shall be 1-inch wide minimum, fully 			covering substrate. No joints shall occur within 2-feet of a sink. Sand surfaces to which plastic 			laminate is to be bonded.

2.09	INTERIOR ORNAMENTAL WORK FOR TRANSPARENT FINISH

A.	Interior ornamental work for transparent finish includes, but is not limited to, the following:

1.	Chair rail.

2.	Wood base.

B.	Quality Standard:  Comply with AWI Section 700.

C.	Grade:  Custom.

D.	Wood Species and Cut:  Walnut, plain sawn or sliced

E. Provide stained sample prior to installation. Verify stain color with architect.

2.10	INTERIOR ORNAMENTAL WORK FOR OPAQUE FINISH

A.	Interior ornamental work for opaque finish includes, but is not limited to, the following:

1.	Existing Oak doors.

B.	Quality Standard:  Comply with AWI Section 700.

C.	Grade:  Custom.

D.	Wood Species:  Any closed-grain hardwood.

2.11	SHELVING

A.	Quality Standard:  Comply with AWI Section 600.

B.	Grade:  Custom.

C.	Utility Shelving:  Thermoset decorative overlay with 3mm PVC edge both faces and ends.

D.	Provide shelving in maximum available lengths.

2.12	INTERIOR BORROWED LITES

A.	Quality Standard:  Comply with AWI Section 1000.

B.	Grade:  Custom

C.	Wood Species for Transparent Finish:  Walnut, plain sliced for stained, transparent finish.

D.	Window Typed:  Fixed unit.

2.13	SOLID-SURFACING-MATERIAL COUNTERTOPS

A.	Grade:  Custom.

B.	Solid-Surfacing-Material thickness:  ¾ inch.

C.	Colors, Patterns, and Finish:  Provide materials and products that result in colors of solid-surfacing 		material complying with the following requirements:

1.	Match color, pattern, and finish as indicated by manufacturer's designations for these 				characteristics.

D.	Fabricate tops in one piece, unless otherwise indicated. Comply with solid-surfacing-material 			manufacturer's written recommendations for adhesives, sealers, fabrication, and finishing.

2.14	SHOP FINISHING

A.	Quality Standard:  Comply with AWI Section 1500, unless otherwise noted.

B.	General:  Priming and finishing of interior architectural woodwork required to be performed at 			fabrication shop are specified in this Section. Refer to Division 9 Section "Painting" for final 			finishing of installed architectural woodwork and for material and application requirements for 			woodwork not specified to receive final finish in this Section.

C.	Preparation for Finishing:  Comply with referenced quality standard for sanding, filling 				countersunk fasteners, sealing concealed surfaces, and similar preparations for finishing 				architectural woodwork, as applicable to each unit of work.

D.	Transparent Finish:  Comply with requirements indicated below for grade, finish system, color, 			effect, and sheen, with sheen measured on 60-degree gloss meter per ASTM D 523:

1.	Grade: Premium system for all casework grades.

2.	AWI Finish System TR-6: Catalyzed Polyurethane.

3.	Staining: Stain as selected by Architect.

4.	Sheen: Satin 30-50 gloss units

E.	Opaque Finish:  Comply with requirements indicated below for grade, finish system, color, effect, 			and sheen, with sheen measured on 60-degree gloss meter per ASTM D523:

1.	Grade: Premium system for all casework grades.

2.	AWI Finish System OP-4: Conversion Varnish.

3.	AWI Finish System OP-6: Catalyzed Polyurethane.

3.	Color: Match Architect's sample.

4.	Sheen: Semi-gloss 55-75 gloss units

PART 3 - EXECUTION

3.01	PREPARATION

A.	Condition woodwork to average prevailing humidity conditions in installation areas before 			installation.

B.	Before installing architectural woodwork, examine shop fabricated work for completion and 			complete work as required, including removal of backing and back printing.

3.02	INSTALLATION

A.	Quality Standard:  Install woodwork to comply with AWI Section 1700 for the same grade 			specified in Part 2 of this Section for type of woodwork involved.

B.	Install woodwork level, plumb, true, and straight. Shim as required with concealed shims. Install 			level and plumb (including tops) to a tolerance of 1/8-inch in 96-inches.

C.	Scribe and cut woodwork to fit adjoining work, and refinish cut surfaces and repair damaged 			finish at cuts.

D.	Anchor woodwork to anchors or blocking built in or directly attached to substrates. Secure with 			countersunk, concealed fasteners and blind nailing as required for complete installation. Use fine 			finishing nails for exposed fastening, countersunk and filled flush with woodwork and matching 			final finish if transparent finish is indicated.

E.	Custom Standing and Running Trim:  Install with minimum number of joints possible, using full-			length pieces (from maximum length of lumber available) to greatest extent possible. Do not use 			pieces less than 36-inches long, except where shorter single-length pieces are necessary. Scarf 			running joints and stagger in adjacent and related members.

1.	Fill gaps, if any, between top of base and wall with plastic wood filler, sand smooth, and 				finish same as wood base, if finished.

2.	Install standing and running trim with no more than 1/8-inch in 96-inch variation from a 				straight line.

F.	Casework:  Install without distortion. Complete installation of hardware and accessory items as 			indicated.

`		1.	Install casework with no more than 1/8-inch in 96-inch sag, bow, or other variation from a 				straight line.

G.	Countertops:  Anchor securely by screwing through corner blocks of base cabinets or other 			supports into underside of countertop.

1.	Install countertops with no more than 1/8-inch in 96-inch sag, bow, or other variation from a 			straight line.

2.	Install countertop brackets specified previously in this Section.  See Section 09900 for 				Painting of Brackets.

3.	Provide cutouts for plumbing fixtures, fixtures and fittings. Verify locations of cutouts from 				on-site dimensions. Seal surfaces of cutout edges.

4.	Caulk space between backsplash and wall with clear sealant.

H.	Shelving:  Install shelving in the maximum continuous lengths available. Screw-attach rest to 			underside of shelving.

I.	Complete the finishing work specified in this Section to extent not completed at shop or before 			installation of woodwork. Fill nail holes with matching filler where exposed. Apply specified 			finish coats, including stains and paste fillers if any, to exposed surfaces where only sealer/prime 			coats were applied in the shop.

J.	Refer to Division 9 Sections for final finishing of installed architectural woodwork.

3.03	ADJUSTING AND CLEANING

A.	Repair damaged and defective woodwork, where possible, to eliminate functional and visual 			defects; where not possible to repair, replace woodwork. Adjust joinery for uniform appearance.

B.	Clean, lubricate, and adjust hardware.

C.	Clean woodwork on exposed and semi-exposed surfaces. Touch-up shop applied finishes to 			restore damaged or soiled areas.

3.04	PROTECTION

A.	Provide final protection and maintain conditions in a manner acceptable to fabricator and Installer 			that ensures that woodwork is without damage or deterioration at the time of Substantial 				Completion.

END OF SECTION 06400