SECTION 07210

BUILDING INSULATION

PART 1 - GENERAL

1.01	RELATED DOCUMENTS

- Drawings and general provisions of Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

1.02	SUMMARY

- This Section includes the following:

  - Concealed building insulation.

- Related Sections:

  - Division 9 Section “Gypsum Board Assemblies” for provision of acoustical 	insulation in wood-framed assemblies.

  - Division 15 Sections for insulation on ducts, piping and equipment.

1.03	DEFINITIONS

- Thermal Resistivity: Where the thermal resistivities of insulation products are designated by “r-values,” they represent the reciprocal of thermal conductivity (k-values). Thermal conductivity is the rate of heat flow through a homogenous material exactly 1 inch thick. Thermal resistivity is expressed by the temperature difference in degrees F between the two exposed faces required to cause one BTU to flow through one square foot per hour at mean temperatures indicated.

1.04	SUBMITTALS

- General:  Submit in accordance with Section 01330.

- Product data: For each type of product indicated.

- Product test reports: Based on comprehensive tests performed by a qualified testing agency, for insulation products.

1.05	QUALITY ASSURANCE

- Source Limitations:  Obtain each type of building insulation through one source with resources to provide products of consistent quality in appearance and physical properties without delaying progress of the Work.

- Fire-Test-Response Characteristics:  Provide insulation and related materials with the fire-test-response characteristics indicated, as determined by testing identical products per test method indicated below by UL or another testing and inspecting agency acceptable to authorities having jurisdiction.  Identify materials with appropriate markings of applicable testing and inspecting agency.

- Surface Burning Characteristic:  ASTM E 84.

- Fire Resistance Ratings:  ASTM E 119.

- Combustion Characteristics: ASTM E 136.

1.06	DELIVERY, STORAGE AND HANDLING

- Protect insulation materials from physical damage and from deterioration by moisture, soiling, and other sources.  Store inside and in a dry location.  Comply with manufacturer's recommendations for handling, storage, and protection during installation.

- Protect plastic insulation as follows:

- Do not expose to sunlight, except to extent necessary for period of installation and concealment.

- Protect against ignition at all times.  Do not deliver plastic insulating materials to project site ahead of installation time.

- Complete installation and concealment of plastic materials as rapidly as possible in each area of construction.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

- In other Part 2 articles where titles below introduce lists, the following requirements apply to product section:

  - Manufacturers:  Subject to compliance with requirements, provide products by one of 	the manufacturers specified.

  - Products: Subject to compliance with requirements, provide one of the products specified.

2.02	INSULATING MATERIALS

- General:  Provide insulating materials that comply with requirements and with referenced standards.

- Preformed Units:  Sizes to fit applications indicated, selected from manufacturer's standard thicknesses, widths, and lengths.

- Unfaced Building Insulation in Batt Form: ASATM C 665, Type I (blankets without membrane facing); consisting of fibers manufactured from glass: with maximum flame-spread and smoke-developed indices of 25 and 50, respectively; passing ASTM E 136 for combustion characteristics. Provide in thickness for full depth of cavity; where cavity requires insulation that is thicker than standard size, install next larger size and compress into cavity.

  - Provide insulation in standard density except as noted otherwise.

a.	Provide high density batt insulation in locations noted.

  - Provide insulation shall have the following minimum R-values except where high 	density insulation is indicated to be provided:

a.	Walls: R-19.

b.	Ceilings – sound attenuation 6”

3.	Manufacturers:

a.	CertainTeed Corporation

b.	Owens Corning

c.	Johns Manville Corporation

2.03	INSULATION FASTENERS

- Insulation Support Anchor: Insul-Fast, 25 gage, galvanized continuous metal support strip with pre-punched tabs at 8 inches on center.

PART 3 - EXECUTION

3.01	EXAMINATION

- Examine substrates and conditions, with Installer present, for compliance with requirements for sections in which substrates and related work are specified and other conditions affecting performance.

- Proceed with installation of insulation only after unsatisfactory conditions have been corrected.

3.02	PREPARATION

- Clean substrates of substances harmful to insulations or vapor retarders, including removing projections capable of puncturing vapor retarders or of interfering with insulation attachment.

3.03	INSTALLATION - GENERAL

- Comply with insulation manufacturer's written instructions applicable to products and application indicated.

- If printed instructions are not available or do not apply to project conditions, consult manufacturer's technical representative for specific recommendations before proceeding with installation of insulation.

- Install insulation that is undamaged, dry, and unsoiled and that has not been left exposed at any time to ice and snow.

- Extend insulation in thickness indicated to envelop entire area to be insulated.  Cut and fit tightly around obstructions, and fill voids with insulation.  Remove projections that interfere with placement.

- Apply single layer of insulation to produce thickness indicated, unless multiple layers are otherwise shown or required to make up total thickness.

3.04	INSTALLATION OF GENERAL BUILDING INSULATION

- Apply insulation units to substrates by method indicated, complying with manufacturer’s written instructions. If no specific method is indicated, bond units to substrate with adhesive or use mechanical anchorage to provide permanent placement and support of units. Fill voids in thermal envelope not covered by the works of other sections.

- Install glass-fiber batts in cavities formed by framing members according to the following requirements:

- Use batt widths and lengths that fill the cavities formed by framing members. If more than one length is required to fill cavity, provide lengths that will produce a snug fit between ends.

- Place batts in cavities formed by framing members to produce a friction fit between edges of insulation and adjoining framing members.

- Install insulation support anchors at top of cavity and spaced every 5 feet on 	center full length of each cavity.

3.07	PROTECTION

- Protect installed insulation from damage due to harmful weather exposures, physical abuse, and other causes.  Provide temporary coverings or enclosures where insulation will be subject to abuse and cannot be concealed and protected by permanent construction immediately after installation.

END OF SECTION 07210