Copyright 1999, The American Institute of Architects (AIA)

SECTION 08211

WOOD DOORS

This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and other Division 1 Specification Sections, apply to this Section.

SUMMARY

This Section includes the following:

Adjust list below to suit Project.

Solid-core doors with wood-veneer faces.

Wood frames for prehung doors.

Shop priming wood doors with opaque finish.

Factory finishing wood doors with transparent finish.

Factory fitting wood doors to frames and factory machining for hardware.

Related Sections include the following:

List below only procedures that the reader might expect to find in this Section but are specified elsewhere.

Retain subparagraph above or below or delete both if not required.

Division 8 Section "Steel Frames" for receiving wood doors.

Division 8 Section "Door Hardware" for hardware and weather-stripping.

Division 8 Section "Glazing" for glass view panels in on-rated wood doors.

Division 8 Section "Painting" for field finishing of factory primed wood doors.

SUBMITTAL

General:  Submit in accordance with Section 01330.

1.	Submittals for Sections 08110, 08211, 08212 and 08710 shall be made concurrently.

Product Date. For each type of door, include details of core and edge construction, louvers, and trim for openings. Include factory-finishing specifications. Submit door manufacturer's storage, handling, finish, installation, maintenance instructions, and sample warranty.

Shop Drawings: Indicate location, size, thickness, and hand of each door; elevation of each kind of door; face veneer, construction details not covered in Product Data; location and extent of hardware blocking; and other pertinent data.

1.	Indicate dimensions and locations of mortises and holes for hardware.

2.	Indicate dimensions and locations of cutouts.

3.	Indicate requirements for veneer matching.

4.	Indicate doors to be factory finished and finish requirements.

5.	Indicate fire ratings for fire doors.

6.	Indicate construction details of stiles, rails, panels and molding (sticking) for stile and 			rail-configured doors.

7.	Indicate doors to be factory glazed.

Existing to Remain:  Submit schedule of doors using same reference numbers for details and openings as those on Contract Drawings.

1.	Indicate coordination of glazing frames and stops with glass and glazing requirements.

E.	Samples: Submit the following:

1.	Factory finishes applied to actual door face materials, approximately 8-inches by 10-				inches for each material and finish.

2.	Frames for light openings, 6-inches long, for each material, type, and finish required.

3.	Hinges: One for prehung swing door.

QUALITY ASSURANCE

Source Limitations: Obtain each type of wood door through one source from a single manufacturer.

Delete references to historic items in paragraph below if not required.

Quality Standard: Comply with WDMA I.S.I-A, "Architectural Wood Flush Door" or AWIs "Architectural Woodwork Quality Standards Illustrated".

DELIVERY, STORAGE, AND HANDLING

Protect wood doors during transit, storage, and handling to prevent damage, soiling and deterioration. Comply with requirements of referenced standard, manufacturer's instructions, and recommendations of WDMA I.S.1, Appendix, "How to Store, Handle, Finish, Install and Maintain Wood Doors".

1.	Package doors at factory prior to shipping.

2.	Protect doors from extremes of heat and cold. Relative humidity shall not be less than 20 			percent or more than 60 percent.

3.	Compare pre-finished doors to approved finish sample upon delivery. Notify Architect if

sample does not match.

B.	Mark each door on top and bottom rail with opening number used on Shop Drawings.

Retain record submittal below, if applicable.  Landfill records may be required by Owner when discarded demolished materials contain hazardous wastes.

Review requirements of work performed by other trades that rely on substrates exposed by selective demolition operations.

Document proceedings, including corrective measures and actions required, and furnish copy of record to each participant.

Provide 72-hour minimum advance notice to participants prior to convening predemolition conference.

PROJECT CONDITIONS

Retain, revise, or delete paragraphs and subparagraphs in this Article to suit Project.  Add other limitations if necessary, such as when adjacent floors will be occupied.

Environmental Limitations: Do not delivery or install doors until building is enclosed, wet work is complete, and HVAC system is operating and will maintain temperature and relative humidity at occupancy levels during the remainder of the construction period.

1.07	WARRANTY

A.	General: Special warranty specified in this Article shall not deprive Owner of other rights Owner may have under other provisions of Contract Documents and will be in addition to and run concurrent with other warranties made by contractor under requirements of Contract Documents.

B.	Special Warranty: Manufacturer's standard form, signed by manufacturer, Installer, and Contractor, in which manufacturer agrees to repair or replace doors that are defective in materials or workmanship, have warped (bow, cup, or twist), show telegraphing of core construction in face veneers, and which do not conform to tolerance limitations of specified quality standards.

1.	Warranty shall also include installation and finishing that may be required due to repair 	or replacement of defective doors.

2.	Warranty shall be in effect during the following period of time from date of Substantial 	Completion:

a.	Solid-Core Interior Doors: Life of installation.

b.	Hollow-Core Interior Doors: One (1) Year

PART 2 - PRODUCTS

2.01	MANUFACTURERS

A.	Manufacturers: Subject to compliance with requirements, provide products by one of the following:

1.	Solid-Core Wood Doors:

a.	Algoma Hardwoods, Inc.

b.	Eggers Industries - Architectural Door Division.

c.	Marshfield Door Systems (Weyerhaeuser).

d.	VT Industries, Inc.

2.02	DOOR CONSTRUCTION GENERAL

A.	Solid-Core Doors for Transparent Finish:

1.	Grade: Premium with Grade A faces.

2.	Species and Cut: Select walnut, plain sliced.

3.	Match between Veneer Leaves: Book match.

4.	Assembly of Veneer Leaves on Door Faces: Running match.

5.	Match: Provide door faces of compatible color and grain for door hung in same opening 	or separated only by mullions.

6.	Room Match: Provide door faces of compatible color and grain within each separate 	room or area of building.

7.	Stiles: Same species as faces.

8.	Finish: Mahogany finish to be selected by Architect.

9.	Provide sample of wood and finish prior to installation.

2.03	SOLID-CORE WOOD DOORS

A.	Particleboard Cores: Comply with the following requirements:

1.	Particleboard: ANSI A208.1, Grade LD-2.

2.	Blocking: Provide wood blocking in particleboard core doors as needed to eliminate 	through-bolting hardware.

B.	Interior Veneer-Faced Doors:

1.	Core: Particleboard for flush doors.

2.	Construction: Five plies with stiles and rails bonded to core, and then entire unit abrasive 	planed before veneering. Type I or II adhesive for core construction and veneer plies. No 	substitution.

3.	Finish: Transparent, factory finished.

2.04	WOOD DOOR FRAMES FOR PREHUNG DOORS

A.	Construction:

1.	Head and Jamb: Minimum 3/4-inch thickness, primed finish over manufacturer's standard 	wood species.

2.	Stops: Minimum ½ inch high, 1 ¼ inch wide.

2.05	FABRICATION

A.	Factory fit doors to suit frame-opening sizes indicated, with the following uniform clearances and bevels, unless otherwise indicated:

1.	Comply with clearance requirements of referenced quality standard for fitting. Comply 	with requirements in NFPA 80 for fire-rated doors.

2.	Coordinate sizing of pairs of doors to provide maximum 3/16-inch gap between leafs to 	permit proper functioning of dead latching feature.

B.	Factory machine doors for hardware that is not surface applied. Locate hardware to comply with DHI-WDHS-3. Comply with final hardware schedules, door frame Shop Drawings, DHI A115-W series standards, and hardware templates.

1.	Coordinate measurements of hardware mortises in metal frames to verify dimensions and 	alignment before factory machining.

C.	Openings: Cut and trim openings through doors to comply with applicable requirements of referenced standards for kind(s) of door(s) required.

1.	Light Openings: Trim openings with moldings of material and profile indicated.

2.	Louvers: Factory install louvers in prepared openings.

2.06	SHOP PRIMING

A.	Doors for Opaque Finish: Shop prime faces and edges of doors, including cutouts, with one coat of wood primer specified in Division 9 Section "Painting".

B.	Finish doors at factory.

C.	Transparent Finish:

1.	Grade:  Premium.

2.	Finish:  AWI System, TR-6 catalyzed polyurethane.

3.	Staining:  As selected by Architect from manufacturer's full range.

4.	Sheen:  Satin.

PART 3 – EXECUTION

3.01	EXAMINATION

A.	Examine doors and installed door frames, with Installer present, before hanging doors.

1.	Verify that frames comply with indicated requirements for type, size, location, and swing 	characteristics and have been installed with level heads and plumb jambs.

2.	Locks, exit devices, door closers and other hardware shall be installed in accordance with the 	manufacturer's instructions. Pilot holes of recommended size, for wood screws required to 	fasten the hardware, shall be drilled by the installing Contractor before screws are fastened to 	the wood doors.

B.	Proceed with installation only after unsatisfactory conditions have been corrected.

3.02	INSTALLATION

A.	Hardware: For installation, see Division 8 Section "Door Hardware."

1.	Hinges shall be shimmed with metal shims at each door to provide equal clearance at each 	jamb.

2.	Locks, exit devices, door closers, and other hardware shall be installed in accordance with the 	manufacturer's instructions. Pilot holes of recommended size, for wood screws required to 	fasten the hardware, shall be drilled by the installing Contractor before screws are fastened to 	the wood doors.

B.	Manufacturer's Written Instructions:  Install doors to comply with manufacturer's written instructions, referenced quality standard, and as indicated.

1.	Install fire-rated doors in corresponding fire-rated frames according to NFPA 80.

C.	Prehung Door Frame Attachment:  Shimmed and fastened through jamb boards at each hinge and corresponding locations in strike jambs. Attachment by trim only is not acceptable.

D.	Factory-Fitted Doors:  Align in frames for uniform clearance at each edge. Coordinate pairs of doors to provide maximum 3/16-inch gap between leafs and accurate alignment of strike to permit proper functioning of dead latching feature.

E.	Factory-Finished Doors (Transparent Finish):  Restore finish before installation if fitting or matching is required at Project site.

F.	Field-Finished Doors:  Division 9 Section "Painting" for doors receiving opaque finish.

3.03	ADJUSTING

A.	Operation:  Rehang or replace doors that do not swing or operate freely.

B.	Factory Finished Doors:  Replace doors that are damaged or do not comply with requirements. Doors may be repaired or refinished if work complies with requirements and shows no evidence of repair or refinishing.

END OF SECTION 08211