## SECTION 09260

## GYPSUM BOARD ASSEMBLIES

### PART 1 – GENERAL

1.1    	RELATED DOCUMENTS

A.  Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

1.2    	SUMMARY

A.   This Section includes the following:

    - Interior gypsum wallboard.

    - Acoustical insulation

    - Non-load-bearing steel framing.

    - Firestopping

B.    Related Sections include the following:

- Division 5 Section "Light Gage Metal Framing" for load-bearing steel framing and 	gypsum 	sheathing.

- Division 6 Section “Rough Carpentry” for concealed wood blocking.

- Division 9 painting sections for coordination/inspection requirements for painting 	contractor and primers applied to gypsum board surfaces.

1.3    	DEFINITIONS

A.  Gypsum Board Terminology: Refer to ASTM C 11 and GA-505 for definitions of terms for 	gypsum board assemblies not defined in this Section or in other referenced standards.

1.4    	SUBMITTALS

- General: Submit in accordance with Section 01330.

- Product Data: For each type of product indicated.

- Shop Drawings: Show locations, fabrication, and installation of control and expansion 	joints 	including plans, elevations, sections, details of components, and attachments to 	other units of 	work.

- Firestopping: For each joint condition where fire-rated walls and partitions interface other 	walls, floors, structural members or other building structure, provide UL firestop system 	description and drawing. Show each kind of construction condition and relationships to 	adjoining construction. Indicate which firestop materials will be used where and thickness for 	different hourly ratings. Include UL firestop design designation that evidences compliance 	with requirements for each condition.

1.5    	QUALITY ASSURANCE

A.	Fire-Test-Response Characteristics: For gypsum board assemblies with fire-resistance ratings, 		provide materials and construction identical to those tested in assembly indicated 	according to 	ASTM E 119 by an independent testing and inspecting agency acceptable to authorities having 	jurisdiction.

1.	Fire-Resistance-Rated Assemblies: Indicated by design designations from UL's "Fire 	Resistance Directory" or GA-600, "Fire Resistance Design Manual" or in 	listing of 	another testing and inspecting agency acceptable to authorities having jurisdiction.

2.	Deflection Firestop Track: Top runner provided in fire-resistance-rated assemblies 	indicated shall be labeled and listed by UL, Warnock Hersey, or another testing and 	inspecting agency acceptable to authorities having jurisdiction.

B.	Source Limitations for Steel Framing: Obtain steel framing members for gypsum board 	assemblies from a single source from a single manufacturer.

C.	Source Limitations for Panel Products:  Obtain each type of gypsum board and other panel 	products from a single source from a single manufacturer.

D.  Source Limitations for Finishing Materials: Obtain finishing materials from either the same 	manufacturer that supplies gypsum board and other panel products or from a 	manufacturer 	acceptable to gypsum board manufacturer.

E.  	Gypsum Board Finish Mockups: Before finishing gypsum board assemblies, install mockup 	using room designated by architect to demonstrate aesthetic effects and qualities of materials and 	execution.

1.	Install mockups for the following applications:

a.	Surfaces indicated to receive non-textured paint finishes.

2.	Simulate finished lighting conditions for review of mockups.

3.	Mockup will be painted to provide finished condition for viewing.

4.	Approved mockups may become part of the completed work if undisturbed at time of 	substantial completion.

1.6    	DELIVERY, STORAGE, AND HANDLING

A. 	Deliver materials in original packages, containers, or bundles bearing brand name and 	identification of manufacturer or supplier.

B.  	Store materials inside under cover and keep them dry and protected against damage from 	weather, direct sunlight, surface contamination, corrosion, construction traffic, and other 	causes. 	Stack gypsum panels flat to prevent sagging.

1.7    	PROJECT CONDITIONS

- Environmental Limitations:  Comply with ASTM C 840 requirements or gypsum board 	manufacturer's written recommendations, whichever are more stringent.

- Room Temperatures: For non adhesive attachment of gypsum board to framing, maintain 	not less 	than 40 degrees F. For adhesive attachment and finishing to gypsum board, maintain not less than 	50 degrees F for 48 hours before application and continuously after until dry. Do not exceed 95 	degrees F when using temporary heat sources.

C.	Ventilation: Ventilate building spaces as required to dry joint treatment materials. Avoid 	drafts 	during hot, dry weather to prevent finishing materials from drying too rapidly.

PART 2 - PRODUCTS

2.1    	MANUFACTURERS

A.  Manufacturers: Subject to compliance with requirements, provide products of the 	following:

- Steel Framing and Furring:

- Dale Industries, Inc.

- Dietrich Industries, Inc.

- MarinoWare; Division of Ware hid.

- National Gypsum Company.

- Unimast, Inc.

- Grid Suspension Assemblies:

  - Armstrong World Industries, Inc.

  - Chicago Metallic Corporation

  - USG Interiors, Inc.

- Gypsum Board and Related Products:

- Domtar Gypsum

- G-P Gypsum Corp.

- National Gypsum Company.

- United States Gypsum Co.

  - STEEL SUSPENDED CEILING AND SOFFIT FRAMING

- Components, General: Comply with ASTM C 754 for conditions indicated

- Fire-Rated Ceilings: Provide components required to construct UL design 	indicated.

- Tie Wires: ASTM A 641/A 641M, Class 1 zinc coating, soft temper, not less than 0.0620-inch diameter (8 gage) wire, or double strand of not less than 0.099-inch diameter (12 gage) wire.

- Hanger Attachments to Concrete: As follows:

- Powder-Actuated Fasteners: Suitable for application indicated, fabricated from 	corrosion-resistant materials, with clips or other devices for attaching hangers of type 	indicated, and capable of sustaining, without failure, a load equal to 10 times that 	imposed by construction as determined by testing according to ASTM E 1190 by a 	qualified independent testing agency.

- Hangers: As follows:

- Wire Hangers: ASTM A641/ A 641M, Class 1 zinc coating, soft temper, not less 	than 	0.160 inch (8 gage) diameter.

- Carrying Channels:

1.	Cold-rolled, commercial-steel sheet with a base metal thickness of 0.0538-inch, a 				minimum 1/2 inch wide flange, with ASTM A 653/A 653M, G40, 						hot-dip galvanized zinc coating.

2.	Depth: 1 ½-inches.

- Furring Channels (Furring Members): Commercial-steel sheet with ASTM A 653/A 653M, 	G40, hot-dip galvanized zinc coating.

- Hat-shaped, rigid furring channels: ASTM C645, 7/8 inch deep; where indicated.

  - Minimum base metal thickness: 0.0179-inch.

- Grid Suspension System for Interior Ceilings: ASTM C 645, direct-hung system 	composed of 	main beams and cross-furring members that interlock, heavy-duty.

- Products: Subject to compliance with requirements, provide one of the following:

a.	Armstrong World Industries, Inc.; furring systems/drywall.

b.	Chicago Metallic Corporation; Drywall furring 640 system.

c.	USG Interiors, Inc.; Drywall suspension system.

2.3	STEEL PARTITION AND SOFFIT FRAMING

Components, General:  As follows:

Comply with ASTM C 754 for conditions indicated.

Steel Sheet Components:  Complying with ASTM C 645 requirements for metal and 	with ASTM A 653/A 653M, G40, hot-dip galvanized zinc coating.

Steel Studs and Runners:  ASTM C 645.

Minimum Base Metal Thickness:  0.0179 inch (25 gage) minimum, unless 	otherwise indicated.

Provide studs with 0.0329 inch (20 gage) minimum thickness at the 	following locations:

For double studs at door jamb openings.

For 6 inch framing.

Where indicated.

Depth:  As indicated.

Maximum Allowable Deflection:  Increase metal thickness where required to meet the 	following:

Maximum Allowable Deflection for Drywall Assemblies:  L/240 	calculated using a 5 pound per square uniform load perpendicular to studs 	and based on stud properties alone.

Deep-Leg Deflection Track:  ASTM C 645 top runner with flanges to allow for 3/4-inch 	deflection.

Firestop Track:  Top runner manufactured to allow partition heads to expand and contract 	with movement of the structure while maintaining continuity of fire-resistance-rated 	assembly indicated; in thickness not less than indicated for studs and in width to accommodate 	depth of studs.  Provide deflection track with flanges to allow for 3/4-inch deflection at floors and 	1½ inch at roofs.

Product:  Fire Trak Corp.; Fire Trak attached to studs with Fire Trak Slip Clip

Flat Strap and Backing Plate:  Steel sheet for blocking and bracing in length and width 	indicated.

Minimum Base Metal Thickness:  0.0598-inch (16 gage), unless indicated 	otherwise.

Cold-Rolled Channel Bridging:  0.0538-inch (16 gage) minimum bare steel thickness, with 	minimum ½ inch wide flange.

Depth:  1 ½ - inches.

Clip Angle:  1 ½ inch by 1 ½ inch, 0.068-inch thick, galvanized steel.

Hat-Shaped, Rigid Furring Channels:  ASTM C 645.

Minimum Base Metal Thickness:  0.0312-inch (20 gage).

Depth:  7/8 inch, unless otherwise shown.

Deflection Brackets:

Construction:  Slotted galvanized steel angle with step bushing to prevent over 	tightening of fasteners.

Vertical Deflection: Total travel as required for condition.

Product:  VertiClip; Signature Industries, (919) 844-0789.

Series:  SL, SDL, SLB, and SLS as required by attachment condition.

Fasteners for Metal Framing:  Of type, material, size, corrosion resistance, holding power, and 	other properties required to fasten steel framing and furring members to substrates involved; 	complying with the recommendations of gypsum board manufacturers for applications indicated.

2.4    	INTERIOR GYPSUM WALLBOARD

A.  Panel Size: Provide in maximum lengths and widths available that will minimize joints in 	each 	area and correspond with support system indicated.

B.  Gypsum Wallboard: ASTM C 36.

- TypeX:

a.	Thickness: 5/8-inch (15.9 mm).

b.	Long Edges: Tapered

2.6   	TRIM ACCESSORIES

A.   Interior Trim: ASTM C 1047, galvanized steel.

- Shapes:

a.    	Cornerbead: 1 ¼ inch by 1 ¼ inch external corner with 1/8-inch nose 			bead; use at outside corners, unless otherwise indicated.

b.   	 LC-Bead (Casing): J-shaped casing with 1/16 inch nose bead ground, not 			less than 30 gage; exposed long flange receives joint compound; use 			where indicated.

c.    	L-Bead: L-shaped; exposed long leg receives joint compound; use where 			indicated

d.	Expansion (Control) Joint: One-piece control joint formed with V-shaped 			slot and removable strip covering slot opening.

2.7		JOINT TREATMENT MATERIALS

  - General: Comply with ASTM C 475 and the recommendations of both the manufacturers 	of sheet 	products and of joint treatment materials for each application indicated.

  - Joint Tape:

- Interior Gypsum Wallboard: Paper reinforcing tape. Fiberglass tape not permitted.

  - Setting-Type Joint Compound: Factory-packaged, job-mixed, chemical-hardening powder 	products formulated for uses indicated.

    - Where setting-type joint compounds are indicated as a taping compound only or for 	taping and filling only, use formulation that is compatible with other joint 	compounds applied over it.

  - Drying-Type Joint Compound: Factory-packaged vinyl-based products complying with 	the 	following requirements for formulation and intended use.

    - Ready-Mixed Formulation: Factory-mixed product

  - Type of Joint Compound for Interior Gypsum Wallboard: For each coat use formulation 	that is 	compatible with other compounds applied on previous or for successive coats.

- Prefilling: At open joints, beveled panel edges and damaged surface areas, use setting-	type taping compound.

- Embedding and First Coat: For embedding tape and first coat on joints, fasteners, 	and trim flanges, use setting-type taping compound or drying-type, all-purpose 	compound.

- Fill Coat: For second coat, use setting-type, sandable topping compound or drying-	type, all-purpose compound.

- Finish Coat: For third coat, use setting-type, sandable topping compound or drying-type, 	all-purpose compound.

2.8 	ACOUSTICAL SEALANT

  - Products: Subject to compliance with requirements, provide one of the following:

    - Acoustical Sealant for Exposed and Concealed Joints:

a.	Pecora Corp., AC-20 FTR Acoustical and Insulation Sealant

b.	United States Gypsum Co., Sheetrock Acoustical Sealant

    - Acoustical Sealant for Concealed Joints:

a.	Ohio Sealants, Inc; Pro-Series SC-170 Rubber Base Sound Sealant

b.	Pecora Corp.; BA-98

c.	Tremco, Inc.; Tremco Acoustical Sealant

  - Acoustical Sealant for Exposed and Concealed Joints: Nonsag, nonstaining, latex sealant 	complying with ASTM C 834 that effectively reduces airborne sound transmission through 	perimeter joints and openings in building construction as demonstrated by testing representative 	assemblies according to ASTM E 90.

  - Acoustical Sealant for Concealed Joints: non drying non hardening, non skinning, non staining, 	gunnable, synthetic-rubber sealant recommended for sealing interior concealed joints to reduce 	airborne sound transmission.

2.9	AUXILIARY MATERIALS

A.  General: Provide auxiliary materials that comply with referenced installation standards and 	manufacturer's written recommendations.

B.  Steel Drill Screws: ASTM C 1002, unless otherwise indicated.

- Fastening gypsum board to steel members: Type S bugle head.

C.  Sound Attenuation Insulation (Acoustical Insulation): ASTM C 665, Type I (fiberglass 	blankets without membrane facing) used as acoustical insulation.

- Fire-Resistance-Rated Assemblies:   Comply with mineral-fiber requirements of 	assembly.

- Manufacturers: Subject to compliance with requirements, provide products by one 	of the following:

  - Certainteed

  - Owens Corning

  - Johns Manville

D.   Thermal Insulation: As specified in Division 7 Section "Building Insulation."

E.   Insulation Support Anchors: Insul-Fast 25 gauge galvanized continuous metal support strip with 	pre-punched tabs at 8 inches on center.

F.  Firestopping: Provide firestopping where fire rated gypsum board assemblies butt 	dissimilar 	materials, including masonry, steel deck, joists, beams and structural members as part of the 	gypsum board assembly work. Penetrations through fire-resistance-rated 	walls and partitions by 	Division 15 and 16 work, including both empty openings and openings containing cables, 	pipes, ducts and conduits are specified as part of the Division 15 and 16 work.

PART 3 - EXECUTION

3.1    	EXAMINATION

    - Examine areas and substrates, with Installer present, and including welded steel door frames and 	borrowed lites, cast-in anchors, and structural framing, for compliance with requirements 	and 	other conditions affecting-performance.

    - Examine panels before installation. Reject panels that are wet, moisture damaged, or mold 	damaged.

    - Proceed with installation only after unsatisfactory conditions have been corrected.

    - Post-Installation Inspection: Inspect the walls for dents and imperfections, with the 	Installer and painter present, prior to painting. Inspect wall again after primer and first coat of 	paint has been applied, with Installer and painter present.

      - Touch up visible gypsum board imperfections before priming of walls.

      - Touch up imperfections found in field of boards and joints made visible from 	painting after first finish coat applied.

      - Joint compound touch up shall be primed and painted before final coat is applied, 	and viewed for acceptability.

3.2    	PREPARATION

A.  Suspended Ceilings: Coordinate installation of ceiling suspension systems with installation of 	overhead structure to ensure that inserts and other provisions for anchorages to building structure 	have been installed to receive ceiling hangers at spacing required to support ceilings and that 	hangers will develop their full strength.

3.3    	INSTALLING STEEL FRAMING, GENERAL

A. 	Installation Standards: ASTM C 754, and ASTM C 840 requirements that apply to framing 	installation.

B. 	Install supplementary framing, blocking, and bracing at terminations in gypsum board 	assemblies to support fixtures, equipment services, heavy trim, grab bars, toilet accessories, 	furnishings, or similar construction. Comply with details indicated and with gypsum board 	manufacturer's -written recommendations or, if none available, with United States Gypsum's 	"Gypsum Construction Handbook."

C.  	Isolate steel framing from building structure at locations indicated to prevent transfer of 	loading 	imposed by structural movement.

1.	Isolate ceiling assemblies where they abut or are penetrated by building structure.

2.	Isolate partition framing and wall furring where it abuts structure, except at floor. 	Install slip-type joints at head of assemblies that avoid axial loading of assembly 	and 	laterally support assembly.

a.	Allow for 3/4 inch deflection at floors and roofs.

b.	Install deflection track top runner or deflection brackets to attain lateral support 		and avoid axial loading.

c.	Install deflection firestop track top runner at fire-resistance-rated assemblies.

i.	Attach jamb studs at openings to tracks using manufacturer’s standard 		stud clip.

D.  	Do not bridge building control and expansion joints with steel framing or furring members. 	Frame both sides of joints independently.

3.4    	INSTALLING STEEL SUSPENDED CEILING AND SOFFIT FRAMING

- Install suspension system components in sizes and spacings indicated on drawings, but not less 	than those required by referenced installation standards for assembly types and other assembly 	components indicated.

- Suspended ceiling hangers from building structure as follows:

  - Install hangers plumb and free from contact with insulation or other objects within 	ceiling 	plenum that are not part of supporting structural or ceiling suspension system. 	Splay hangers only where required to miss obstructions and offset resulting 	horizontal forces by bracing, counter splaying or other equally effective means.

  - Where width of ducts and other construction within ceiling plenum produces hanger 	spacings that interfere with the location of hangers required to support standard 	suspension system members, install supplemental suspension members and hangers to 	support ceiling loads within performance limits established by referenced standards.

  - Wire Hangers: Secure wire hangers by looping and wire-tying, either directly to 	structures or to inserts, eye screws, or other devices and fasteners that are secure and 	appropriate for substrate, and in a manner that will not cause them to deteriorate or 	otherwise fail.

  - Do not attach hangers to steel deck tabs. Attach hangers to structural members.

  - Do not attach hangers to steel roof deck. Attach hangers to structural members.

  - Do not connect or suspend steel framing from ducts, pipes, or conduit.

- Installation Tolerances: Install steel framing components for suspended ceiling so 	members for panel attachment are level to within 1/8 inch in 12 feet measured lengthwise 	on each member and transversely between parallel members.

- Wire-tie furring channels to supports, as required to comply with requirements for 	assemblies indicated.

- Install suspended steel framing components in sizes and spacings indicated, but not less than 	that required by the referenced steel framing and installation standards.

  - Hangers: 48 inches o.c.

  - Carrying channels (main runners): 48 inches o.c.

  - Furring channels (furring members): 16 inches o.c.

- Grid Suspension System: Attach perimeter wall track or angle where grid suspension system 	meets vertical surfaces. Mechanically join main beam and cross-furring members to each other 	and butt-cut to fit into wall track.

3.5    	INSTALLING STEEL PARTITION AND SOFFIT FRAMING

A.  Install tracks (runners) at floors, ceilings, and structural walls and columns where gypsum 	board assemblies abut other construction.

B.  Installation Tolerance: Install each steel framing and furring member so fastening 	surfaces vary 	not more than 1/8 inch (3 mm) from the plane formed by the faces of 	adjacent framing.

C.  Extend partition framing full height to structural supports or substrates above suspended 	ceilings, except where partitions are indicated to terminate at suspended ceilings. 	Continue 	framing over frames for doors and openings and frame around ducts penetrating partitions above 	ceiling to provide support for gypsum board.

1.	Cut studs 3/4 inch short of full height to pro vide perimeter relief. Do not fasten studs to 	top track to allow independent movement of studs and track.

2.	For fire-resistance-rated and STC-rated partitions that extend to the underside of 	floor/roof slabs and decks or other continuous solid-structure surfaces to obtain ratings, 	install framing around structural and other members extending below floor/roof slabs 	and decks, as needed to support gypsum board closures and to make partitions 	continuous from floor to underside of solid structure.

D.   Install steel studs and furring at the following spacings:

1.  	Single-Layer Construction: 16 inches (406 mm) o.c., unless otherwise indicated.

E.    Install steel studs so flanges point in the same direction and leading edge or end of each 	panel 	can be attached to open (unsupported) edges of stud flanges first.

1.  	Attach both flanges to floor runner track with screws.

F.  	Frame door openings to comply with GA-600 and with gypsum board manufacturer's 	applicable written recommendations, unless otherwise indicated. Screw vertical studs at jambs 	to jamb anchor clips on door frames; install runner track section (for cripple studs) at head 	and secure to jamb studs.

1.   	Install two studs at each jamb, unless otherwise indicated.

2.   	Install cripple studs at head adjacent to each jamb stud, with a minimum ½ inch (13-mm) 	clearance from jamb stud to allow for installation of control joint.

3.   	Extend jamb studs through suspended ceilings and attach to underside of floor or 	roof 	structure above, even when partitions are not full height. Provide diagonal bracing 	at tall partitions to stop deflection and vibration of studs when doors are 	slammed shut.

4. 	 Extend jamb studs one-piece full height.

G. 	Frame openings other than door openings the same as required for door openings, unless 	otherwise indicated. Install framing below sills of openings to match framing required above 	door heads.

3.6   	INSTALLATION OF ACOUSTICAL INSULATION

- Install acoustical insulation at locations indicated before installing gypsum panels, unless 	blankets are readily installed after panels have been installed on one side. Cut and fit tightly 	around obstructions, and fill voids with insulation. Remove projections that interfere with 	placement.

- Install a single layer of insulation of required thickness to fill the full depth of cavity, unless 	otherwise shown. Where cavity requires insulation that is thicker than standard size, install next 	to larger size and compress into cavity.

- Hold batt insulation in place with insulation support anchors located at 5 feet on center full 	height of wall, starting at the top of each stud space.

- Stuff glass fiber loose fill insulation into miscellaneous voids and cavity spaces. Fill box 	headers, and voids while framing is being erected that will be inaccessible for installation 	later. Compact to approximately 40 percent of normal maximum volume (to a density of 	approximately 2.5 pcf).

3.8    	APPLYING AND FINISHING PANELS, GENERAL

A 	Gypsum Board Application and Finishing Standards: ASTM C 840 and GA-216, except as 	specified otherwise.

B.  Install acoustical insulation, where indicated, before installing gypsum panels, unless blankets are 	readily installed after panels have been installed on one side.

C.  Install ceiling board panels across framing to minimize the number of abutting end joints and to 	avoid abutting end joints in the central area of each ceiling. Stagger abutting end joints of 	adjacent panels not less than one framing member.

D.  Install gypsum panels with face side out. Butt panels together for a light contact at edges 	and 	ends with not more than 1/16 inch (1.5 mm) of open space between panels. Do not force into 	place.

E.   Locate edge and end joints over supports, except in ceiling applications where intermediate 	supports or gypsum board back-blocking is provided behind end joints. Do not place tapered 	edges against cut edges or ends. Stagger vertical joints on opposite sides of partitions. Do 	not make joints other than control joints at comers of framed openings.

F.   Attach gypsum panels to steel studs so leading edge or end of each panel is attached to open 	(unsupported) edges of stud flanges first.

G.   Attach gypsum panels to framing provided at openings and cutouts.

H.   Form control and expansion joints with space between edges of adjoining gypsum panels.

1.	Where control joints are not shown, provide control joints at a maximum spacing 	of 30

feet; review proposed locations with architect prior to commencement of work.

I.   Cover both faces of steel stud partition framing with gypsum panels in concealed spaces 	(above 	ceilings, etc.), except in chases braced internally.

1.   	Unless concealed application is indicated or required for sound, fire, air, or smoke 	ratings, coverage may be accomplished with scraps of not less than 8 sq. ft. (0.7 	sq. m) 	in area.

2.   	Fit gypsum panels around ducts, pipes, and conduits.

3.   	Where partitions intersect open concrete coffers, concrete joists, and other structural 	members projecting below underside of floor/roof slabs and decks, cut gypsum panels to 	fit profile formed by coffers, joists, and other structural members; allow ¼-inch to 3/8-	inch-(6.4- to 9.5-mm-) wide joints to install sealant.

J.  	Isolate perimeter of non-load-bearing gypsum board partitions at structural abutments, except 	floors. Provide ¼-inch to ½-inch (6.mm to 12.7mm) wide spaces at these locations, and rim edges 	with U-bead edge trim where edges of gypsum panels are exposed. Seal joints between edges and 	abutting structural surfaces with acoustical sealant.

K.  Space fasteners in gypsum panels according to referenced gypsum board application and 	finishing standard and manufacturer's written recommendations.

1.    	Space screws a maximum of 12 inches (304.8 mm) o.c. for vertical applications.

L.   Space fasteners in panels that are tile substrates a maximum of 8 inches (203.2 mm) o.c.

M.  Remove screws that do not hit studs, supports or blocking.

3.9    	PANEL APPLICATION METHODS

A.    Single-Layer Application:

1.  	On ceilings, apply gypsum panels before wall/partition board application to the greatest 	extent possible and at right angles to framing, unless otherwise indicated.

2.  	On partitions/walls, apply gypsum panels vertically (parallel to framing), unless 	otherwise indicated or required by fire-resistance-rated assembly, and minimize end 	joints.

a.   	Stagger abutting end joints not less than one framing member in alternate courses 	of board.

b.    	High walls, install panels horizontally, unless otherwise indicated or required by 	fire-	resistance-rated assembly.

B.   Single Layer Fastenings Methods: Apply gypsum panels to supports with steel drill screws.

3.10   	INSTALLING TRIM ACCESSORIES

A.	General: For trim with back flanges intended for fasteners, attach to framing with same 	fasteners used for panels.   Otherwise, attach trim according to manufacturer's written 	instructions.

B.  Install corner bead at external corners.

C.  Install edge trim where edge of gypsum panels would otherwise be exposed. Provide edge 	trim type with face flange formed to receive joint compound, except where other types are 	indicated.

1.  	Install LC-bead where gypsum panels are tightly abutted to other construction and 	back flange can be attached to framing or supporting substrate.

2.  	Install L-bead where edge trim can only be installed after gypsum panels are 	installed.

D. 	Control Joints: Install control joints according to ASTM C 840 and in specific locations 	approved by Architect for visual effect.

3.11    	FINISHING GYPSUM BOARD ASSEMBLIES

A.  General: Treat gypsum board joints, interior angles, flanges of corner bead, edge trim, control 	joints, penetrations, fastener heads, surface defects, and elsewhere as required to prepare gypsum 	board surfaces for decoration. Promptly remove residual joint compound from adjacent surfaces.

B.  	Prefill open joints, beveled edges and damaged surface areas using setting-type joint 	compound.

C.  Apply joint tape over gypsum board joints, except those with trim having flanges not 	intended for tape.

D.  Apply joint tape over gypsum board joints and to flanges of trim accessories as recommended by 	trim accessory manufacturer.

E.  Gypsum Board Finish Levels:   Finish panels to levels indicated below, according to ASTM C 	840, for locations indicated:

1.   	Level 1: At ceiling plenum areas, concealed areas, and where indicated, unless a 	higher 	level of finish is required for fire-resistance-rated assemblies and sound-	rated 	assemblies.

2.   	Level 4: At panel surfaces that will be exposed to view, unless otherwise 	indicated.

F. 	Where Level 1 gypsum board finish is indicated, embed tape in joint compound. Surface shall be 	free of excess joint compound.

G.  	For Level 4 gypsum board finish, embed tape in joint compound and apply first, fill 		(second), and finish (third) coats of joint compound over joints, angles, fastener heads and 	accessories. Touch up and sand between coats and after last coat as needed to produce a surface 	free of visual defects and ready for decoration.

1.  	At tapered edge joints, draw the compound down to a level plane, leaving a 	monolithic surface that is flush with the paper face. Finish coat shall be feathered 	a minimum of 8-inches beyond both sides of the center of joint tape.

2.	At end to end butt joints, draw the compound down to minimize the hump created 	by the joint tape application. Finish coat shall be feathered to a minimum of 16-inches 	beyond both sides of the center of the joint tape.

3.	The end product shall be a surface that appears level without telegraphing joint 	locations as high spots when viewed down the wall after painting.

4.  	Finish board to within 1/4 inch of the floor, providing full support for resilient wall 	base without telegraphing joint.

3.12    	FIELD QUALITY CONTROL

A.	Above-Ceiling Observation: Before Contractor installs gypsum board ceilings, Architect 	will 	conduct an above-ceiling observation and report deficiencies in the Work observed. Do not 	proceed with installation of gypsum board to ceiling support framing until deficiencies have been 	corrected.

- Notify Architect seven days in advance of date and time when Project, or part of 	Project 	will be ready for above-ceiling observation.

- Before notifying architect, complete the following areas to receive gypsum board 	ceilings:

  - Installation of 80 percent of lighting fixtures, powered for operation.

  - Installation, insulation, and leak and pressure testing of water piping 	systems.

  - Installation of air-duct systems

  - Installation of air devices

  - Installation of mechanical system control-air tubing

  - Installation of above ceiling automatic fire suppression piping, including 	leak 	and pressure testing

  - Installation of ceiling support framing.

3.13    	CLEANING AND PROTECTION

- Promptly remove any residual joint compound from adjacent surfaces.

- Protect installed products from damage from weather, condensation, direct sunlight, 	construction, and other causes during remainder of the construction period.

- Remove and replace panels that are wet, moisture damaged, or mold damaged.

  - Indications that panels are wet or moisture damaged include, but are not limited 	to, 	discoloration, sagging or irregular shape.

  - Indications that panels are mold damaged include, but are not limited to, fuzzy or 	splotchy surface contamination and discoloration.

- Provide final protection and maintain conditions, in a manner acceptable to installer, that 	ensure 	gypsum board assemblies are without damage or deterioration at the time of substantial 	completion.

END OF SECTION09260