SECTION 09310

CERAMIC TILE

PART 1 - GENERAL

1.01	RELATED DOCUMENTS

A.	Drawings and general provisions of the Contract, including General and Supplementary

Conditions and Division 1 Specification Sections, apply to this Section.

1.02	SUMMARY

A.	This Section includes the following:

1.	Floor Tile and Wall Tile (porcelain).

2.	Crack-suppression membrane for thin-set tile installations.

3.	Metal edge strips installed as part of tile installations.

B.	Related Sections include the following:

1.	Division 3 Section "Cast-in-Place Concrete" for monolithic slab finishes specified for tile 				substrates.

2.	Division 7 Section "Joint Sealants" for sealing of expansion, contraction, control, and

isolation joints in tile surfaces.

3.	Division 9 Section "Gypsum Board Assemblies" for glass-mat, water-resistant backer

board.

1.03	SUBMITTALS

A.	General:  Submit in accordance with Section 01330.

B.	Product Data:  For each type of product indicated.

C.	Shop Drawings:  Show locations of each type of tile and tile pattern.  Show widths, details, 	and 	locations of expansion, contraction, control, and isolation joints in tile substrates and 	finished tile 	surfaces.

D.	Samples: Submit Samples of grout consisting of strips of actual products showing full range of 	colors available.

1.04	QUALITY ASSURANCE

A.	Source Limitations for Tile:  Obtain all tile of same type from one source or producer.

1.	Obtain tile from same production run and of consistent quality in appearance and

physical properties for each contiguous area.

B.	Source Limitations for Setting and Grouting Materials:  Obtain ingredients of a uniform 	quality 	for each mortar, adhesive, and grout component from a single manufacturer and 	each aggregate 	from one source or producer.

C.	Source Limitations for Other Products:  Obtain each of the following products specified in 	this 	Section through one source from a single manufacturer for each product:

1.	Crack-suppression membrane.

2.	Metal edge strips.

D.	Preinstallation Conference:  Conduct conference at Project site to comply with requirements 	in 	Division 1 Section "Project Management and Coordination."

1.05	DELIVERY, STORAGE, AND HANDLING

A.	Deliver and store packaged materials in original containers with seals unbroken and labels 	intact 	until time of use.  Comply with requirement in ANSI A137.1 for labeling sealed tile 	packages.

B.	Store tile and Cementitious materials on elevated platforms, under cover, and in a dry 	location.

C.	Prevent damage or contamination to materials by water, freezing, foreign matter, and other

causes.

1.06	PROJECT CONDITIONS

A.	Environmental Limitations:  Do not install tile until construction in spaces is complete and

ambient and substrate temperatures and humidity conditions are maintained at the levels

indicated in referenced standards and manufacturer's written instructions.

1. 	Maintain temperatures at 50 deg F or more in tiled areas during installation and for 7 									days	after completion, unless higher temperatures are required by referenced 	installation 				standard or 	manufacturer's instructions.

B.	Vent temporary heaters to exterior to prevent damage to tile work from carbon dioxide 	buildup.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

A.	In other Part 2 articles where titles below introduce lists, the following requirements apply 	for 	product selection:

1.	Products:  Subject to compliance with requirements, provide one of the products

specified.

2.	Manufacturers:  Subject to compliance with requirements, provide products by one of 	the 				manufacturers specified.

2.02	PRODUCTS, GENERAL

A.	ANSI Ceramic Tile Standard:  Provide tile that complies with ANSI A137.1, 	"Specifications 	for 	Ceramic Tile," for types, compositions, and other characteristics 	indicated.

1.	Provide tile complying with Standard grade requirements, unless otherwise indicated.

B.	ANSI Standards for Tile Installation Materials:  Provide materials complying with ANSI

standards referenced in "Setting and Grouting Materials" Article.

C.	Colors, Textures, and Patterns:  Where manufacturer's standard products are indicated for 	tile, 	grouts, and other products requiring selection of colors, surface textures, patterns, and 	other 	appearance characteristics, provide specific products or materials complying with the 	following 	requirements:

1.	As indicated by manufacturer's designations on Interior Finish Legend.

D.	Factory Blending:  For tile exhibiting color variations within ranges selected during Sample

submittals blend tile in factory and package so tile units taken from one package show 		same 	range in colors as those taken from other packages and match approved Samples.

2.03	TILE PRODUCTS

A.	Porcelain Floor Tile, T1:  Provide flat tile complying with the following requirements:

1.	Composition:  Porcelain.

2.	Fascial Dimensions:  24 b-inches by 24-inches.

3.	Thickness:  7/16-inch.

4.	Face:

a.	T1:  Plain with square edge.

5.	Trim Unit: Cove base 4- by 12-inches.

6.	Product: RAGNO, Metropolitan Porcelain Stoneware.

a.	Colors:  As indicated in Interior Finish Legend.

b.	Locations:  As indicated in the documents.

c.	Grout width:  7/16-inch

B.	Porcelain Wall Tile, T2:  Provide flat tile complying with the following requirements:

1.	Composition:  Porcelain.

2.	Fascial Dimensions:  12- by 24-inches.

3.	Thickness:  7/16-inch.

4.	Face:

a.	T2:  Plain with square edge.

5.	Trim Unit: As required for wall installation.

6.	Product: Marazzi, Stone collection..

a.	Colors:  As indicated in Interior Finish Legend.

b.	Locations:  A indicated in the documents.

c.	Grout width:  3/16-inch.

2.04	CRACK-SUPPRESSION MEMBRANES FOR THIN-SET TILE INSTALLATIONS

A.	General:  Manufacturer's standard product that complies with ANSI A118.10.

B.	Anti-Fracture Membrane:  Consisting of a two-part, liquid rubber, and fabric reinforcement;

applied over all floor cracks and saw cuts with Laticrete latex thin-set mortar.

1.	Location:  Use under porcelain paver tile and stone hearths.

2.	Product:  Laticrete Blue 92 Anti-Fracture Membrane; LATICRETE International Inc.

2.05	SETTING AND GROUTING MATERIALS

A.	Latex-Portland Cement Mortar (Thin Set) and Grout, G1:  ANSI A118.4 and ANSI A118.6

respectively, consisting of the following:

1.	Prepackaged dry-mortar mix combined with acrylic resin liquid-latex additive.

2.	Manufacturer: MAPEI Corporation.

3.	Colors:  As selected by Architect from manufacturer's full range of options.

B.	Organic Adhesive: Premium Grade emulsion based adhesive conforming to ANSI A136.1, Type I.

2.06	ELASTOMERIC SEALANTS

A.	General:  Provide manufacturer's standard chemically curing, Elastomeric sealants of base

polymer and characteristics indicated that comply with applicable requirements in Division 	7 	Section "Joint Sealants."

B.	Colors:  Provide colors of exposed sealants to match colors of grout in tile adjoining sealed

joints, unless otherwise indicated.

2.07	MISCELLANEOUS MATERIALS

A.	Trowelable Underlayment and Patching Compounds:  Latex-modified, Portland cement-	based 	formulation provided or approved by manufacturer of tile-setting materials for 	installations 	indicated.  Flat and wall surfaces.

B.	Metal Edge Strips:  L-shape, zinc alloy or stainless steel terrazzo strips, 1/8-inch wide at top

edge with integral provision for anchorage to mortar bed or substrate unless otherwise 	indicated.

1.	Product: Schluter-SCHIENE.

C.	Control Joints (CJ):  Control joints for porcelain tile, thermoplastic movement joint with

opposing metal profiles.

1.	Product:  Schluter DILEX-KS.

D.	Tile Cleaner:  A neutral cleaner capable of removing soil and residue without harming tile and 	grout surfaces, specifically approved for materials and installations indicated by tile 	and grout 	manufacturers.

E.	Grout Sealer:  Manufacturer's standard product for sealing grout joints that does not change

color or appearance of grout.

1.	Products:

a.	Bostik; CeramaSeal Grout Sealer.

b.	MAPEI Corporation; KER 004, Keraseal Penetrating Sealer for Unglazed Grout and 				Tile.

2.	Installation:  Seal material that is clean and residue- and debris-free and prior to accepting 						foot traffic.

2.08	MIXING MORTARS AND GROUT

A.   	Mix mortars and grouts to comply with referenced standards and mortar and grout

manufacturers' written instructions, including those for accurate proportioning of materials,

water, or additive content; type of mixing equipment, selection of mixer speeds, mixing

containers, mixing time, and other procedures needed to produce mortars and grouts of 	uniform 	quality with optimum performance characteristics for application indicated.

B.	Obtain and use type of mixing equipment, mixer speeds, mixing containers, mixing time, and 	other procedures to produce mortars and grouts of uniform quality with optimum 	performance 	characteristics for installations indicated.

PART 3 - EXECUTION

3.01	EXAMINATION

A.	Examine substrates, areas, and conditions where tile will be installed, with Installer present, for 	compliance with requirements for installation tolerances and other conditions affecting 	performance of installed tile.

1. 	Check flatness of substrate.  Level floor to provide a base for thin set that allows for a

smooth, flat floor without irregularities. Grinding high spots until substrate is acceptable to 			the flooring Installer is specified in Section 03300.

2. 	Verify that substrates for setting tile are firm; dry; clean; free of oil, waxy films, and

curing compounds; and within flatness tolerances required by referenced ANSI A108 								Series of tile installation standards for installations indicated.

3.	Verify that installation of grounds, anchors, recessed frames, electrical and 	mechanical 						units of work, and similar items located in or behind tile has been 	completed before 									installing tile.

B.	Proceed with installation only after unsatisfactory conditions have been corrected.

C.	Lay tile in patterns indicated.  When field conditions conflict with indicated pattern, notify

Architect in advance of installation for review and approval of revisions.

3.02	PREPARATION

A.	Remove coatings, including curing compounds and other substances that contain soap, 	wax, oil, 	or silicone, that are incompatible with tile-setting materials.

B.	Provide concrete substrates for tile floors installed with thin-set mortar that comply with

flatness tolerances specified in referenced ANSI A108 Series of tile installation standards.

1.	Fill cracks, holes, and depressions with Trowelable leveling and patching compound

according to tile-setting material manufacturer's written instructions. Use product

specifically recommended by tile-setting material manufacturer.

2.	Remove protrusions, bumps, and ridges by sanding or grinding.

C.	Blending:  For tile exhibiting color variations within ranges selected during Sample submittals, 	verify that tile has been factory blended and packaged so tile units taken from 	one package show 	same range of colors as those taken from other packages and match 	approved Samples.  If not 	factory blended, either return to manufacturer or blend tiles at 	Project site before installing.

D.	Provide proper surface preparation for wall tiles and backing.

3.03	INSTALLATION, GENERAL

A.	ANSI Tile Installation Standards:  Comply with parts of ANSI A108 Series "Specifications 	for 	Installation of Ceramic Tile" that apply to types of setting and grouting materials and to 	methods 	indicated in ceramic tile installation schedules.

B. 	TCA Installation Guidelines:  TCA's "Handbook for Ceramic Tile Installation." Comply	with 	TCA installation methods indicated in the Tile Installation Schedule.

C. 	Extend tile work into recesses and under or behind equipment and fixtures to form 	complete 	covering without interruptions, unless otherwise indicated.  Terminate work 	neatly at 	obstructions, edges, and corners without disrupting pattern or joint alignments.

D. 	Accurately form intersections and returns.  Perform cutting and drilling of tile without 	marring 	visible surfaces.  Carefully grind cut edges of tile abutting trim, finish, or built-in 	items for 	straight aligned joints.  Fit tile closely to electrical outlets, piping, fixtures, and 	other penetrations 	so plates, collars, or covers overlap tile.  Top setting of coved base is not 	permitted.

E.	Tile shall lay flat and each edge flush with adjacent tile, free of tilting and skewed tile.  	Provide 	additional setting material to shim accent tiles that are thinner than the field tiles so 	face is in the 	same plane.

F. 	Jointing Pattern:  Lay tile in grid pattern, unless otherwise indicated.  Align joints when adjoining 	tiles on floor, base, walls, and trim are same size.  Lay out tile work and center 	tile 	fields in both 	directions in each space or on each wall area.  Adjust to minimize tile 	cutting. 	Provide uniform 	joint widths, unless otherwise indicated.

G. 	Expansion Joints:  Locate expansion joints and other sealant-filled joints, including control,

contraction, and isolation joints, where indicated during installation of setting materials, 	mortar 	beds, and tile.  Do not saw-cut joints after installing tiles.

1. 	Locate expansion joints in accordance with approved Shop Drawings.  Space joints no 							greater than 36 feet apart, 16 feet apart at areas exposed to direct sunlight.

2.	Prepare joints and apply sealants to comply with requirements in Division 7 Section "Joint 			Sealants."

H.	Grout tile to comply with requirements of the following tile installation standards:

1.	for ceramic tile grouts (latex-Portland cement grouts), comply with ANSI A108.10.

3.04	CRACK-SUPPRESSION MEMBRANE INSTALLATION

A.	Install crack-suppression membrane to comply with manufacturer's written instructions to

produce membrane of uniform thickness bonded securely to substrate.

3.05	FLOOR TILE INSTALLATION

A.	General:  Install tile to comply with requirements in the Floor Tile Installation Schedule,

including those referencing TCA installation methods and ANSI A108 Series of tile 	installation 	standards.

1.	For installations indicated below, follow procedures in ANSI A108 Series tile installation 				standards for providing 95 percent mortar coverage.

a.	Tile floors composed of tiles 8- by 8-inches or larger.

B.	Joint Width:  Install tile on floors with the following joint width:

1.	Tile:   Per manufacturer's recommended installation guidelines.

C.	Metal Edge Strips:  Install at locations indicated or where exposed edge of tile flooring 	meets 	carpet, wood, or other flooring that finishes flush with top of tile.

3.06	WALL TILE INSTALLATION

A.	Install types of tile designated for wall installations to comply with requirements in the 	Wall Tile 	Installation Schedule, including those referencing TCA installation methods and 	ANSI setting-	bed standards.

B.	Joint Width:  Install tile on walls with the following joint width:

1.	Tile:  Per manufacturer's recommended installation guidelines.

3.07	CLEANING AND PROTECTING

A.	Cleaning:  On completion of placement and grouting, clean all ceramic tile surfaces so they 	are 	free of foreign matter.

1.	Remove latex-Portland cement grout residue from tile as soon as possible.

2.	Clean grout smears and haze from tile according to tile and grout manufacturer's written 					instructions, but no sooner than 10 days after installation. Use only cleaners 	recommended 		by tile and grout manufacturers and only after determining that cleaners are safe to use by 				testing on samples of tile and other surfaces to be cleaned.  	Protect metal surfaces and 								plumbing fixtures from effects of cleaning. Flush surfaces	with clean water before and after 		cleaning.

B. 	When recommended by tile manufacturer, apply coat of neutral protective cleaner to 	completed 	tile walls and floors.  Protect installed tile work with Kraft paper or other heavy 	covering during 	construction period to prevent staining, damage, and wear.

C.	Prohibit foot and wheel traffic from tiled floors for at least seven days after grouting is completed.

D.	Before final inspection, remove protective coverings and rinse neutral cleaner from tile 	surfaces.

3.08	TILE INSTALLATION SCHEDULE

A.	Porcelain Tile over Concrete Floor:  Thin-set latex Portland cement mortar tile

setting bed over anti-fracture membrane, TCA F113 modified.

END OF SECTION 09310