Copyright 2003 and 2005 by The American Institute of Architects (AIA)

Exclusively published and distributed by Architectural Computer Services, Inc. (ARCOM) for the AIA

SECTION 09650

RESILIENT FLOORING

This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 01 Specification Sections, apply to this Section.

SUMMARY

This Section includes the following:

Adjust list below to suit Project.

Vinyl composition tile (VCT)

Sheet vinyl floor covering

Resilient wall base, reducer strips, and other accessories.

Related Sections include the following:

List below only products and construction that the reader might expect to find in this Section but are specified elsewhere.

Division 06 Section "Sheathing" for roof sheathing and subflooring.

Borate treatment in Section referenced in first subparagraph below may be an acceptable substitute for borate-treated wood specified in this Section.  Delete if borate treatment is specified in this Section.

Retain paragraph below if an allowance is specified for permanent bracing.  If retaining below, indicate in Division 01 Section "Allowances" that allowance includes installation as well as materials.  Delete if bracing is shown on Drawings.

Allowances:  Provide wood truss bracing under the Metal-Plate-Connected Truss Bracing Allowance as specified in Division 01 Section "Allowances."

SUBMITTALS

General:  Submit in accordance with Section 01330.

Product Data:  For each type of product indicated.

Samples:  For each type of product indicated. Samples shall be in form of manufacturer's color charts consisting of the following:

1.	Welding Beach:  Color charts consisting of strips of welding bead showing full range 			of colors available for each manufacturer.

2.	Resilient Accessories:  Color charts consisting of strips of resilient base showing full 				range of colors available for each product exposed to view.

D.	Test Results:  Provide results of specified alkalinity and adhesion tests, calcium chloride 		moisture tests, and relative humidity test specified. Include manufacturer's written moisture 	requirements for each resilient flooring type specified.

E.	Product Certifications:  Signed by resilient flooring manufacturer of products supplied that 	comply with the specifications and state/local regulations controlling the use of volatile organic 	compounds (VOC's).

F.	Qualification Data:  For Installer of sheet vinyl flooring.

G.	Maintenance Data:  For resilient products to include in maintenance manuals.

1.4		QUALITY ASSURANCE

A.	Sheet Vinyl Installer Qualifications:  A qualified Installer who employs workers for this Project 			that are competent in heat-welding techniques required by manufacturer for floor covering 				installation.

B.	Source Limitations for Sheet Vinyl Flooring:  Obtain each type, color, and patter of sheet vinyl 			flooring from a single source with resources to provide products of consistent quality in 					appearance and physical properties without delaying progress of the Work.

1.5		DELIVERY, STORAGE, AND HANDLING

A.	Deliver resilient flooring materials and installation accessories to project site in original 					manufacturer's unopened cartons and containers each bearing name of product and 						manufacturer, Project identification, and shipping and handling instructions.

B.	Store resilient products and installation materials in dry spaces protected from the weather, with 		ambient temperatures maintained within range recommended by manufacturer, but not less than 		50 degrees Fahrenheit or more than 90 degrees Fahrenheit. Store tiles on flat surfaces and 				rolls upright.

C.	Move flooring materials and accessories and installation products into spaces where they will be 		installed at least 48 hours in advance of installation. Do not install flooring materials until they 			are at the same temperature as the space where they are to be installed.

1.6		PROJECT CONDITIONS

A.	Maintain ambient and substrate temperatures with range recommended by manufacturer, but 			not less than 70 degrees Fahrenheit or more than 85 degrees Fahrenheit, in spaces to receive 			floor tile during the following time periods:

1.	48 hours before installation.

2.	During installation.

3.	48 hours after installation.

B.	After post installation period, maintain temperatures within range recommended by 					manufacturer, but not less than 55 degrees Fahrenheit or more than 95 degrees Fahrenheit.

C.	Close spaces to traffic during floor covering installation.

D.	Close spaces to traffic for 48 hours after floor covering installation.

1.7		SEQUENCE AND SCHEDULING

A.	Install resilient products after other finishing operations, including painting, have been 					completed.

B.	Do not install flooring over concrete slabs until slabs have cured and are efficiently dry to bond 			with adhesive as determined by manufacturer's recommended bond and moisture test.

1.8		EXTRA MATERIALS

A.	Furnish extra materials described below that match products installed and that are packaged 				with protective covering for storage and identified with labels describing contents.

1.	Floor Tile:  Furnish 1 box of each type, color, and pattern of floor tile installed.

2.	Sheet Rubber Flooring:  Furnish not less than 10 linear feet for every 500 linear feet or 				fraction thereof, in roll form and in full roll width for each color, pattern, and type of 					floor covering installed.

3.	Sheet Vinyl Flooring:  Furnish not less than 10 linear feet for every 500 linear feet or 					fraction thereof, in roll form and in full roll width for each color, pattern, and type of 						floor covering installed.

4.	Resilient Wall Base and Accessories:  Furnish not less than 10 linear feet for every 500 				linear feet or fraction thereof, of each type, color, pattern, and size of resilient product 				installed.

PART 2 – PRODUCTS

2.1	MANUFACTURERS

A.	Products:  Subject to compliance with requirements, provide one of the products listed in other 			Part 2 articles.

2.2		VINYL COMPOSITION TILE

A.	Vinyl Composition Tile, VCT1: ASTM F 1066

1.	Product: Mannington Commercial

a.	Colors – As indicated in Interior Finish Legend.

2.	Class: 2 (through pattern tile).

3.	Wearing Surface: Smooth

4.	Thickness:  0.125-inch.

5.	Size: 12-inches by 12-inches.

6.	Fire-Test-Response Characteristics:

a.	Critical Radiant Flux Classifications – Class 1, not less than 0.45 W/sq. cm per 						ASTM E648.

2.3		SHEET VINYL FLOORING

A.	Sheet Vinyl Floor Covering RI:  ASTM F 1303.

1.	Product:  Armstrong, Timberline

a.	Color:  As indicated in Interior Finish Legend.

2.	Thickness:  0.080-inch.

3.	Wear Layer Thickness:  0.024-inch.

4.	Wearing Surface:  Smooth

5.	Sheet Width:  6-feet 7-inches.

6.	Seaming Method:  Heat welded.

7.	Static Coefficient of Friction:  Complies with ASTM D 2047.

8.	Warranty:  5 years from date of Substantial Completion.

2.4		RESILIENT WALL BASE

A.	Vinyl Wall Base, VCB1 & VCB2:  ASTM F 1861.

1.	Product: Vinyl Cove Wall Base - Johnsonite

a.	Colors – As indicated in Interior Finish Legend.

2.	Type (Material Requirement):  TV (vinyl).

3.	Group (Manufacturer Method):  1 (solid).

4.	Style:  Cove (with top-set toe)

5.	Minimum Thickness:  0.125-inch.

6.	Height:  4-inches.

7.	Lengths:  Coils in manufacturer's standard length.

8.	Inside and Outside Corners:  Job formed.

9.	Surface:  Smooth.

2.5		RESILIENT MOLDING ACCESSORY

A.	Description:  Flooring Transition Strips.

1.	Manufacturer:  Johnsonite

B.	Material:  Vinyl

C.	Transition Strips:  The following product identification numbers are for products manufacturer 			by Johnsonite.

1.	Carpet to Resilient:  No. CTA-XX-D.

2.6		SHEET VINYL ACCESSORIES

A.	Heat-Welding Beach:  Solid-strand product of floor covering manufacturer.

1.	Color:  As selected by Architect from manufacturer's full range.

B.	Integral-Flash-Cover Accessories:

1.	Cover Strip:  1-inch radius provided or approved by floor covering manufacturer.

2.	Cap Strip:  Vinyl cap provided or approved by floor covering manufacturer.

2.7		INSTALLATION MATERIALS

A.	Concrete Slab Primer:  No staining type as recommended by flooring manufacturer.

B.	Trowelable Leveling and Patching Compounds:  Latex-modified, Portland cement based or 				blended hydraulic cement based formulation provided or approved by resilient product 					manufacturer for applications indicated.

1.	Product:  Ardex; SD-F Feather Finish.

C.	Latex Adhesives (Cements):  Premium Grade, water-resistant type recommended by 					manufacturer to suit resilient products and substrate conditions indicated.

PART 3 – EXECUTION

3.1		EXAMINATION

A.	Examine substrates, with Installer present, for compliance with requirements for installation 			tolerances, moisture content, and other conditions affecting performance.

1.	Verify that substrates comply with tolerances and other requirements specified in other 				Sections and those substrates are free of cracks, ridges, depressions, scale, and foreign 				deposits that might interfere with adhesion of resilient products.

B.	Proceed with installation only after unsatisfactory conditions have been corrected.

3.2		PREPARATION

A.	Prepare substrates according to manufacturer's written recommendations to ensure adhesion of 			resilient products.

B.	Concrete Substrates:  Verify that concrete slabs comply with ASTM F 710 and the following:

1.	Verify that substrates are dry and free of curing compounds, sealers, hardeners, and other 				material whose presence would interfere with bonding of adhesive. Determine adhesion 				and dryness characteristics by performing bond and moisture tests recommended by 					flooring manufacturer, and with the specified requirements.

2.	An independent testing agency shall perform alkalinity and adhesion tests, calcium 					chloride moisture tests, and relative humidity test. Testing shall be conducted as follows:

a.	Maintain a minimum temperature of 70 degrees Fahrenheit in spaces to receive 						flooring for at least 72 hours prior to and during the tests.

b.	Perform the tests at rate of not less than 1 test/1000 sq. ft. of floor area for 							slabs-on-grade.

c.	Provide additional tests on floors after radiant heat has been in operation for not less 					than 2 weeks. Perform tests while system is operating.

3.	Alkalinity and Adhesion Testing:  Perform tests recommended by manufacturer. Proceed 				with installation only after substrates pass testing.

4.	Moisture Testing:

a.	Anhydrous Calcium Chloride Test:  Perform test in accordance with 									recommendations of flooring manufacturer and ASTM F 1869, except area of CaC12 					dish shall not be deducted.

b.	Relative Humidity Test:  Perform test using in situ probes, ASTM F 2170.

5.	Proceed with installation only after substrates have maximum moisture-vapor-emission 				rate of 3 lbs of water/1000 sq. ft in 24 hours, a maximum 75% relative humidity level 				measurement, and manufacturer's requirements for alkalinity and adhesion are met.

C.	Remove substrate coatings and other substances that are incompatible with adhesives and that 			contain soap, wax, oil, or silicone, using mechanical methods recommended by manufacturer. 			Do Not Use Solvents.

D.	Use trowelable leveling and patching compound to fill cracks, holes, and depressions in 				substrates.

E.	Move resilient products and installation materials into spaces where they will be installed at 			least 48 hours in advance of installation.

F.	Sweep and vacuum clean substrates to be covered by resilient products immediately before 				installation. After cleaning, examine substrates for moisture, alkaline salts, carbonation, and 			dust. Proceed with installation only after unsatisfactory conditions have been corrected.

3.3		TILE INSTALLATION

A.	Install in accordance with the manufacturer's written instructions and the requirements of this 			Section.

B.	Lay out tiles from center marks established with principal walls, discounting minor offsets, so 			tiles at opposite edges of room are of equal width. Adjust as necessary to avoid using cut widths 		that equal less than one-half tile at perimeter. Install tiles square with room axis, unless 					otherwise indicated.

C.	Match tiles for color and pattern by selecting tiles from cartons in the same sequence as 				manufactured and packaged, if so numbered. Discard broken, cracked, chipped, or deformed 			tiles.

1.	Verify pattern and grain direction with Architect prior to installation.

D.	Adhere tiles to flooring substrates using a full spread of adhesive applied to substrate to 				produce a completed installation without open cracks, voids, raising, and puckering at joints, 			telegraphing of adhesive spreader marks, and other surface imperfections.

E.	Hand roll tiles where required by tile manufacturer.

3.4	INSTALLATION OF SHEET FLOOR COVERING

A.	Unroll sheet floor coverings and allow them to stabilize before cutting and fitting.

B.	Lay out sheet floor coverings as follows:

1.	Maintain uniformity of floor covering direction.

2.	Minimize number of seams; place seams in inconspicuous and low-traffic areas; at least 				6-inches away from parallel joints in floor covering substrates.

3.	Match edges of floor coverings for color shading and pattern at seams.

4.	No cross seams.

C.	Adhere floor coverings to substrates using a full spread of adhesive applied to substrate to 				produce a completed installation without open cracks, voids, raising and puckering at joints, 			telegraphing of adhesive spreader marks, and other surface imperfections. Comply with floor 			covering manufacturer's directions, including those for trowel notching, adhesive mixing, and 			adhesive open and working times.

D.	Heat-Welded Seams:  Comply with ASTM F 1516. Rout joints and use welding bead to 				permanently fuse sections into a seamless floor covering. Prepare, weld, and finish seams to 			produce surfaces flush with adjoining floor covering surfaces.

E.	Integral Flash Cove Base:  Where indicated, cove floor coverings 6-inches up vertical surfaces. 			Support floor coverings at horizontal and vertical junction by cove strip. Butt at top against cap 			strip. Form inside and outside corners uniformly, without tears, open joints or irregularities.

F.	Hand roll sheet vinyl floor coverings in both directions from center out to embed floor 					coverings in adhesive and eliminate trapped air. At walls, door casings, and other locations 				where access by roller is impractical, press floor coverings firmly in place with flat-bladed 				instrument.

3.5	RESILIENT WALL BASE INSTALLATION

A.	Apply wall base to walls, columns, pilasters, casework and cabinets in toe spaces, and other 			permanent fixtures in rooms and areas where base is required. Where toe space is less than 4-			inches, cut down base to proper height.

B.	Install straight base before installation of carpet.

C.	Install wall base in lengths as long as practicable without gaps at seams and with tops of 				adjacent pieces aligned.

D.	Tightly adhere wall base to substrates throughout length of each piece, with base in continuous 			contact with horizontal and vertical substrates.

E.	Do not stretch wall base during installation.

F.	Job-Formed Corners:

1.	Outside Corners:  Use straight pieces of maximum lengths possible. Form without 					producing discoloration (whitening) at bends. Shave back of base at points where bends 				occur and remove strips perpendicular to length of base that are only deep enough to 					produce snug fit without removing more than half the wall base thickness.

2.	Inside Corners: Use straight pieces of maximum lengths possible. Form by cutting an 				inverted V-shaped notch in toe of wall base at the point where corner is formed. Shave 				back of base where necessary to produce a snug fit to substrate.

3.	Adhere base to substrate with contact adhesive 12-inches each side of outside corner to 				properly hold base in permanent proper position in tight contact with wall. Base shall run 				continuous around corners with butt joints 12-inches minimum for corner.

G.	Molded Resilient Wall Base:  Inside and outside corners shall be miter cut and fitted using a 			compound miter saw in the field.

3.8		CLEANING AND PROTECTION

A.	Perform the following operations immediately after completing resilient product installation:

1.	Remove adhesive and other blemishes from exposed surfaces using cleaner 							recommended by resilient products manufacturers.

2.	Sweep and vacuum surfaces thoroughly.

3.	Damp mop surface to remove marks and soil.

a.	Do not wash surfaces until after time period recommended by manufacturer.

B.	Protect resilient products from mars, marks, indentations, and other damage from construction 			operations and placement of equipment and fixtures during remainder of construction period. 			Use protection methods recommended in writing by manufacturer.

1.	Do not move heavy and sharp objects directly over surfaces. Place hardboard or plywood 				panels over flooring and under objects while they are being moved. Slide or roll objects 				over panels without moving panels.

C.	Final cleaning and buffing specified in Division 1 Section "Closeout Procedures."

END OF SECTION