SECTION 09900

PAINTING

PART I – GENERAL

1.01	RELATED DOCUMENTS

A.	Drawings and general provisions of the Contract, including General and Supplementary 			Conditions and Division I Specification Sections, apply to this Section.

1.02	SUMMARY

A.	This Section includes the following:

1.	Exposed interior items and surfaces with low VOC coatings complying with ME 					DEP regulations.

2.	Surface preparation, priming, and finish coats specified in this Section are in 					addition to shop priming and surface treatment specified in other Sections.

B.	Related Sections include the following:

1.	Division 6, Section "Finish Carpentry" for surface preparation of exterior and 					interior standing and running trim, siding and finish carpentry.

2.	Division 6, Section "Architectural Woodwork" for shop finishing of architectural 					casework.

3.	Division 9, Section "Gypsum Board Assemblies" for surface preparation of 					gypsum board.

4.	Review all sections for shop primed items requiring field painting.

1.03	DEFINITIONS

A.	General:  Standard coating terms defined in ASTM D 16 apply to this Section.

1.	Flat refers to a lusterless or matte finish with a gloss range below 15 when 					measured at an 85-degree meter.

2.	Eggshell refers to low-sheen finish with a gloss range between 20 and 35 when 					measured at a 60-degree meter.

3.	Satin refers to low-sheen finish with a gloss range between 15 and 35 when 					measured at a 60-degree meter.

4.	Semi gloss refers to medium-sheen finish with a gloss range between 35 and 70 					when measured at a 60-degree meter.

5.	Full gloss refers to high-sheen finish with a gloss range more than 70 when 					measured at a 60-degree meter.

1.04	SUBMITTALS

A.	General:  Submit in accordance with Section 01330.

B.	Product Data:  For each paint system indicated. Include block fillers and primers.

1.	Material List:  An inclusive list of required coating materials. Indicate each 					material and cross-reference specific coating, finish system, and application. 				Identify each material by manufacturer's catalog number and general 						classification.

2.	Manufacturer's Information:  Manufacturer's technical information, including 					label analysis and instructions for handling, storing, and applying each coating 					material proposed for use.

3.	VOC Limits:  Manufacturer's product data for paints and coatings, including 					printed statement of VOC content and chemical components.

C.	Schedule:  Provide schedule of all surfaces to be coated, with prime and finish coat 				material listed, and manufacturer's recommended wet film thickness.

D.	Samples:  For each type of exposed finish required, submit color chips, 3-inches by

5-inches, matching colors indicated on Finish Schedule.

E.	Manufacturer Certificates:  Signed by manufacturer certifying that product(s) with 				limit VOC amounts specified comply with requirements.

F.	Qualifications Data:  For Applicator.

1.05	QUALITY ASSURANCE

A.	Applicator Qualifications:  Engage an experienced Applicator who has completed 				painting system applications similar in material, design, and extent to those indicated 				for this Project, whose work has resulted in applications with a record of successful in-				service performance.

B.	Source Limitations:  Obtain block fillers, primers and undercoat materials for each 				coating system from the same manufacturer as the finish coats.

C.	Benchmark Samples (Mockups):  Provide a full-coat benchmark finish sample for each 				type of coating and substrate required. Duplicate finish of approved sample Submittals.

1.	Architect will select one room or surface to represent surfaces and conditions for 					each type of coating and substrate to be painted.

a.	Wall Surfaces:  Provide samples of at least 100 sq. ft.

b.	Small Areas and Items:  Architect will designate items or areas required.

2.	After permanent lighting and other environmental services have been activated, 					apply benchmark samples, according to r3equirements for completed Work. 					Provide required sheen, color, and texture on each surface.

3.	Final approval of colors will be from benchmark samples.

1.06	DELIVERY, STORAGE, AND HANDLING

A.	Deliver materials to the Project Site in manufacturer's original, unopened packages and 				containers bearing manufacturer's name and label, and the following information:

1.	Product name or title of material.

2.	Product description (generic classification or binder type).

3.	Manufacturer's stock number and date of manufacture.

4.	Contents by volume, for pigment and vehicle constituents.

5.	Thinning instructions.

6.	Application instructions

7.	Color name and number.

8.	VOC content.

B.	Store materials that are not in use in tightly covered containers in a well-ventilated area 				at a minimum ambient temperature of 45 deg F. Maintain containers used for storage in 			a clean condition, free of foreign materials and residue.

1.	Protect from freezing. Keep storage area neat and orderly.

2.	Remove oily rags and waste daily.

3.	Take necessary measures to ensure that workers and work areas are protected 				from fire and health hazards resulting from handling, mixing, and application.

1.07	PROJECT CONDITIONS

A.	Apply paints only when temperatures of surfaces to be painted and surrounding air are 				between 45 and 95 deg F.

B.	Do not apply paint in snow, rain, fog, or mist; or when relative humidity exceeds 85 				percent; or at temperatures less than 5°F above the dew point; or to damp or wet 				surfaces.

1.	Painting may continue during inclement weather if surfaces and areas to be 					painted are enclosed and heated within temperature limits specified by 						manufacturer during application and drying periods.

2.	Allow wet surfaces to dry thoroughly and attain temperature and conditions 					specified before proceeding with or continuing coating operation.

1.08	EXTRA MATERIALS

A.	Furnish extra paint materials from the same production run as the materials applied and 			in the quantities described below. Package with protective covering for storage and 				identify with labels describing contents. Deliver extra materials to Owner.

1.	Quantity:  Furnish Owner with an additional 3 percent, but not less than 1 gal. or 					1 case, as appropriate, of each material and color applied.

PART 2 – PRODUCTS

2.01	MANUFACTURERS

A.	Products:  Subject to compliance with requirements, provide one of the products listed 				in other Part 2 articles.

B.	Manufacturers' Names:  Shortened versions (shown in parenthesis) of the following 				manufacturers' names are used in other Part 2 articles:

1.	Sherwin Williams Co. (S-W).

2.	Benjamin Moore & Company (Moore)

3.	ICI Dulux Paints (ICI)

4.	Samuel Cabot, Inc. (Cabot)

2.02	COATING MATERIALS – GENERAL

A.	Material Compatibility:  Provide primers, undercoats, and finish-coat materials that are 				compatible with one another and with the substrates indicated under conditions of 				service and application, as demonstrated by manufacturer based on testing and field 				experience.

B.	Material Quality:  Provide manufacturer's best quality coating material of the various 				coating types specified that are factory formulated and recommended by manufacturer 				for application indicated. Paint material containers not displaying manufacturer's 				product identification will not be acceptable.

1.	Where schedule says no substitutions, use proprietary product only. Do not 					propose substitutions, as the products from the other manufacturers have been 					considered, and are not acceptable.

C.	VOC Compliance for Paints and Coatings:  Provide the manufacturer's formulation for 				the products specified below that are VOC compliant with the State of Maine 					Department of Environmental Protection Regulation, "Chapter 151:  Architectural and 				Industrial Maintenance (AIM) Coatings" and the following chemical restrictions 				expressed in grams per liter:

1.	Plat Paints and Coatings:  VOC content of not more than 100 g/L.

2.	Non-Flat Paints and Coatings:  VOC content of not more than 150 g/L.

3.	Non-Flat Paints and Coatings – High Gloss:  VOC content of not more than 250 g/L.

4.	Anticorrosive (Rust Preventative) Coatings:  VOC content of not more than 400 g/L.

5.	Clear Wood Coatings:

a.	Clear Brushing Lacquers:  VOC content of not more than 680 g/L.

b.	Lacquers (including Lacquer Sanding Sealers):  VOC content of not more than 					550 g/L.

c.	Varnishes:  VOC content of not more than 350 g/L.

6.	Fire Retardant Coatings:

a.	Clear:  VOC content of not more than 650 g/L.

b.	Opaque:  VOC content of not more than 350 g/L.

7.	Primers, Sealers, and Undercoaters:  VOC content of not more than 200 g/L.

8.	Quick-Dry Enamels:  VOC content of not more than 250 g/L.

9.	Quick-Dry Primers, Sealers, and Undercoaters:  VOC content of not more than 200 g/L.

10.	Specialty Primers, Sealers, and Undercoaters:  VOC content of not more than 350 g/L.

11.	Stains:  VOC content of not more than 250 g/L.

D.	Colors:  Provide color selections made by the Architect.

PART 3 – EXECUTION

3.01	EXAMINATION

A.	Examine substrates, areas, and conditions, with Applicator and drywall subcontractor present, 			under which painting will be performed for compliance with paint application requirements.

1.	Inspect walls for dents and imperfections prior to painting. Inspect walls again after 				primer and first coat of paint applied, with Applicator and drywall subcontractor present.  			Drywall subcontractor shall touch-up as follows:

a.	Touch-up visible gypsum board imperfections before priming of walls.

b.	Touch-up imperfections found in field of boards and joints made visible from 					painting after first finish coat applied.

2.	If unacceptable conditions are encountered, prepare written report, endorsed by 					Applicator, listing conditions detriment to performance of work.

3.	Verify compatibility with and suitability of substrates, including compatibility with 				existing finishes or primers.

4.	Application coating indicates Applicator's acceptance of surfaces and conditions within a 				particular area.

5.	Being coating application only after unsatisfactory conditions have been corrected and 				surfaces are dry.

B.	Coordination of Work:  Review other Sections in which primers are provided to ensure 				compatibility of the total system for various substrates. On request, furnish information on 			characteristics of specified finish materials to ensure use of compatible primers.

1.	Notify Architect about anticipated problems when using the materials specified over 				substrates primed by others.

3.02	PREPARATION

A.	General:  Remove hardware and hardware accessories, plates, machined surfaces, lighting    			fixtures, and similar items already installed that are not to be painted. If removal is impractical 			or impossible because of size or weight of the item, provide surface-applied protection before 			surface preparation and painting.

1.	After completing painting operations in each space or area, reinstall items removed using 				workings skilled in the trades involved.

B.	Cleaning:  Before applying paint or other surface treatments, clean substrates of substances that 		could impair bond of the various coatings. Remove oil and grease before cleaning.

1.	Schedule cleaning and painting so dust and other contaminants from the cleaning process 				will not fall on wet, newly painted surfaces.

C.	Surface Preparation:  Clean and prepare surfaces to be painted according to manufacturer's 			written instructions for each particular substrate condition and as specified.

1.	Provide barrier coats over incompatible primers or remove and reprime.

2.	Wood:  Clean surfaces of dirt, oil, and other foreign substances with scrapers, mineral 				spirits, and sandpaper, as required.  Sand surfaces exposed to view smooth and dust off.

a.	Sand exposed wood framing members to remove exposed grade stamps.

b.	Scrape and clean small, dry, seasoned knots, and apply a thin coat of white 					shellac or other recommended knot sealer before applying primer. After priming, 					fill holes and imperfections in finish surfaces with putty or plastic wood filler. 					Sand smooth when dried.

c.	Prime, stain, or seal wood to be painted immediately on delivery. Prime edges, 					ends, faces, undersides, and back sides of wood, including paneling.

d.	If transparent finish is required, backprime with spar varnish.

3.	Ferrous Metals:  Clean ungalvanized ferrous-metal surfaces that have not been shop 				coated; remove oil, grease, dirt, loose mill scale, and other foreign substances. Use 				solvent or mechanical cleaning methods that comply with SSPC's recommendations.

a.	Treat bare and sandblasted or pickled clean metal with a metal treatment wash 					coat before priming.

b.	Touch up bare areas and shop-applied prime coats that have been damaged. 					Wire-brush clean with solvents recommended by paint manufacturer, and touch 					up with same primer as the shop coat.

4.	Galvanized Surfaces:  Uniformly abrade galvanized surfaces with a palm sander and 60-				grit aluminum oxide so surface is free of oil and surface contaminants. Remove 					pretreatment from galvanized sheet metal fabricated from coil stock by mechanical 				methods.

a.	Clean field welds with non petroleum-based solvents so surface is free of oil and 					surface contaminants.

D.	Material Preparation:  Mix and prepare paint materials according to manufacturer's written 			instructions.

1.	Maintain containers used in mixing and applying paint in a clean condition, free of 				foreign materials and residue.

2.	Stir material before application to produce a mixture of uniform density. Stir as required 				during application. Do not stir surface film into material. If necessary, remove surface 				material before using.

3.	Use only thinners approved by paint manufacturer and only within recommended limits.

3.03	APPLICATION

A.	General:  Apply paint according to manufacturer's written instructions. Use applicators and 			techniques best suited for substrate and type of material being applied.

1.	Paint colors, surface treatments, and finishes are indicated in the paint schedules.

2.	Do not paint over dirt, rust, scale, grease, moisture, scuffed surfaces, or conditions 				detrimental to formation of a durable paint film.

3.	Provide finish coats that are compatible with primers used.

4.	The term "exposed surfaces" includes areas visible when permanent or built-in fixtures, 				grilles, convector covers, covers for finned-tube radiation, and similar components are in 				place. Extend coatings in these areas, as required, to maintain system integrity and 				provide desired protection.

5.	Paint surfaces behind movable equipment and furniture the same as similar exposed 				surfaces. Before final installation of equipment, paint surfaces behind permanently fixed 				equipment or furniture with prime coat only.

6.	Paint interior surfaces of ducts with a flat, nonspecular black paint where visible through 				registers or grilles.

7.	Paint back sides of access panels and removable or hinged covers to match exposed 				surfaces.

8.	Finish exterior doors on tops, bottoms, and side edges the same as exterior faces.

9.	Sand lightly between each succeeding enamel and varnish coat.

B.	Scheduling Painting:  Apply first coat to surfaces that have been cleaned, pretreated, or 				otherwise prepared for painting as soon as practicable after preparation and before subsequent 			surface deterioration.

1.	The number of coats and film thickness required are the same regardless of application 				method. Do not apply succeeding coats until previous coat has cured as recommended by 				manufacturer. If sanding is required to produce a smooth, even surface according to 				manufacturer's written instructions, sand between applications.

2.	Omit primer over metal surfaces that have been shop primed and touch-up painted.

3.	If undercoats, stains, or other conditions show through final coat of paint, apply 					additional coats until paint film is of uniform finish, color, and appearance. Give special 				attention to ensure that edges, corners, crevices, welds, and exposed fasteners receive a 				dry film thickness equivalent to that of flat surfaces.

4.	Allow sufficient time between successive coats to permit proper drying. Do not recoat 				surfaces until paint has dried to where it feels firm, and does not deform or feel stick 				under moderate thumb pressure, and until application of another coat of paint does not 				cause undercoat to lift or lose adhesion.

C.	Paint all exposed surfaces, except where the paint schedules indicate that a surface or material 			is not to be painted or is to remain natural. If the paint schedules do not specifically mention an 			item or a surface, paint the item or surface the same as similar adjacent materials or surfaces 			whether or not schedules indicate colors. If the schedules do not indicate color or finish, the 			Architect will select from standard colors and finishes available.

1.	Painting includes field painting of exposed bare and covered pipes and ducts (including 				color-coding), hangers, exposed steel and iron work, and primed metal surfaces of 				mechanical and electrical equipment at all locations except mechanical and electrical 				rooms.

D.	Do not paint prefinished items, concealed surfaces, finished metal surfaces, operating parts, and 		labels.

1.	Labels:  Do not paint over Underwriters Laboratories (UL), Factory Mutual (FM), or 				other code-required labels or equipment name, identification, performance rating, or 				nomenclature plates.

E.	Application Procedures:  Apply paints and coatings by brush, roller, spray, or other applicators 			according to manufacturer's written instructions. Walls shall have roller finish.

1.	Brushes:  Use brushes best suited for type of material applied. Use brush of appropriate 				size for surface or item being painted.

2.	Rollers:  Use rollers of carpet, velvet-back, or high-pile sheep's wool as recommended by 			manufacturer for material and texture required.

F.	Minimum Coating Thickness:  Apply paint materials no thinner than manufacturer's 				recommended spreading rate to achieve dry film thickness indicated. Provide total dry film 			thickness of the entire system as recommended by manufacturer.

G.	Mechanical and Electrical Work:  Painting of mechanical and electrical work is limited to items 		exposed in occupied spaces (outside mechanical and electrical rooms).

H.	Mechanical items to be painted include, but not limited to, the following:

1.	Piping, pipe hangers and supports.

2.	Heat exchangers.

3.	Tanks.

4.	Ductwork, including interior of ductwork visible through air devices.

5.	Insulation.

6.	Motors and mechanical equipment.

7.	Exposed rooftop units.

8.	Accessory items.

I.	Electrical items to be painted include, but are not limited to, the following:

1.	Conduit and fittings.

2.	Switchgear.

3.	Panelboards.

J.	Prime Coats:  Before applying coats, apply a prime coat, as recommended by manufacturer, to 			material that is required to be painted or finished and that has not been prime-coated by others. 			Recoat primed and sealed surfaces where evidence of suction spots or unsealed areas in first 			coat appears, to ensure a finish coat with no burn-through or other defects due to insufficient 			sealing.

K.	Pigmented (Opaque) Finishes:  Completely cover surfaces as necessary to provide a smooth, 			opaque surface of uniform finish, color, appearance, and coverage. Cloudiness, spotting, 			holidays, laps, brush marks, runs, sages, ropiness, or other surface imperfections will not be 			acceptable.

L.	Transparent (Clear) Finishes:  Use multiple coats to produce a glass-smooth surface film of 			even luster. Provide finish free of laps, runs, cloudiness, color irregularity, brush marks, orange 			peel, nail holes, or other surface imperfections.

1.	Provide satin finish for final coats, unless otherwise noted.

M.	Stipple Enamel Finish:  Roll and redistribute paint to an even and fine texture. Leave no 			evidence of rolling, such as laps, irregularity in texture, skid marks, or other surface 				imperfections.

N.	Completed Work:  Match approved samples for color, texture, and coverage. Remove, refinish, 			or repaint work not complying with requirements.

O.	Interior Ferrous Metal items to be painted include, but are not limited to, the following:

1.	Steel frames.

2.	Wood door glass lite kits and astragals.

3.	Wood door louvers.

4.	Access panels (both sides).

5.	Countertop supports.

6.	Miscellaneous metal items.

3.04	CLEANING

A.	Cleanup:  At the end of each workday, remove empty cans, rags, rubbish, and other discarded 			paint materials from the Project Site.

1.	After completing painting, clean glass and paint-spattered surfaces. Remove spattered 				paint by washing and scraping. Be careful not to scratch or damage adjacent finished 				surfaces.

B.	Provide "Wet Paint" signs to protect newly painted finishes. Remove temporary protective 			wrappings provided by others to protect their work after completing painting operations.

1.	At completion of construction activities of other trades, touch-up and restore damaged or 				defaced painted surfaces.

3.05	LOW ODOR/LOW VOC INTERIOR COATINGS

A.	VOC Compliance – General:  Provide the manufacturers' formulations for the products 				specified below that comply with VOC requirements for the State of Maine Department of 			Environmental Protection in paragraph 2.02.C. of this Section.

B.	Gypsum Board:  Provide the following finish systems over interior gypsum board surfaces:

1.	Flat Acrylic Finish (Ceilings):  2 finish coats over a primer.

a.	Primer: Latex-based, interior primer applied at spreading rate recommended by the 					manufacturer to achieve a total dry film thickness of not less than indicated for 					product.

1)	S-W:  	PrepRite 200 Interior LatexB28W200 Series; 1.6 mils DFT.

b.	First and Second Coats:   Flat, acrylic-latex-based, interior paint applied at spreading 					rate recommended by the manufacturer to achieve a total dry film thickness of not 					less than indicated for product.

1)	S-W:	ProMar 200 Interior Latex Flat Wall Paint B30W200 Series; 2.8 mils 							DFT.

2.	Walls for Vinyl Wall Coverings:  Prime walls designated to receive vinyl wall coverings 				with the following:

a.	Primer:  Latex-based, interior primer applied at spreading rate recommended by the 					manufacturer to achieve a total dry film thickness of not less than indicated for 					product.

1)	S-W:	PrepRite 200 Interior Latex Primer B28W200 Series; 1.6 mils DFT.

3.	Low-Luster (Eggshell), Acrylic-Enamel Finish (Walls):   2 finish coats over a primer.

a.	Latex-based, interior primer applied at spreading rate recommended by the 						manufacturer to achieve a total dry film thickness of not less than indicated for 					product.

1)	S-W:	PrepRite 200 Interior Latex Primer B28W200 Series; 1.6 mils DFT.

b.	First and Second Coats:  Low-luster (eggshell or satin), acrylic-latex, interior enamel 					applied at spreading rate recommended by the manufacturer to achieve a total dry 					film thickness of not less than indicated for product.

C.	Natural-Finish Woodwork:  Provide the following natural finishes over new, interior 				woodwork:

1.	Waterborne, Satin-Varnish Finish:  3 finish coats of a waterborne, clear-satin varnish 				over an alkyd-based, interior wood stain.

a.	Transparent Stain Coat:  Alkyd-based, penetrating interior wood stain applied at 					spreading rate recommended by manufacturer. Stain color as selected by Architect 					from the manufacturer's full range of options.

1)	S-W:	Minwax Wood Finish 250 VOC Compliant.

b.	First, Second, and Third Finish Coats:  Waterborne, varnish finish applied at 						spreading rate recommended by the manufacturer.

1)	S-W:	Minwax Polycrylic.

D.	Wood Wainscot, Wainscot Trim and Trellis, Transparent Finish:  Provide the following fire 			retardant clear finish system over new, interior wood surfaces.

1.	Satin-Lacquer Finish:  2 finish coats of clear-satin lacquer over fire retardant barrier 				coating to provide Class A fire surface burning classification.

a.	Fire Retardant Coating:  Spray applied at spreading rate recommended by the 					manufacturer to achieve a total dry film thickness of not less than 7.5 mils.

1)	Flame Seal products, Inc. Tel (713) 668-4291: FX-100 Fire Retardant Barrier 						Coating.

b.	First and Second Finish Coats:  Lacquer finish applied at spreading rate 						recommended by the manufacturer.

1)	Minwax:  Clear Lacquer Finish, Satin – no substitutions.

E.	Wood Trim, Opaque Finish:  Provide the following paint finish systems over new, interior 			wood surfaces:

1.	Semi-gloss, Acrylic-Enamel Finish:  2 finish coats over a primer.

a.	Primer:  Quick drying, stain blocking alkyd primer applied at spreading rate 						recommended by the manufacturer to achieve a total dry film thickness of not less 					than indicated for product.

1)	S-W:	PrepRite Quick Seal Exterior/Interior Alkyd Fast Dry Primer Y24W980; 							1.7 DFT.

b.	First and Second Coats:  Semi-gloss, acrylic-latex, interior enamel applied at 						spreading rate recommended by the manufacturer to achieve a total dry film 						thickness of not less than indicated for product.

1)	S-W:	ProMar 200 Interior Latex Egg-Shell Enamel B20W200 Series;

3.2 mils DFT.

G.	Ferrous Metal:  Provide the following finish systems over ferrous metal:

1.	Semi-gloss, Acrylic-Enamel Finish:  2 finish coats over a primer.

a.	Primer:  Quick drying, corrosion resistant, alkyd-based or epoxy metal primer, as 					recommended by the manufacturer for this substrate, applied at spreading rate 					recommended by the manufacturer to achieve a total dry film thickness of not less 					than indicated for product.

1)	S-W:	Galvite HS paint B50WZ30; 3.5 mils DFT.

b.	First and Second Coats:  Semi-gloss, corrosion resistant, acrylic interior enamel, as 					recommended by manufacturer for this substrate, applied at spreading rate 						recommended by manufacturer to achieve a total dry film thickness of not less 					than indicated for product.

1)	S-W:	ProMar 200 Interior Latex Semi-Gloss B31-2200 Series; 3.0 mils DFT.

H.	Telecommunication and Electrical Backboards:  Provide the following finish over plywood:

1.	Flat In tumescent Finish:  2 finish coats over a primer.

a.	Primer:  Latex-based, interior primer applied at spreading rate recommended by the 					manufacturer to achieve a total dry film thickness of not less than indicated for 					product.

1)	Moore:	Pristine EcoSpec Interior Latex Primer Sealer 231; 0.8 mils DFT.

b.	First and Second Coats:  In tumescent-type, fire retardant paint applied at spreading 					rate recommended by manufacturer to achieve a total dry film thickness of not less 					than 4 mils DFT; white color for telecommunications and black for electrical.

1)	Moore:	M59-220 Latex Fire Retardant Coating.

END OF SECTION 09900