SECTION 10431

SIGNS

PART I – GENERAL

1.01	RELATED DOCUMENTS

A.	Drawings and general provisions of the Contract, including General and 					Supplementary Conditions and Division 1 Specifications Sections, apply to this 				Section.

1.02	SUMMARY

A	This Section includes the following:

1.	Client Logo Sign.

2.	Interior Panel Signs.

1.03	SUBMITTALS

A.	General:  Submit in accordance with Section 01330.

B.	Product Data:  Include construction details, material descriptions, dimensions of 				individual components and profiles, and finishes for each type of sign.

C.	Shop Drawings:  Include plans, elevations, and large scale sections of typical members 			and other components. Show mounting methods, grounds, mounting heights, layout, 			spacing, reinforcement, accessories, and installation details.

1.	Provide message list for each sign, including large scale details of wording, 				lettering, artwork, and Braille layout.

D.	Samples for Initial Selection:  For each type of sign material indicated that involves color 		selection.

E.	Maintenance Data:  For signage cleaning and maintenance requirements to include in 			maintenance manuals.

1.04	QUALITY ASSURANCE

A.	Source Limitations:  Obtain each type through one source from a single 	manufacturer.

1.05	COORDINATION

A.	For signs supported by or anchored to permanent construction, advise Installers of 	anchorage devices about specific requirements for placement of anchorage 	devices and similar items to be used for attaching signs.

PART 2 – PRODUCTS

2.01	SIGNS

A.	General:  Provide panel signs that comply with requirements indicated for materials, 			thickness, finishes, colors, designs, shapes, sizes, and details of construction.

1.	Produce smooth panel sign surfaces constructed to remain flat under installed 				conditions within tolerance of plus or minus 1/16-inch measure diagonally.

B.	Fabricator:  Welch Architectural Signage, 7 Glasgow Road, Scarborough, ME 04092, 			Tel. (207) 883-6200, FAX (207) 883-8588, Contact: Jeff Papalardo.

2.02	SIGN TYPES COMMON AREAS

A.	Interior Decorative Panel Sign (Conference Rooms – General Use):  See drawings 	for details.

1.	Substrate:  Fabricate signs from 1/8-inch thick matte clear acrylic face plate with 				custom image applied to sign.

2.	Size:  As indicated.

3.	Font Style and Size:  As selected by Architect.

4.	Colors:  To be selected by Architect from manufacturer's standards and custom 				colors.

5.	Letterform:  Apply 1/32-inch computer precision cut tactile copy. All uppercase, 				normal space, 5/8-inch minimum letter height. Tactile letters will be applied in a 				manner that avoids scoring of the sign's surface at base of tactile letters.

6.	Braille:  Use raster process to create all Braille cells. Drill holes in each dot 				location and fit clear raster balls into each hole.

B.	Client Logo Sign & Floor Signage:  Provide Sign(s) as detailed on drawings and having 			the following characteristics:

1.	Flat cut dimensional aluminum text and individually prepared aluminum sections 			for logo.

2.	Size:  As indicated.

3.	Font Style and Size:  As selected by Architect.

C.	Interior Panel Signs:  Provide Sign(s) as detailed on drawings and having the following 			characteristics:

1.	Substrate:  Fabricate signs from 1/8-inch thick matte clear acrylic with ¼ inch 				beveled backer plate. Edges mechanically and smoothly finished eliminating cut 				marks. Background color to be sub surface design of sign.

2.	Background Color: Custom color to be selected by Architect.

3.	Edges:  Straight.

4.	Corners:  Radiused.

5.	Size:  As required to accommodate 20 letters.

3.	Font:  Helvetica.

4.	Colors:  To be selected by Architect from manufacturer's standards and custom 				colors.

D.	In-use signs (Refer to Architectural sheet A912)

E.	Applied vinyl letters (Refer to Architectural sheet A912)

2.03	FINISHES – GENERAL

A.	Appearance of Finished Work:  Variations in appearance of abutting or adjacent pieces 			are acceptable if they are within one-half of range of approved Samples. Noticeable 			variations in same piece are not acceptable. Variations in appearance of other 				components are acceptable if they are within range of approved Samples and are 				assembled or installed to minimize contrast.

PART 3 – EXECUTION

3.01	EXAMINATION

A.	Examine substrates, areas, and conditions, with Installer present, for compliance with 			requirements for installation tolerances and other conditions affecting performance of 			work.

B.	Verify that items provided under other sections of Work are sized and located to 				accommodate signs.

C.	Examine supporting members to ensure that surfaces are at elevations indicated or 			required to comply with authorities having jurisdiction and are free from dirt and other 			deleterious matter.

D.	Proceed with installation only after unsatisfactory conditions have been corrected.

3.02	INSTALLATION

A.	General:  Locate signs and accessories where indicated, using mounting methods in 			compliance with manufacturer's written instructions.

1.	Install signs level, plumb, and at heights indicated, with sign surfaces from 				distortion and other defects in appearance.

2.	Interior Wall Signs:  Install signs on walls adjacent to latch side of door where 				applicable. Where not indicated or possible, such as double doors, install signs on 			nearest adjacent walls. Locate to allow approach within 3-inches of sign without 				encountering protruding objects or standing within swing of door.

3.03	CLEANING AND PROTECTION

A.	After installation, clean soiled sign surfaces according to manufacturer's written 				instructions. Protect signs from damage until acceptance by Owner.

3.04	SIGN SCHEDULE

A.	Interior Decorative Panel Signs:  Located at all conference rooms.

B.	Client Logo Sign:  Elevator Lobby 300.

C.	Interior Panel Signs:  Provide where indicated and where required by code.

D.	In Use Signs:  Located at all conference rooms and Mothers' Room 330.

E.	Applied vinyl signage:  Doors 300 & 300A.

END OF SECTION 10431