SECTION 10655

INDIVIDUAL, OMNI-DIRECTIONAL

OPERATIONAL PARTITIONS

PART 1 - GENERAL

1.01	DESCRIPTION

A.	General

1.	Furnish and install operable partitions and suspension system. Provide all labor, 					materials, tools, equipment, and services for operable walls in accordance with provisions 			of contract documents.

1.02	RELATED WORK BY OTHERS

A.	Preparation of opening will be by General Contractor. Any deviation of site conditions contrary 		to approved shop drawings must be called to the attention of the architect.

B.	All header, blocking, support structures, jambs, track enclosures, surrounding insulation, and 			sound baffles as required in 1.04 Quality Assurance.

C.	Prepunching of support structure in accordance with approved shop drawings.

D.	Paint or otherwise finishing all trim and other materials adjoining head and jamb of operable 			partitions.

1.03	SUBMITTALS

A.	Complete shop drawings are to be provided prior to fabrication indicating construction and 			installation details. Shop drawings must be submitted within 60 days after receipt of signed 			contract.

1.04	QUALITY ASSURANCE

A.	Preparation of the opening shall conform to the criteria set forth per ASTM E557 Standard 			Practice for Architectural Application and Installation of Operable Partitions.

B.	The partition STC (Sound Transmission Classification) shall be achieved per the standard test 			methods ASTM E90.

C.	Noise isolation classifications shall be achieved per the standard test methods ASTM E336 and 			ASTM E413.

D.	Noise Reduction Coefficient (NRC) ratings shall be per ASTM C423.

E.	Rack testing for 10 years. (Tensional Strength Stress Test.)

F.	The manufacturer shall have a quality system that is registered to the ISO 9001 standards.

1.05	PRODUCT DELIVERY, STORAGE, AND HANDLING

A.	Proper storage of partitions before installation and continued protection during and after 			installation will be the responsibility of the General Contractor.

1.06	WARRANTY

A.	Partition system shall be guaranteed for a period of 2 years against defects in material and 			workmanship, excluding abuse.

PART 2 - PRODUCTS

2.01	ACCEPTABLE MANUFACTURERS

A.	Upon compliance with all of the criteria specified in this section, Manufacturers wishing to bid 			products equal to the product specified must submit to the architect 10 days prior to bidding 			complete data in support of compliance and a list of 3 past installations of products similar to 			those listed. The submitting manufacturer guarantees the proposed substituted product complies 		with the performance items specified and as detailed on the drawings.

2.02	MATERIALS

A.	Product to be top supported Series 631 individual, omni-directional panels as manufactured 			by Hufcor, Inc.

1.	Panels shall be nominally 3-inches (76) thick and up to 48-inches (1219) in width.

2.	Panel faces shall be laminated to appropriate substrate to meet the STC requirement in 				2.04 Acoustical Performance.

a.	Optional face material (not all substrates are available for all STC ratings. Consult 					your Hufcor Distributor for more information:

1)	Steel

2)	Non-Steel

3)	Medium Density Fiberboard

b.	Horizontal Splice. Heights over 16'3" (4953) with non-steel faces require a 						structural splice placed at approximately 12'3" (3734) from the floor.

3.	Frames shall be of 16 gauge (1.42mm) painted steel with integral factory applied 					aluminum vertical edge and face protection.

a.	Option:  Face finish shall wrap around the vertical panel edges and provide no 					protective vertical face trim.

4.	Vertical sound seals shall be of tongue and groove configuration, ensure panel-to-panel 				alignment and prevent sound leaks between panels.

5.	Horizontal top seals shall be fixed continuous contact dual 4-finger vinyl.

a.	Option:  Horizontal top seals shall be retractable, provide 1" (25) nominal operating 				clearance, and exert upward force when extended. All panels, including pass door 					panels and lever closure panels must have retractable top and bottom seals. Not 					available with automatic bottom seals.

6.	Horizontal bottom seals shall be retractable, provide up to 2" (50) nominal operating 				clearance, and exert downward force when extended.

a.	Optional Seals:

1)	Horizontal bottom seals shall be automatic and provide up to 2" (50) nominal 					operating clearance. Consult your Hufcor Distributor for more information.

2)	Horizontal bottom seals shall be fixed continuous contact dual 4-finger vinyl.

7.	Horizontal trim shall be aluminum.

B.	Weight of the panels shall be 5.7-10.2 lbs, per sq. ft. (27.8-49.8kg/sq.m) based on options 			selected.

C.	Suspension System:

1.	Track shall be of clear anodized architectural grade extruded aluminum alloy 6063-T6. 				Track design shall provide precise alignment at the trolley running surfaces and provide 				integral support for adjoining ceiling, soffit, or plenum sound barrier. Track shall be 				connected to the structural support by pairs of minimum 3/8" (10) dia. threaded steel 				hanger rods. Pairs of rods are directly attached to the track, no single point attachment 				allowed. L, T, or X intersections shall be factory assembled and welded.

a.	Each panel shall be supported by two 2-wheeled counter-rotating horizontal 					carriers. Wheels to be of precision ground steel ball bearings with heat treated and 					hardened races encased with molded polymer tires.

1)  	Optional Type 38 (for panels weighing up to 400 lbs. (182 kg) :

Each panel shall be supported by two 1-wheel horizontal rotating carriers.

Wheel to be of precision ground steel ball bearings with heat treated and 						hardened races encased with molded polymer tires.)

2.	Plenum closure (by others):  Design of plenum closure must permit lifting out of header 				panels to adjust track height. Plenum closure required for optimum sound control of 				partition.

3.	Option (available for select layouts; consult your Hufcor Distributor):  The panels shall 				be supported by the Unispan pre-engineered truss and post system fabricated of steel and 				aluminum. Unispan is attached to the building structure for lateral support only. The load 				of the truss and partition is supported by end columns and the system transfers the 				partition weight to the floor.

D.	Finishes:

1.	Face finish shall be:

a.	Factory applied reinforced vinyl fabric with woven backing, weighing not less than 				15 oz. per lineal yard (465 g/m). Color shall be selected from the manufacturers 					standard color selections.

2.	Exposed metal trim and seal color shall be:

a.	Lamb's Wool (standard).

3.	Aluminum track shall be clear anodized.

2.03	OPERATION

A.	Panels are manually moved from the storage area, positioned in the opening, and seals set.

B.	Retractable Seals:

1.	Retractable seals shall be activated by a removable quick-set operating handle located 				approximately 42" (1067) from the floor in the panel edge. Seal activation requires 				approximately 15 lbs. (6.8 kg) of force per panel and approximately a 190 degree turn of 				the removable handle. Top and bottom retractable seals on each panel shall be operated 				simultaneously.

C.	Automatic Floor Seals:

1.	Horizontal seals shall be activated by pressing the edge of the panel into the edge of the 				adjacent panel or wall.

2.	Seal activation requires approximately 15 lbs. (6.8 kg) or force per panel.

D.	Final partition closure to be:

1.	Pivot Panel (Optional for heights to 12'3" (3734) and a maximum of 10 panels):

a.	Pivot panel is attached to the wall and permits access between adjacent rooms. 					Pivot panel is of the same construction as basic panels but with continuous contact 					multi-ply top and bottom seals. The lead end of the panel has full height finger pull 					and vertical seal of multi-ply vinyl.

2.04	ACOUSTICAL PERFORMANCE

A.	Acoustical performance shall be tested at a laboratory accredited by the U.S. Dept. of 				Commerce, National Institute of Standards and Technology, under the National Voluntary 			Laboratory Accreditation Program (NVLAP) and in accordance with ASTM E90 Test 				Standards. Standard panel construction shall have obtained an STC rating of 51.

1.	Complete, unaltered written test report to be made available upon request.

PART 3 - EXECUTION

A.	Installation:

1.	The complete installation of the operable wall system shall be by an authorized factory-				trained installer and be in strict accordance with the approved shop drawings and 					manufacturer's standard printed specifications, instructions, and recommendations.

B.	Cleaning:

1.	All track and panel surfaces shall be wiped clean and free of handprints, grease, and soil.

2.	Cartons and other installation debris shall be removed to onsite waste collection area, 				provided by others.

C.	Training:

1.	Installer shall demonstrate proper operation and maintenance procedures to owner's 				representatives.

2.	Operating handle and owner's manuals shall be provided to owner's representatives.

END OF SECTION 10655