SECTION 10801

TOILET AND BATH ACCESSORIES

PART 1 - GENERAL

1.01	RELATED DOCUMENTS

A.	Drawings and general provisions of the Contract, including General and Supplementary

Conditions and DIVISION 1 Specification Sections, apply to this Section.

1.02	SUMMARY

A.	This Section includes toilet and bath accessories. Extent of each type is indicated in Schedule

in Part 3.

B.	Related Sections include the following:

1.	DIVISION 6 Section "Rough Carpentry" for concealed wood blocking to support

accessories.

1.03	SUBMITTALS

A.	General:  Submit in accordance with Section 01330.

B.	Product Data:  Include construction details, material descriptions and thicknesses, dimensions,

profiles, fastening and mounting methods, specified options, and finishes for each type of

accessory specified.

C.	Shop Drawings:  Include blocking locations and mounting heights identified.

D.	Maintenance Data:  For accessories to include in maintenance manuals specified in 	DIVISION 1.  Provide lists of replacement parts and service recommendations.

1.04	QUALITY ASSURANCE

A.	Source Limitations:  Provide products of same manufacturer for each type of accessory unit 	and for units exposed to view in same areas, unless otherwise approved by Architect.

B.	Insofar as possible, fitting, construction, and fabrication of the work shall be executed at 	shops, ready for delivery and erection at buildings.

C.	Provide all holes, connections, and fastenings for and to work of other trades abutting, 	adjoining, or intersecting work of this Section.

1.05	COORDINATION

A.	Coordinate accessory locations with other work to prevent interference with clearances 	required for access by disabled persons, proper installation, adjustment, operation, cleaning, 	and servicing of accessories.

B.	Deliver inserts and anchoring devices set into concrete or masonry as required to prevent

delaying the Work.

1.06	WARRANTY

A.    	General Warranty:  Special warranty specified in this Article shall not deprive Owner of 						other rights Owner may have under other provisions of the Contract Documents and shall be 			in addition to, and run concurrent with, other warranties made by Contractor under require- 				ments 	of the Contract Documents.

PART 2 - PRODUCTS

2.01	MANUFACTURERS

A.	In other Part 2 articles where titles below introduce lists, the following requirements apply 	for product selection:

1.	Products: Subject to compliance with requirements, provide one of the products

specified.

2.	Manufacturers: Subject to compliance with requirements, provide products by the

manufacturers specified.

2.02	TOILET ACCESSORIES

A.	Products:  General

1.	Manufacturer:  Bobrick or Bradley meeting specified requirements.

2.	Style:  Contura.

3.	Mounting:  Concealed.

4.	Keying:  All keyed alike.

5.	Finish:  Satin stainless steel.

B.	Hand Soap Dispenser, Soap, Adapter:

1.	TC OneShot Automatic Foaming Hand Soap Dispenser, Chrome, Item 750339.

2.	Foam Free 'n Clean Soap, Item #750390

3.	6-Pack AC Adapter 490071 (connect up to 6 OneShot dispensers to 120V outlet).

C.	Hand Dry Dispenser:

1.	Dyson Airblade Touch-Free Hand Dryer with infrared activation.

D. 	Toilet Tissue Dispenser, Surface Mounted: Bobrick B-4288 concealed mounting, curved 							front with radius corners, stainless-steel roll-in-reserve dispenser with hinged front 										secured with tumbler lockset with noncontrol delivery with manufacturer's standard theft-				resistant spindle designed for 4½- or 5-inch diameter-core tissue rolls.

E.	Sanitary Napkin Disposal Unit, Surface-Mounted:  Bobrick B-270, stainless steel sanitary

napkin disposal unit with seamless exposed walls; curved front with radius corners; stainless-

steel, continuous hinge.

F.	Recessed Automated Touchless Towel Dispenser:

1.	Georgia-Pacific enMotion® Stainless, Item 59466 .

G.	Stainless Steel Custom Trash Receptacle:

1.	Georgia-Pacific Item #59471.

H.	Grab Bar:  Bobrick B-6806 Series; 1½-inch in diameter.

1.	Sizes and configurations:  As indicated.

I.	Decorative Mirror:  Simplymirrors.com Hitchcock-Butterfield Dark Series Traditions Oval 	Wall Mirror 770, dark walnut; 29-inches wide by 41-inches high.

2.03	FABRICATION

A.	Sections and shapes shall be rolled, formed, drawn, or extruded as required for respective

functions.

B. 	Molded work shall have sharply defined profile and shall be clean and straight.  Plain work

shall be leveled, straight and surfaces true and smooth. Edges, angles, and corners shall be 	square, clean, and sharp, unless otherwise detailed.

C. 	Fastenings, exposed metal fastenings, and accessories, unless Underwriters prohibit for 	safety, shall be of same materials, texture, color and finish as the base metal to which applied.

D. 	Molds, trim, frames, and other metalwork shall be proper dimensions to receive masonry 	block and tile, plaster, ceramic tile, or other scheduled finishes.

E. 	Surface-Mounted Toilet Accessories:  Unless otherwise indicated, fabricate units with tight

seams and joints, and exposed edges rolled. Hang doors and access panels with continuous 	stainless-steel hinge.  Provide concealed anchorage where possible.

F.	Keys:  Provide universal keys for internal access to accessories for servicing and resupplying.

Provide minimum of six keys to Owner's representative.

PART 3 - EXECUTION

A. 	Install accessories according to manufacturers' written instructions, using fasteners 	appropriate to substrate indicated and recommended by unit manufacturer. Install units level, 	plumb, and firmly anchored in locations and at heights indicated.

B. 	Grab bars shall be screwed to solid blocking in stud partitions. Install grab bars to withstand 	a downward load of at least 250 lbf, when tested according to method in ASTM F 446.

C.	Concealed Blocking:  Provide concealed wood blocking, 3/4-inch thick plywood covering 	32- by 32-inch area, in stud walls for toilet accessories.

3.02	TOILET ACCESSORIES SCHEDULE

A.	Men's Toilet Room 325:

1.	Provide 4 decorative mirrors.

2.	Provide 1 towel dispenser.

3.	Provide 4 soap dispensers.

4.	Provide 1 hand dry dispenser.

5.	Provide 3 toilet tissue dispensers.

6.	Provide 1 trash receptacle.

7.	Provide 2 grab bars in handicap accessible stall.

B.	Women's Toilet Room 325:

1.	Provide 4 decorative mirrors.

2.	Provide 1 towel dispenser.

3.	Provide 1 hand dry dispenser.

4.	Provide 4 soap dispensers.

5.	Provide 5 toilet tissue dispensers.

6.	Provide 2 grab bars in handicap accessible toilet stall.

7.	Provide 5 sanitary napkin disposal units.

8.	 Provide 1 trash receptacle.

C.	Men's Toilet Room 410:

1.	Provide 3 decorative mirrors.

2.	Provide 1 towel dispenser.

3.	Provide 1 hand dry dispenser.

4.	Provide 3 soap dispensers.

5.	Provide 3 toilet tissue dispensers.

6.	Provide 2 grab bars in handicap accessible toilet stall.

7.	Provide 1 trash receptacle.

D.	Women's Toilet Room 409

1.	Provide 3 decorative mirrors.

2.	Provide 1 towel dispenser.

3.	Provide 1 hand dry dispenser.

4.	Provide 3 soap dispensers.

5.	Provide 4 toilet tissue dispensers.

6.	Provide 2 grab bars in handicap accessible toilet stall.

7.	Provide 4 sanitary napkin disposal units.

8.	 Provide 1 trash receptacle.

3.03	ADJUSTING AND CLEANING

A.	Adjust accessories for unencumbered, smooth operation and verify that mechanisms function

properly.  Replace damaged or defective items.

B.	Remove temporary labels and protective coatings.

C.	Clean and polish exposed surfaces according to manufacturer's written recommendations.

END OF SECTION 10801