Copyright 1997, The American Institute of Architects (AIA)

SECTION 11451

RESIDENTIAL APPLIANCES

PART 1 - This Section uses the term "Architect."  Change this term to match that used to identify the design professional as defined in the General and Supplementary Conditions.

Verify that Section titles referenced in this Section are correct for this Project's Specifications; Section titles may have changed.

GENERAL

  - RELATED DOCUMENTS

Drawings and general provisions of the Contract, including General and Supplementary Conditions and Division 1 Specification Sections, apply to this Section.

  - SUMMARY

A		This Section includes the following:

Adjust list to suit Project.  Coordinate with information on Drawings and in residential appliance schedule at the end of Part 3.

Microwaves.

Refrigerator/freezers.

Dishwashers.

B.	Related Sections: Other specification Sections which directly relate to the work of this Section include, but are not limited to, the following:

- Division 6 Section "Finish Carpentry" for coordination with casework receiving appliances.

- Division 15 Sections for water distribution, drainage, vent piping, and plumbing fixtures.

- Division 16 Sections for electrical services and connections to residential appliances.

1.03	SUBMITTALS

A.	General:  Submit in accordance with Section 01330.

        - Product Data:  For each appliance type required indicating compliance with requirements.  Include complete operating and maintenance instructions for each appliance.

        - Appliance Schedule:  Submit schedule of appliances, using the same room designations shown on Drawings.

1.04	QUALITY ASSURANCE

- Installer Qualifications:  An experienced Installer who is an authorized representative of the appliance manufacturer for both installation and maintenance of appliances required for this Project.

- Source Limitations:  Obtain appliances through one source from a single manufacturer.

1.	Provide products from the same manufacturer for each type of appliance required.

- UL and NEMA Compliance:  Provide electrical components required as part of appliances that are listed and labeled by UL and that comply with applicable NEMA standards.

- Regulatory Requirements, Accessibility:  Where residential appliances are indicated to comply with accessibility requirements, comply with the U.S. Architectural & Transportation Barriers Compliance Board's "Americans with Disabilities Act (ADA), Accessibility Guidelines for Buildings and Facilities (ADAAG)," ANSI A117.1,  and the Fair Housing Accessibility Guidelines.  If conflicts occur between regulatory guidelines, comply with the more restrictive as 	determined by the Architect.

Operable Parts:  Provide controls with forward reach no higher than 48 inches (1219 mm) above the floor, horizontal front reach no more than 25 inches (635 mm), horizontal side- reach no more than 24 inches (610 mm), and that do not require tight grasping, pinching, or twisting of the wrist and that operate with a force of not more than 5 lbf (22.2 N).

Refrigerator/Freezer:  Provide 50 percent of freezer space within 54 inches (1370 mm) of the floor.

- AHAM Standards:  Provide appliances that comply with the following AHAM standards:

          - Dishwashers:  AHAM DW-DW1.

          - Electric Ovens:  AHAM ER-1.

          - Refrigerators and Freezers:  Total volume and shelf area ratings certified according to ANSI/AHAM HRF-1.

- Energy Ratings:  Provide appliances that carry labels indicating energy-cost analysis (estimated annual operating costs) and efficiency information as required by the Federal Trade Commission.

  - DELIVERY

- Deliver appliances only after utility rough-in is complete and construction in the spaces to receive appliances is substantially complete and ready for installation.

1.06	WARRANTIES

- General Warranty: Special warranties specified in this Article shall not deprive Owner of other rights Owner may have under other provisions of the Contract Documents and shall be in addition to, and run concurrent with, other warranties made by Contractor under requirements of the Contract Documents.

- Special Warranties: Written warranties, executed by manufacturer of each appliance specified agreeing to repair or replace appliances or components that fail in materials or workmanship within specified warranty period.

Revise warranties below to suit appliances specified.  Warranties below are examples only.  Warranties on appliances and component parts vary among manufacturers.  After the first year, most limited warranties cover only parts and exclude labor.

          - Microwave Oven:  10-year limited warranty for service on defects in the magnetron tube.

          - Refrigerator/Freezer:  Five-year limited warranty on the sealed refrigeration system.

          - Dishwasher:  10-year warranty against deterioration of tub and door liner.

PART 2 - PRODUCTS

  - PRODUCTS AND MANUFACTURERS

- Products:  Subject to compliance with requirements, provide the appliances indicated for each designation in the Appliance Schedule at the end of Part 3.

  - RESIDENTIAL APPLIANCES

- Microwave Oven:  Countertop mounted microwave oven, listed by UL, and complying wit requirements specified in the Appliance Schedule.

- Refrigerator/Freezer:  Full width Pantry, listed by UL, and complying with requirements specified in the Appliance Schedule.

Revise paragraph below if portable or convertible dishwasher is required.

- Dishwasher: Built-in, under counter, automatic dishwasher, sized to replace 24-inch- (610-mm-) base cabinet, listed by UL, and complying with requirements specified in the Appliance Schedule.

PART 3 - EXECUTION

  - EXAMINATION

A.	Examine roughing-in for plumbing, mechanical, and electrical services, with Installer present, to verify actual locations of services before appliance installation.

          - Proceed with installation only after unsatisfactory conditions have been corrected.

3.02	INSTALLATION

- A.	General:  Comply with manufacturer's written instructions.

- B.	Built-In Appliances:  Securely anchor to supporting cabinetry or countertops with concealed fasteners.  Verify that clearances are adequate for proper functioning and rough openings are completely concealed.

- Freestanding Appliances:  Place units in final locations after finishes have been completed in each area.  Verify that clearances are adequate to properly operate equipment.

- Utilities:  Refer to Divisions 15 and 16 for plumbing and electrical requirements.

3.03	ADJUSTING AND CLEANING

- Test each item of appliances to verify proper operation.  Make necessary adjustments.

B. 	Verify that accessories required have been furnished and installed.

C.	Remove packing material from appliances and leave units in clean condition, ready for operation.

B.	Microwave Oven:  Countertop type, 1.5 cu. ft. cavity, 1,200-watt output with recessed glass turntable.  Microwave features shall include electronic digital display with clock, electronic touch controls, 10 level variable cooking power controls, automatic defrost, cooking complete reminder, warm hold cycle, and child lookout feature.

          - Color:  Stainless Steel.

Locations:  Lunchroom 334.

Product:  Whirlpool MT4155SPS.

Quantity: 4

C.	Full Pantry Refrigerator/Freezer:   Provide freestanding, frost-free, two-door, bottom-mount freezer full pantry model refrigerator/freezer.

1.	Capacity: Provide the following minimum values, measured according to ANSI/AHAM 	HRF-1 and certified by AHAM:

Total Volume:  24.8cu. ft.

2.		Temperature Controls: Include separate temperature controls for each compartment.

3.	Color:  Monochromatic Stainless Steel.

4.	Location:  Lunchroom 334.

Product:  Whirlpool GX5FHDXVY

Quantity:  3

Dishwasher:  Automatic, Energy Star Rated, built-in, under-the-counter dishwasher; sized to replace 24-inch (610-mm) base cabinet and complying with the following:

Tub and Door Liner: Polypropylene.

Detergent Dispenser:  Sealed detergent and automatic rinsing-aid dispensers in door liner.

Rack System: Coated sliding dish racks with removable silverware basket.

Operation:  Five wash cycles with hot-air and heat-off drying cycle options.

Controls: Solid-state, electronic, press-to-start type.

Front Panel Finish: Manufacturer’s standard panels.

Standard features include the following:

Full-extension, coated, upper and lower dish racks.

Removable silverware basket with cover.

Sound-absorbing exterior insulation around tub and back.

Soft food disposer.

Self-cleaning food-filter system.

Optional features include the following:

Double wash arms.

Pots and pans cycle.

High temperature scour feature.

Delay Start feature.

Color:  Stainless.

Location:  Lunchroom 334.

Product:  Whirlpool DU1030XTXS

END OF SECTION 11451