SECTION 06200

FINISH CARPENTRY

1.	GENERAL

1.1	GENERAL PROVISIONS:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2	DESCRIPTION OF WORK:

A.	The extent of work shall be as shown on Drawings and called for in these Specifications.  	Performance shall meet the requirements of these Specifications.  The work covered by this 	section of Specifications consists of the following:

1. 	All finished carpentry work and millwork as required by Drawings and as specified under 			this section.

2. 	Installation of metal and other items furnished by other trades, if specifically noted in 				these Specifications.

2. 	PRODUCTS:

2.1 	BOARD LUMBER shall comply with the American Lumber Standards Simplified Practice Recommendation No. 16.  Grade of board lumber shall be suitable for its intended use.  Finish lumber is to be painted and shall be dressed free of tool marks and other objectionable defects.  All exposed lumber to be architectural quality grade:  Custom.

2.4 	STAIR RISERS AND TREADS:  3/4" APA plywood.

2.6 	STAIR SKIRTBOARDS: Pine

2.8  	NAILS:  6d for 1/2" finish stock and 4d finish for thinner wood.  Use 8d generally for nailing 3/4" wood trim to framing.

2.9 	SCREWS, BOLTS & OTHER FASTENERS:  as shown on Drawings with penetration into framing or blocking adequate to support loads shown.  Where not shown, consult Architect.

3.  	EXECUTION:

3.1  	ALL ITEMS OF MILLWORK shall be carefully erected, leveled and plumbed with tight-fitting joints and square corners, carefully cut and secured.  Exposed nails shall be set adequately for putty.  Moulds and faces shall be free from hammer or other tool marks, clean-cut and true pattern.  All work shall be thoroughly cleaned and sanded to receive the finish.  Sharp corners of small members of finished woodwork shall be slightly rounded.  All trim baseboards, etc. fastened to walls shall be secured to wall framing members and nails set.  Care shall be taken to avoid splitting ends of trim boards.

3.2 	INTERIOR TRIM:  Install trim with finishing nails and glue where required to assure permanent, tight joints, according to Drawing details.

3.3 	STAIRS:  Skirtboards and handrails installed as shown on Drawings

END OF SECTION