SECTION 07900

JOINT SEALERS

1. 	GENERAL:

  - REFERENCES:

- Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

- Section 01045 Cutting and Patching, SPECIFICALLY Section 2.1B Fire stopping & section 07860 fire stopping & smoke seals.

  - DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet requirements of these Specifications.

2.   	PRODUCTS:

2.1	CAULKING MATERIAL

A.	Tremco Dymonic; one part polyurethane on exterior walls for caulking joints at all junctions as necessary to obtain complete watertight construction.

B.	Tremco Latex 834 for general interior caulking.

3.  	EXECUTION:

3.1	ALL POTENTIAL INFILTRATION cracks & joints to be caulked.  Caulking shall be done only by workmen who are thoroughly experienced in this work.  Exterior caulking shall be applied around windows, doors, vents, utilities, and any other infiltration "crack".

3.2	INTERIOR CAULKING shall be applied to seal all penetrations through top plates of interior walls, (due to electrical or plumbing), and at tubs, showers, counter tops, bottom of party walls GWB, and other as shown on Drawings.

  - IN GENERAL, caulking to be done prior to (in conjunction with) siding installation.  See Drawings for any additional applications.  Joints and spaces to be caulked shall be dry and free from dust.  Finished caulking "bead" shall be neat and smooth, free of gaps and sags and run continuously.  Complete all caulking work and allow to stand for the manufacturer's recommended time period before painting.  Prime if required before finish coat of paint is applied.

END OF SECTION