SECTION 09250

GYPSUM BOARD

1.	GENERAL

1.1	REFERENCES:

A.	Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

B.	NOTE:  Selection of Finish colors and patterns in overall color scheme to be made by Architect.  Contractor to notify Architect prior to commencing Gypsum Board work, to allow adequate time for color selections, Owner's approval and material ordering lead time.

1.2	DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet the requirements of these Specifications.  The work covered by this section of Specifications consists of the following:

A. 	Drywall installation as required by Drawings and noted in these Specifications.

B.   Taping and finishing all walls and ceilings, except where other kind of finish is                specified.

2.  PRODUCTS

2.1	NOTE:  GWB types are shown as U.S.G. brand names “Sheetrock”, “Firecode”, “Firecode C”, “M.R. Board” and “Shaftwall”.  Substitutions must have equal U.L. and STC ratings. See Drawings for Specific assembly.

2.2  EXTERIOR & INTERIOR WALLS & CEILINGS:  See rated & non rated assemblies and wall types on the drawings.

2.3	RESILIANT CHANNEL:  USG-RC-1

3.  EXECUTION

3.1 	THE DRYWALL CONTRACTOR shall inspect all areas affected by his work to ascertain that all work is complete and has been accepted.  Defective installations shall be corrected before finished surfaces are painted or sprayed with acoustical material.

3.2  DRYWALL INSTALLATION.  Install drywall as shown on plans, noted in the UL Specifications, and as set forth in U.S.G. Handbook.  Installation of non-UL rated drywall assemblies on steel studs shall comply with the following minimum requirements:

- Spacing for attachment members shall not exceed 24" o.c. for walls and 16" o.c. for ceilings.  	All drywall shall be screwed with approved drywall screws made specifically for the purpose 	and of length adequate for wall types.  On walls, screws shall not be placed more than 16" apart 	for 16" o.c. framing or 12" apart for 24" o.c. framing.  Screw all edges 12" o.c. maximum.

- The drywall contractor may use a few drywall nails to temporarily secure a sheet of drywall before securing with drywall screws.  In this event, the drywall nails must be countersunk prior to taping.  Corner beads shall be used on all corners and casing beads used whenever Gypsum Board abuts dissimilar material.  Caulking to also be applied at these junctions.  At all party and unit/corridor walls, Gypsum Board to be set in caulking (for sound).

- Drywall shall be laid vertically or horizontally.  No tapered joints at floor base.

- Note: Gypsum board to be installed behind all tubs and shower units which results in double gypsum board on some bathroom walls.  See bathroom drawing sheet.

- Ceiling suspension system:

  - Space hangers not over 48 in. o.c. in direction of main runner channels, and within 6 in. of ends of main runner runs and of boundary walls, structural steel, partitions, and similar interruptions of ceiling continuity.  Install additional hangers at ends of each suspension member and at ceiling equipment not separately suspended, 6 in. from vertical surfaces.  Do not splay wires more than 5 in. in a 4 ft. vertical drop.  Wrap wire a minimum of three times horizontally, turning ends upward.

  - Attach hangers directly to ceiling structure, or to supplementary framing members supplied and installed under this section.  Hangers may not be suspended from mechanical or electrical equipment such as ductwork, conduit or piping.

  - Install 1-1/2 in. main runner channels spaced not over 48 in. o.c. within 6 in. of wall.  Position channels for proper ceiling height, level and secure, with hanger wire saddle-tied along channel.  Provide 1 in. clearance between runners and abutting walls and partitions.  At channel splices, interlock flanges, overlap ends 12 in., and secure each end with double-strand 18 ga. tie wire.

  - Erect ¾ in. metal furring channels at right angles to main runner channels or main support members.  Space furring not over 16 in. o.c., and within 6 in. of wall.  Provide 1 in. clearance between furring ends and abutting walls and partitions. Secure furring to carrying channels with clips or saddle-tie to supports with double strand 18 ga. tie wire.  At splices, next furring channels at least 8 double-strand 18 ga. tie wire.

  - At openings interrupting main or furring channels, install additional cross-reinforcing as required, to restore lateral stability of ceiling framing system.

  - Finished installations shall be level to within ¼ in. in 10 ft.

3.3 	ON SURFACES TO BE PAINTED:  tape and cement all joints and screw locations with three coats of compound, then sand to smooth finish, acceptable to paint.

3.4	DURING WORK PROGRESS, remove all excess materials and debris resulting from operations, which may disrupt the work of other trades, and after completion leave the premises broom clean.

END OF SECTION