SECTION 09900

PAINTING

1.	 GENERAL

1.1 	DESCRIPTION OF WORK

A.	Drawings and general provisions of Contract, including General Conditions and 				Division 1 specifications, apply to work in this section.

B. 	The extent of work shall be as shown on Drawings and called for in these 					Specifications.  Performance shall meet the requirements of these Specifications.  The 		work covered by this section of Specifications consists of the following:

1. 	Painting all interior and exterior surfaces as called for in the Finish 							Schedule on Drawings or in these Specifications.

2.	Painting interior walls, door trim, window trim, etc.

3. 	Painting all exterior doors as specified.

- Painting and finishing any other work requiring finishing left unfinished by others.

NOTE: All colors to be selected by Architect.  The Contractor shall submit to the Architect, for approval color samples.

1.2 	SUBMITTALS

A. 	Issue submittals in accordance with Section 01300, Submittals.

B. 	Submit as follows:

1. 	Manufacturer's data, application instructions, and color chips on all specified 				products.

2.   	Paint schedule covering all surfaces to be painted.

2.  	PRODUCTS

2.1 	General

A. 	Paint: Acceptable manufacturers, unless specific manufacturer is noted:  California Products Corporation, Benjamin Moors, Pratt & Lambert, Sherwin-Williams, Tnemec.

- All products used shall be manufacturer's top quality product for each type of finish specified.

2.2 	MATERIALS

A. 	Where primer is called for, use primer recommended by manufacturer for particular combination of substrate and finish coat.  Where painting over shop-applied primers, verify that finish paint proposed for field application is compatible with shop primers actually used.

- Exterior Doors

- All Gypsum Walls and Ceilings to be painted.

- Finish-Walls.

- Finish Ceiling

- Interior Window sash and exposed softwood woodwork as noted on Drawings

- Wood Door Frames & Trim & Miscellaneous interior wood trim.

- Wood store fronts

3.  	EXECUTION

3.1  	JOB CONDITIONS

A.	Store materials in sealed containers.  Provide a fire extinguisher in storage room.  			Remove flammable rags and waste from building at end of day.

B. 	Do not perform exterior work in rain or when precipitation is forecast imminently; or in 		hot, dry, or windy weather which would cause finish to cure too rapidly, or be marred 		by windstorm dust; or at temperatures below 40 degrees F.

C. 	Maintain temperature at interior locations between 50 and 75 degrees F, maximum 80 		percent relative humidity, while paint is being applied.  Provide adequate ventilation, by 		mechanical means if necessary, for drying of paint and prevention of condensation and 		mildew.  Do not apply finish in areas in which dust is being generated.

D. 	Protect finished surfaces and equipment not being painted with masking tape, canvas 			dropcloths, polyethylene sheets, etc.  Items such as lighting switch covers, fixture 			canopies, and door handles shall be temporarily removed, carefully stored, and replaced 		after painting, or carefully covered during painting operations.

3.2 	PREPARATION

A. 	Preparation of newly-installed materials to receive finish painting is specified under 			those Sections installing materials.  This includes, but is not necessarily limited to: 			touch-up of damaged shop coats; taping, sealing and sanding of drywall; patching 			masonry; sanding finish wood; and cleaning off grease, oil, dirt, mildew, factory-			applied protective coatings, and other foreign materials.

B. 	At wood surfaces to be painted, scrape and clean small, dry, seasoned knots, and apply a 		thin coat of white shellac or other recommended knot sealer, before application of 			priming coat.  After priming, fill holes and imperfections in finish surfaces with putty or 		plastic wood-filler.  Sandpaper smooth when dried.

- Before beginning work under this Section, verify that preparation of substrates under other Sections has been done as specified.  Thoroughly remove water, dirt, and dust with clean cloths, brooms, or brushes. Allow masonry motar joints to cure as long as possible before beginning paint application, 7 days minimum, and 28 days preferably.

3.3 	APPLICATION

A. 	Apply all materials in accordance with the manufacturer's recommendations.

B. 	Apply materials with suitable brushes, rollers, and spraying equipment.  Keep 				application equipment clean, dry, and free from contaminants.  Thoroughly stir 				materials before applying, and periodically during application.

C. 	Rate and method of application and drying time between coats shall be strictly in 			accordance with manufacturer's recommendations.

D.	Touch-up shop applied primers before field painting.

E.	Do not apply first coat until surface is dry to touch.  Moisture content of surface shall be 		within limitations recommended by paint manufacturer.

F.	Leave all parts of moldings and ornaments clean and true to detail, without excessive paint in corners and depressions.  Make edges of paint adjoining other materials or colors clean and sharp with no overlapping.  Paint surfaces visible through grilles one (1) coat flat black.

G.	Finish coats shall be smooth, free of brush marks, streaks, laps or pile-up of paint, and 		skipped or missed areas.  Refinish whole wall if unacceptable finish is extensive or of 		such a nature that it cannot be repaired by normal touch-up.

H. 	After completion of painting work, remove spilled or spattered paint.  Touch-up and 			repair finishes damaged in any way by work under this Section.  Protect finished 				surfaces.

3.4 	Exterior

- Exterior and interior - Steel-Clad door:  Two (2) coats exterior enamel over factory primer.  Doors shall be laid flat if sprayed.  Doors may be rolled or brushed in place, however with no visible brush marks, drips or imperfections.

- All metal work (steel) to include railings and brackets.

a.	Alkyd Systems

Gloss Finish

1st Coat:	S-W All surface Enamel Primer, A11w210

2nd Coat: S-W All Surface Enamel, A11 Series

3rd Coat: S-W All Surface Enamel, A11 Series

(4 mils wet, 1.6 mils dry per coat)

C.	Wood store fronts to receive one (1) coat alkyd primer, two (2) coats of 100% acrylic latex primer.

3.5 	Interior

- Interior Painting:  Paint shall be applied in the following number of coats, primer and finish.  Tint all primers to match finish color.

1. 	Two (2) fully applied finish coats of even coverage.  NOTE:  Contractor to 					adequately cover M.R. (Blueboard) or other colored drywall by primer or finish 				coat as necessary to eliminate any visible "bleed through".

- Drywall:  All interior walls to receive paint: one (1) coat latex base primer-sealer, two (2) finish coats latex eggshell.  Ceiling: One (1) coat primer and two (2) coats latex flat.

- Door Frames & Trim, and Miscellaneous Interior Wood Trim- one (1) coat primer and two (2) coats finish for all soft wood.

END OF SECTION