November 17, 2009

March 25, 2010

To:   	Jean Fraser

Barbara Barhydt

From:	David Margolis-Pineo

Re:	231 York Street - Public Services Review Comments

- The applicant is asked to close the curb cut on Brackett Street with raised granite curbing and a new brick sidewalk.  The brick sidewalk on Brackett Street is currently in poor condition whereas the brick sidewalk on York Street is in very good condition.  Therefore the applicant is asked to replace the entire brick sidewalk on Brackett Street from the street right of way to curb from the York Street sidewalk to the property line on Brackett Street with the Pinehall Paver bricks now specified by the City.

The applicant has agreed to do so.

- The plans are not stamped.

The plans are now stamped

- The applicant is asked to evaluate an alternative to discharging the proposed foundation drain to the City’s sanitary sewer.  Is it possible to discharge to catch basin where future stormwater separation would remove this water from the sanitary system?

The applicant is requesting to run a 6” foundation drain to the sanitary sewer on York St.  Since no separated stormwater and sanitary system exists, this request is allowed.  Again, a backflow preventer is advised and the applicant is requested to install the 6” foundation drain at an elevation where it may be extended over the top of the existing sewer if the city chooses to install a separate stormwater sewer on the easterly side of York St in the future.

- The existing water and gas service on Brackett Street are not shown on the utility plan.  Will they be reused or abandoned.

The applicant has addressed this issue.

- Since the proposed sanitary sewer connection into York Street will connect to a combined sewer system, the applicant is advised to install a backflow preventer on the sewer lateral.

The applicant has addressed this issue.

- The applicant shall obtain a seal drain permit and demolition permit before commencing.

The applicant has not addressed this issue.  This issue should be added as a condition of approval.

- It is the City’s desire to inspect the granite vault on the corner of Brackett and York Streets.  If the structure is in a failure condition, the City will coordinate with the applicant.

If after approval this structure is found to be in need or repair, the city will facilitate.

Additional Comments

- Survey pins should be set at the property corners.

- Sheet 2 shows an existing street line M Monument to be reset.  The City suggest that the note be changed to set a new monument at the street line with a three foot offset corner as per City of Portland Technical Standard Detail for Granite Survey Monuments.  This department will supply a 5/8" copper bolt and brass survey washer to the surveyor who will mark the new monument.  See attached detail.