MMC TDM

Presentation Notes

- Alex to introduce and acknowledge that the condition was ambiguous and that staff did not clarify expectations;  some advantages to the timing as it allows synergy with Transit Study

- Jean overview of the “state of the art”  -  key messages from current practice and research

  - [?my background?]

  - Context-  TDM Pyramid and potential measures (hand out)

  - Need carrots as well as sticks to be effective-  often TDM plans become superficial and ineffective (in UK called “greenwash”)

  - Need to customize TDM plans to the particular travel characteristics of a group of employees-  need information to know how to customize and need objectives so can measure effectiveness

  - Usually need 3-5 years for TDM Plan to evolve and become effective-  some trial and error to find the right package

  - Very important to have central transportation coordinator who has budget, time and power to achieve measures and monitor and make adjustments as necessary

  - Parking management needed to support and complement other TDM measures-  partly to avoid pushing cars into the surrounding area, but also to provide some of the “sticks” that may be needed (especially re hospitals)

  - Monitoring and correction need to be built in, with contingency plans identified if measures not working

- RE the MMC TDM

  - Its always possible to do more within a TDM  - but as this is a relatively new initiative may be OK to focus on a few measures and make sure they are introduced correctly

  - Agree with their emphasis on:

    - Having a Transportation Coordinator in place early

    - Importance of doing a survey of employees

    - Value of linking into the Portland TDM initiatives

  - Recommend that more rigorous timetable and detailing of even this first phase would assist in ensuring delivery;  need outputs that would come to the City and mechanism for regular liaison