SECTION 02230

SITE CLEARING AND GRUBBING

PART 1  GENERAL

1.01	SECTION INCLUDES

A.	Removal of surface debris.

B.	Remove root system of trees, brush and shrubs.

C.	Removal of paving, curbs, and existing gravel.

D.	Removal of culverts, catch basins, manholes and other drainage features.

E.	Removal of fences, posts, bollards, poles, signs, gates and other minor structures.

F.	Removal and stockpiling of topsoil.

1.02	RELATED SECTIONS

A.	Section 02250 -  Dewatering

B.	Section 02315 - Common Excavation, Embankment and Compaction

C.	Section 02320 - Slope Protection and Erosion Control.

1.03	DEFINITIONS

A.	Loam

1.	Friable clay loam surface soil found in depth of not less than 4 inches.

2.	Satisfactory topsoil is free of subsoil, clay lumps, stones, and other objects over 2 inch in diameter, and without weeds, roots and other objectionable material.

1.04	REGULATORY REQUIREMENTS

A.	Obtain required permits from authorities.

B.	Notify affected utility companies before starting work and comply with their requirements.

C.	Do not close or obstruct roadways without permits.

D.	Conform to applicable code for disposal of debris.

E.	Conform to applicable regulatory procedures when hazardous or contaminated materials are discovered.

1.05	PROJECT CONDITIONS

A.	Conform to applicable regulations relating to environmental requirements, disposal of debris, and use of herbicides.

B.	Coordinate clearing work with utility companies.

C.	Protect utilities to remain from damage.

D.	Provide protection necessary to prevent damage to existing improvements, trees, or vegetation indicated.

E.	Provide traffic control as required, in accordance with the U.S. Department of Transporation "Manual of Uniform Traffic Control Devices" and Maine Department of Transportation (MDOT) requirements.

F.	Conduct site clearing operations to ensure minimum interference with roads, streets, walks and other adjacent occupied or used facilities.  Do not close or obstruct streets, walks, or other occupied or used facilities without permission from authorities having jurisdiction.  Streets and roadways shall be thoroughly cleaned and/or swept on a daily basis or more frequently as required by the governing authority

G.	Promptly repair damage to adjacent facilities caused by the clearing and grubbing operations, at no cost to the Owner.

PART 2  PRODUCTS

2.01	MATERIALS

A.	Snow Fence:  Beacon Plus Orange Construction Fence by Geotenax Corporation, 4800 Monument Street, Baltimore, Maryland, 21205 or approved equal.  Snow or Construction Fence shall be supported with 1" steel posts spaced at a maximum of 8'-0" on center.

PART 3  EXECUTION

3.01	PREPARATION

A.	Locate and identify utilities to remain.

B.	Identify a waste area for placing removed materials.

3.02	PROTECTION

A.	Protect utilities to remain from damage.

B.	Pollution Controls:  Use water sprinkling to limit to the lowest practical level the amount of dust and dirt rising and scattering in the air.  Do not use water when it may create hazardous conditions, ice, flooding or pollution

C.	Clean adjacent structures and improvements of dust, dirt and debris caused by clearing and grubbing or earthwork operations.  Return adjacent areas to condition existing prior to the start of the work.

3.03	REMOVAL

A.	Remove paving, curbs, poles, posts, signs, fences, gates, culvert and minor structures to facilitate construction.  Where required by these Drawings, or directed by Owner, preserve those curbs, poles, posts, signs, fences, gates, culverts, minor structures, and other features called for to be reset.  Reset removed objects immediately upon completion of backfilling, unless otherwise directed by Owner.

B.	Remove existing pavement; as indicated.

C.	Remove debris from site.

3.04	DISPOSAL

A.	Burning of Materials:  Burning will not be permitted.

B.	Removal:  Remove material, debris, rock and extracted plant life from site daily as it accumulates and legally dispose of.

C.	Dumping:  Dispose of material in an approved off site legally operated disposal area.

D.	Chipping:  Reduce to dimensions of less than 2 inches by use of an approved chipping machine and dispose of at an approved off site, legally operated disposal area.

E.	Trucks removing demolition debris from the site shall be covered or shall be of a closed body design to prevent the accidental throwing upon any way of tacks, nails, wire, scrap metal, glass, crockery, or other substances injurious to the feet of persons or animals or to tires or wheels of vehicles.

3.05	RESTORATION

A.	Restore any improvements damaged by or removed by this work to original condition, as acceptable to Owners or other parties or authorities having jurisdiction including but not limited to fences, curbs, signs, trees, shrubs, vegetation, poles, and posts.

B.	Repair or replace trees and vegetation damaged by construction operations, in a manner acceptable to Owner.

C.	Replace trees damaged beyond repair.

END OF SECTION