SECTION 02250

DEWATERING

PART 1  GENERAL

1.01	SECTION INCLUDES

A.	Furnish, operate and maintain dewatering equipment for control, collection, and disposal of ground and surface water entering trenches and excavations.

1.02	RELATED SECTIONS

A.	Section 02315- Common Excavation, Embankment and Compaction.

B.	Section 02317- Trenching.

C.	Section 02320 - Slope Protection and Erosion Control.

1.03	DESIGN REQUIREMENTS

A.	Design dewatering facilities including drains, piping and pumping.

1.04	SUBMITTALS

A.	Prior to start of excavation and trenching, submit dewatering design and methods to Owner for review.

PART 2  PRODUCTS

2.01	EQUIPMENT

A.	Provide pumps, drains, piping and other facilities necessary to keep excavations and trenches free of water including spare units available for immediate use in the event of equipment failure.

PART 3  EXECUTION

3.01	PROTECTION

A.	Protect watercourses, sewer systems and adjacent properties from siltation by use of sediment ponds or other measures acceptable to Owner.

B.	Keep excavations clear of groundwater, surface water, seepage, sewage and stormwater.

3.02	INSTALLATION

A.	Install, construct and maintain equipment and facilities required for work of this section.

B.	Dispose of water removed from Work in a suitable manner which will not interfere with other work, cause erosion, damage pavements, other surfaces or property and is acceptable to Owner:

C.	Remove dewatering equipment and facilities when no longer required.

D.	Backfill excavations in accordance with 02315.

E.	Repair damage resulting from dewatering operations.

END OF SECTION