SECTION 02480

LANDSCAPE WORK

1.	GENERAL

1.1	REFERENCES

A.	Drawings and general provisions of Contract, including General and Supplementary Conditions and Division 1 specifications, apply to work in this section.

B.  	American National Standards Institute (ANSI), Z60.1, "American Standard for Nursery Stock".

C.  	Official Seed Analysis of North America

D.  	State of Maine Department of Transportation (MDOT), Standard Specifications, Highways and Bridges.

1.2 	DESCRIPTION OF WORK:  Extent of Landscape Work is shown on the drawings.

1.3 	QUALITY ASSURANCE

A.  	Refer to Section 01631, Products and Substitutions, for general provisions covering product selection, substitutions, material storage, and installation.

B.  	Refer to Section 01400, Quality Control Services, for provisions for testing and inspection.

C.  	Warranty all plants, shrubs, and trees for one year against death and unhealthy condition, except as may result from neglect by Owner or damage by others.  Replace at optimum planting time.

D.  	Warranty lawns through specified lawn maintenance period and until final acceptance.

1.4 	SUBMITTALS

A.  	Issue submittals in accordance with Section 01300, Submittals.

B.  	Submit planting schedule showing coordination of normal planting times with construction schedule for other (related) work.

C.  	Submit analysis or certification of loam to show conformance with specification requirements.

2.  	PRODUCTS

2.1 	PLANT SIZE AND QUALITY

A.	Provide sizes of plants as shown or scheduled, conforming to ANSI Z60.1  "American Standard for Nursery Stock" for shape and quality.

B.  	Furnish balled and burlapped (B&B) trees and shrubs, except container-grown plants 	may be furnished if indicated size is below limit established in ANSI Z60.1.

C.	Deciduous shrubs may be furnished in bare root condition if adequately maintained and protected from drying through transplanting period.

D.  	Furnish ground cover plants in removable containers or integral peat pots.

2.2 	LOAM

A. 	Loam shall be good quality friable loam free of stones over 1 in., objectionable weeds, 	roots or seeds, clay lumps, sticks, trash, or other extraneous material.

B. 	The loam shall have an organic content greater than 1.5% by weight and shall not contain soluble salt greater than 500 parts per million.

C.	Provide loam to supplement that (if any) shown as available for reuse at site.  Provide 	clean, fertile, friable, natural loam obtained from a local, well drained source.

2.3 	FERTILIZER

A. 	Provide fertilizer, humus and other soil amendments of a type which are known to improve pH condition of soil for particular plant material to be planted.

B. 	Mix peat humus (FA Q-P-166) with loam in the ratio of 1:3 for use in planting.

3. 	EXECUTION

3.1 	PLANTING TREES

A. 	Excavate pit to 1-1/2 times diameter of tree ball and not more than 6" deeper.  Compact layer of loam in pit to locate collar of plant properly in a slightly dished finish grade.  Backfill around ball with loam, compacted to eliminate voids and air pockets, watering thoroughly as layers are placed.  Build 3" high berm of loam beyond edge of 	excavation.  Apply 2" mulch of ground hemlock bark.

B.  	Prune trees to remove damaged branches, improve natural shape, thin out structure and 	remove not more than 15% of branches.  Do not prune back terminal leader.

C.  	Guy and stake tree 3 directions with galvanized wire, through flexible-hose chafing guards, with wooden stake anchors.

3.2 	PLANTING SHRUBS

A.  	Excavate pits or trench to 1-1/2 times diameter of balls or containers, or 1'-0" wider than spread of roots, and 3" deeper than required for positioning at proper height.  Lightly compact a layer of loam in bottom before placing plants.  Backfill around plants with loam, compacted to eliminate voids and air pockets.  Water thoroughly as layers are placed.  Form grade slightly dished, and bermed at edges of excavation.  Apply 2" mulch of ground hemlock bark.

- Prune shrubs to remove damaged branches or improve natural shape.  Do not otherwise prune plant material.

3.3 	PLANTING GROUND COVER

A.	Loosen subgrade to depth of 4" in areas where loam has been stripped, and spread loam to depth of 4", except as otherwise indicated.

B. 	Space plants 2'-0" apart both ways, except as otherwise indicated.  Dig holes large enough to allow for spreading of roots.  Compact backfill to eliminate voids, and leave grade slightly dished at each plant.  Water thoroughly.  Apply 2" mulch of ground hemlock bark planting mulch over entire planting bed, lifting plant foliage above mulch.

C. 	During periods of hot sun and wind at time of planting, provide protective cover for several days.

3.4 	APPLYING FERTILIZER

A. 	Fertilizer for planting trees, shrubs and ground cover shall be a 5-10-5 (5% nitrogen, 10% phosphorus and 5% potash) commercial fertilizer, applied and mixed at rate of not less than 0.25 lbs. per cu. ft. of soil and humus.

B. 	Fertilize loam for planting grass with a high-nitrogen content commercial fertilizer, containing 10% phosphorus, 10% potash and 5% nitrogen to supply not less than 1.0 lbs. of actual nitrogen per 1000 sq. ft. lawn area.  Apply fertilizer prior to seeding.

3.5 LANDSCAPE MAINTENANCE

A. 	Maintain landscape work for a period of 60 days immediately following complete installation of each major category of work.

B.  	Include watering, weeding, cultivating, restoration of grade, mowing and trimming grass, pruning trees and shrubs, protection from insects and diseases, fertilizing and similar operations as needed to ensure normal growth and good health for live plant material.

END OF SECTION