SECTION 05715

SPIRAL STAIRS

1. 	GENERAL

1.   	PRODUCTS

1.1  	SPIRAL STAIRS

A.  	Manufactured by Custom Iron, Inc., Supplier G & S Associates (207) 985-3627

Model Old Faithful, Model # D100

Handrail: Steel Standard railcap profile

Balusters: 10110

Tread: Painted Metal

Riser Bar to be included

- The spiral stairway shall have a 7.5 inch minimum clear tread depth at a point 12 inches form the narrow edge.  The risers shall be sufficient to provide a headroom of 78 inches minimum, but risers height shall not be more that 9.5 inches.  The minimum stairway width shall be 26 inches.

END OF SECTION