SECTION 06200

FINISH CARPENTRY

1.	GENERAL

1.1	GENERAL PROVISIONS:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2	DESCRIPTION OF WORK:

A.	The extent of work shall be as shown on Drawings and called for in these Specifications.  	Performance shall meet the requirements of these Specifications.  The work covered by this 	section of Specifications consists of the following:

1. 	All finished carpentry work and millwork as required by Drawings and as specified under 			this section.

2. 	Installation of metal and other items furnished by other trades, if specifically noted in 				these Specifications.

2. 	PRODUCTS:

2.1 	BOARD LUMBER shall comply with the American Lumber Standards Simplified Practice Recommendation No. 16.  Grade of board lumber shall be suitable for its intended use.  Finish lumber is to be painted and shall be dressed free of tool marks and other objectionable defects.  All exposed lumber to be architectural quality grade:  Custom.

2.2 	INTERIOR TRIM:  Door trim casing WM351 8710, Window Apron - Brosco style 8645, Back Relieved.  Window stool – See Drawings, Base – See add Alternate #1.  All interior trim unless noted otherwise on Drawings or in Specifications to be equal to No. 1 Pine or Poplar.  Finger joints shall be allowed. See drawings for bay window detail. Note: Windows to receive one finish coat over factory prime.

2.3 	PUBLIC CORIDORS:  1 X 6 Oak Baseboard.

2.4 	STAIR RISERS AND TREADS:  3/4" APA plywood.

2.5  	STAIR RAILINGS:  Similar to Brosco, #75 Oak (1-1/2" x 1-3/4" round).

2.6 	STAIR SKIRTBOARDS: Oak

2.7	STAIR HANDRAIL BRACKETS:  Stanley SP7081, Satin brass finish.  Secure with #8 or #10 Brass screws of adequate length for wall condition, minimum 1-1/4" into blocking. At CMV wall condition, anchor with 5/8” or ¾” diameter HILTI HIT HY20 Adhesive Anchor (or similar).

2.8  	NAILS:  6d for 1/2" finish stock and 4d finish for thinner wood.  Use 8d generally for nailing 3/4" wood trim to framing.

2.9 	SCREWS, BOLTS & OTHER FASTENERS:  as shown on Drawings with penetration into framing or blocking adequate to support loads shown.  Where not shown, consult Architect.

2.10	COUNTERTOPS:  Rounded-edge preformed plastic laminate countertops, color choice of Architect.  See Section 11450-Residential Equipment & Kitchens.

2.11	PLASTIC LAMINATE:  See Section 11450

2.12	CLOSET SHELVING:  Premanufactured plastic coated wire shelving with integral clothes hanger.  Closet Maid or equal.

3.  	EXECUTION:

3.1  	ALL ITEMS OF MILLWORK shall be carefully erected, leveled and plumbed with tight-fitting joints and square corners, carefully cut and secured.  Exposed nails shall be set adequately for putty.  Moulds and faces shall be free from hammer or other tool marks, clean-cut and true pattern.  All work shall be thoroughly cleaned and sanded to receive the finish.  Sharp corners of small members of finished woodwork shall be slightly rounded.  All trim baseboards, etc. fastened to walls shall be secured to wall framing members and nails set.  Care shall be taken to avoid splitting ends of trim boards.

3.2 	INTERIOR TRIM:  Install trim with finishing nails and glue where required to assure permanent, tight joints, according to Drawing details.

3.3 	STAIRS:  Skirtboards and handrails installed as shown on Drawings (handrails supported every 4'-0" o.c. minimum) secured into solid blocking (1-1/4" minimum screw depth for handrails).  Risers and treads to be glued and screwed together.

END OF SECTION