SECTION 07200

INSULATION AND VAPOR BARRIERS

1.	GENERAL:

1.1  	GENERAL PROVISIONS:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2  	DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet the requirements of the Specifications.  The work covered by this section of Specifications consists of the following:

1.  	Installation of rigid insulation, fiberglass batts and sound insulation in exterior walls, interior walls, ceilings and floors where shown on Drawings.

2. 	Vapor barriers to be installed as shown.

2.	PRODUCTS:

  - BATT INSULATION TYPE:  Fiberglass by Owens-Corning- R-19 in walls, Fiberglass, or approved equal.

2.2	RIGID INSULATION: 2” Blue Board, see Drawings for locations.

2.3	ROOF INSULATION:  See Section 07218

2.4	MOISTURE PROTECTION:  6 mil. clear polyethylene film in exterior walls.

2.5	SHEATHING PAPER AT ALL EXTERIOR WALLS: 15# asphalt felt. NOTE: No equals will be allowed.

  - WATER RESISTANT BARRIER UNDER LEAD SIDING: Tyvek by Dupont or equal.

3.  	EXECUTION:

3.1 	FIBERGLASS INSULATION

- Fiberglass batts in exterior walls shall be fluffed to full nominal depth and shall be stuffed in around window unit frame to fill gap between frame and rough opening studs.  Secure wall batts at top of cavity with wire or nails into side of studs.  Provide foam insulation in ¾” or less gaps between frame and R.O.  Insure that insulation is tight and full

3.2  	MOISTURE PROTECTION:  A continuous 6-mil. vapor barrier shall be installed on all exterior walls stapled to hold fiberglass batts in place, as part of the work of this section.  Vapor barrier on walls shall be 8' wide to minimize horizontal joints.  All joints in vapor barrier shall be taped, and all vapor barrier free edges shall be taped to substrate.  Minimum lap at joints to be 8" including lap at wall.

END OF SECTION