SECTION 08200

INTERIOR APARTMENT DOORS AND FINISH HARDWARE

A. 	GENERAL:

SCOPE:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet the requirements of these Specifications.  The work covered by this section of Specifications consists of the following:

1. 	Furnishing and installing all door frames as called for on drawings or noted in Specifications.

2. 	Furnishing and installing all interior wood and exterior metal doors as specified.

3. 	Furnishing and installing hardware in accordance with Door Schedule, including locksets, 			closers, holders, knockers etc.

NOTE:  The Contractor shall submit drawings on every item specified in this section.  There shall be no substitutions without a specific written explanation from the subcontractor that the specific item is equal with the item specified by the Architect.  All substitutions shall be approved by the Architect and the Owner.

B. 	PRODUCTS:

All doors and frames shall be of the material, type and finish as called for on Drawings or in these Specifications.  All dimensions shall be as shown by Door Schedule on Drawings.  Door identified by manufacturer's name and type of brand name may be substituted for others of equal quality only with the approval of the Architect.  Doors delivered for installation shall be carefully stored to prevent damage or warping.

All Interior unit swing doors and sliding shall be 1-3/8” Atherton #550 moulded smooth panel doors by Door Craft Inc. and distributed by Brosco or equal.  Units shall be prehung and primed. Verify finish and coordinate with painting specification.

Apartment Entry Door: To be 1 ¾ solid oak veneer with metal frame.

Hardware:  See Hardware Schedule

C.  	EXECUTION:

Install doors after completion of all other work which would raise the moisture content of wood doors or damage door surfaces.  Fit, hang and trim as required by the opening so the doors will close and not bind.  Solid blocking at hinges and latch required.  Provide even clearance of 1/8" at sides and top, 1/4" over thresholds, and 3/4" over floors.  See also Section 06100 & 06200 Rough and Finish Carpentry.

Install doorstops for all swing doors.

At completion of work, door glass shall be cleaned, leaving no masking tape or any other visible marks on the surface; doors shall be free of any nicks, scratches or marks; all doors shall open and close freely; and all locksets shall operate with key, (if required) and hardware function properly.

D.  	HARDWARE:

SUBMITTALS:

Samples:  Submit representative samples of all items of finish hardware and finishes for approval of the Architect, upon the Architect's request.  Samples shall show the design, material and finish proposed for use.

Provide samples of the apartment numerals.

Hardware Schedule and Keying Chart  Prepare and submit a complete Hardware Schedule for approval of the Architect before any hardware is ordered.  After approval of the Hardware Schedule, a key and master key chart shall be submitted to the Architect for the Owner's approval.  No changes shall be made to the approved schedule or chart without the written consent of the Architect.

Templates:  Provide hardware templates to the various trades and fabricators requiring them, immediately after receipt of approved Hardware Schedule, to assure accurate setting and finish hardware.

PACKING AND MARKING:

Hardware:  Shall have the required screws, bolts, and fastenings necessary for installation in the same package with the hardware, including keys and instructions.  Each package shall be legibly marked and adequately labeled, indicating the part of the work for which it is intended.  Each marking shall correspond to the number shown on the approved Hardware schedule.  Within each packed lockset, keys shall be tagged and plainly marked on the face of the envelope with the key change number, door designation and all other identifying information as required.

PROTECTION:

Hardware:  All wrapping furnished by the manufacturer on knobs, handles and pulls shall be replaced upon the hardware as soon as it is installed and shall remain thereon until the completion of construction.

KEY SYSTEM:

All locks shall be made to a master key system.  Two change keys shall be furnished for each lock and three master keys.  Master keys shall be given directly to the Owner.

E. 	PRODUCTS:  See Hardware Schedule

END OF SECTION