SECTION 08210 - WOOD DOORS

PART 1 - GENERAL

1.01		GENERAL PROVISIONS:

A.		The CONDITIONS OF THE CONTRACT and all Sections of Division 1 are hereby made a part of  this section.

1.02		DESCRIPTION OF WORK:

A.		Work Included:  Provide labor, materials, and equipment necessary to complete the work of this section.  Extent of wood doors required is indicated on drawings and in schedules.

1.	Furnish and Install:

a.	Flush wood doors for steel frames

b.	Related work specified elsewhere:

1.	SECTION 08100:	STEEL DOORS AND FRAMES

2.	SECTION 08700:	FINISH HARDWARE

3.	SECTION 09900:	PAINTING

1.03		QUALITY ASSURANCE; SUBMITTALS:

A.		General:  Comply with requirements of  SECTION 01300 - SUBMITTALS, MEETINGS & RECORD DOCUMENTS; SECTION 01400 - QUALITY CONTROL SERVICES.

B.		Manufacturer:  Provide wood doors complying with these specifications from one of the following:

1.	Weyerhaeuser

2.	Brosco

3.	Mohawk

C. 		Supplier:  A recognized wood door supplier, with in-house fabrication and warehousing facilities, who has been furnishing doors and frames in the project's vicinity for a period of not less than five years.

D.		Product Data:  Submit four copies of manufacturers technical product data for each item. Include whatever information may be necessary to show compliance with requirements, and include instructions for installation and maintenance.

E.		Door Schedule:  Submit final door schedule in manufacturer’s standard format.  Coordinate doors,  frames and related work to ensure proper size, thickness, hand, function, and fasteners.

1.	NOTE:  Contractor shall make all submittals for finish hardware, 	doors, frames and related items simultaneously, only after proper review and coordination by own staff beforehand.

2.	Shop Drawings:  Submit separate detail drawings, referenced to door 	schedule, showing size, hand, construction, fasteners, elevation and all other details pertinent to the fabrication of doors and frames for this 	project.

1.04		APPROVAL OF SUBSTITUTIONS:

A.		Manufacturers and model numbers specified herein are to establish a standard of quality.  If products other than those specifically identified herein are to be considered for this Project, they must be submitted for approval of the Architect not less than ten (10) calendar days prior to receipt of General Bids.

B.		Requests for approval of substitutions shall be in writing, accompanied by catalog cuts, technical information and physical samples.

C.		Approval of substitutions shall only be valid when issued by Architect to all bidders in the form of Addendum.

1.05		REFERENCES:

A.		Applicable AWI standards.

B.		NFPA 80, NFPA 101.

C.		Other applicable building and life safety codes.

D.		Door and Hardware Institute:  "Recommended Locations for Builder's Hardware.

E.		ANSI A117.1:  American National Standard Providing Accessibility and Usability for Physically Handicapped People.

F.		Other applicable industry standards.

1.06		PRODUCT PACKAGING AND HANDLING:

A.		Tag each item or package separately, with identification related to final door schedule.

B.		All doors shall be packaged in full cartons and securely banded.

C.		Doors and frames shall be received by the contractor at the jobsite and handled in a manner so as not to be damaged. They shall be stored upright in a protected area on wood runners or skids and shall be covered with vented tarpaulins or plastic.

1.07		WARRANTY:	Doors and frames specified for this Project shall be guaranteed against defects in material and workmanship for a period of one (1) year from date of Substantial Completion of Project.

PART 2 - PRODUCTS

2.01		FLUSH WOOD DOORS:

A.		Doors shall be 1-3/4” thick with particle board cores bonded to stiles and rails.

B.		Provide standard 3-ply face veneer of plain slice oak.

C.		Where glass lites are required, provide manufacturer’s standard wood molding to match face veneer on non-fire rated doors, and standard steel molding on fire rated doors.

D.		Factory prepare doors to receive concealed or mortise hardware as specified in 08700 FINISH HARDWARE.

PART 3 - EXECUTION

3.01		INSTALLATION

A.		Doors and frames shall be assembled, installed, and erected plumb and in true alignment and in conformance with manufacturer’s recommendations and final approved shop drawings. Preparation for surface applied hardware shall be performed on the jobsite. Frames shall be rigid and securely anchored in place. Doors shall be installed in a manner to achieve functional operation and appearance.

B.		Install hardware in compliance with 08700 FINISH HARDWARE.

END OF SECTION