SECTION 08600

WINDOWS & SLIDING DOORS

1. 	GENERAL;

1.1	REFERENCES:  Drawings and general provisions of Contract, including General Conditions and Division 1 specifications, apply to work in this section.

1.2	DESCRIPTION OF WORK:  The extent of work shall be as shown on Drawings and called for in these Specifications.  Performance shall meet the requirements of these Specification.  The work covered by this section of specifications consists of the following:

A.  	Furnishing and installing all windows as shown on Drawings, complete with all 				hardware, operators and other accessories, including corner flashing pieces.

B.  	Furnishing screens.

C.  	Adjusting the windows and doors for smooth and faultless operation.

2. 	PRODUCTS:

2.1	AWNING, DOUBLE HUNG FIXED GLASS WINDOWS & SLIDING DOORS shall be “Pella Proline” or equal wood/aluminum with insulated glazing; window color to be “Standard Color Brown Pro 51”. Every operable window and doors to have screens.  Screens to be packaged independently of windows.  Insulating glass contains ¾” contoured aluminum grills, installed between the two panes of glass.  See Drawings for types. Interior to be factory primed.

2.2  	ALL DIMENSIONS shall be as shown on Drawings or from manufacturer's information. See details on Drawings for finish installation details.

2.3	Minimum  Fenestrati U Value of 0.35.

3. 	EXECUTION:

3.1 	WINDOWS AND DOORS shall be installed by workmen experienced in this kind of work.  Set frames plumb, level and square, within clearance limits of the respective openings.  Fasten frames securely to the wall framing.  Frames and other installation materials shall be handled carefully at all times and shall be protected from all possible sources of damage such as dampness, dirt, mortar, etc.  Units shall be stacked standing on edge on wood strips to prevent contact with ground.  Installation of windows shall strictly follow the manufacturer's recommendations.

3.2 	CAULK windows as required in other sections and on drawings.  Install corner flange closures and caulk as window is installed.

3.3   AFTER the windows and doors are installed, they shall be checked for smooth operation and adjusted as necessary.  Install screens.  Leave all installed windows and screens clean, tight and weatherproof.

END OF SECTION